## Slide 1: Upper Layer Data on Management frames
Date: 2011-07-18
Authors:
Name | Affiliations | Address | Phone | email
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com

## Slide 2: Abstract
To reduce total time for connection setup through all layers, processing for each layer should be running in parallel and data for each layer should be conveyed in the same packet if possible.
This presentation introduces technical proposal that 802.11ai provides container framework for data of upper layers.

## Slide 3: Grammatical: Upper or Higher?
In 802.11-2007, both ‘upper layer’ and ‘higher layer’ are used.
Do they have the same meanings?

## Slide 4: Desirable nature of “container”
Compatibility with existing 802.11 (Required)
Convey multiple upper layer protocols simultaneously
Big enough to accommodate upper layer data
Take opportunities effectively for sending and receiving data and easy for upper layer to use
Declare and check security conditions of each container
Keep principle of layered network architecture
  Do not care of inside of upper layer data
  Least limitation on behaviours of upper layers
  Possibilities for other protocols than IPv4/v6

## Slide 5: Compatibility
Convey on :
  Beacon, Association Request/Response and Action.
  Any other type of frames?
Use newly-defined IE
  Old AP and stations ignore it. (7.2.3)
Element ID of new IE is larger than one of vendor specific IE.
  >221
  in order to keep the order of IEs
  upper layer data should be placed at last of packets.

## Slide 6: Compatibility (cont.)
It’s ok that there are multiple number of the same IEs in a frame.
  Vendor specific IE do so. (7.3.2.26)
In the following story, let’s assume that new IE ‘Upper Layer IE’ is defined, whose element ID is 222.
 | Element ID | length | data
Octets: | 1 | 1 | 1 - 255

## Slide 7: Multiple protocols
Each of data frame has a protocol type.
  IPv4/v6 uses SNAP header (RFC1042) aa-aa-03-00-00-00
Each of ‘data block’ should be had a protocol type in the same manner.
  data block = IE? go to the next slide.
 | Element ID | length | SNAP header | protocol | data
Octets: | 1 | 1 | 6 | 2 | 1 - 247

## Slide 8: Size of data block and IE
IE has 1-byte length field.
  Maximum size of IE is 1(type) + 1(length) + 255(data)
  This is too small for some kinds of upper layer protocols.
‘Data block’ for an upper layer protocol should be fragmented to several IEs when needed.
New IE has to have the ‘More IE Fragment’ bit.
Order of New IEs must not be changed during transmission.
  otherwise, each of New IE have sequence number?
802.11 has fragmentation mechanism for big frames
  Fragment Number field (7.1.3.4.2)

## Slide 9: Size of data block and IE (cont.)
 | Element ID | length | flags | SNAP header | protocol | data
Octets: | 1 | 1 | 1 | 6 | 2 | 1 - 246
 | Element ID | length | flags | data (cont.) |  | 
Octets: | 1 | 1 | 1 |  | 1 - 254 | 
More IE fragment bit = 1
More IE fragment bit = 0

## Slide 10: More opportunities for data exchange
Action frames (7.2.3.12) with new IEs should be permitted to be exchanged between Association Request and Response, moreover, after Association Response.
For a convenience for upper layer programmers, MLME interface of this framework should be able to used after association completed (that is, after Association Response)
  upper layer setup may not be finished until Association Response.

## Slide 11: More opportunities for exchange (cont.)
Association Request
Association Response
STA
AP
Action
Action

## Slide 12: Declare and check security status
802.11ai may provide multiple authentication and key management protocols.
Security status of a packet varies according to protocols and their state.
  No security
  Signed (data is not altered during transmission)
  Encrypted (data is not revealed during transmission)
  Trusted (creator of data is trusted by sender)
802.11ai should tell upper layers such status.
upper layers should tell 802.11ai requirement of security nature of data to be sent, and 802.11ai checks it.

## Slide 13: Declare and check security status (cont.)
 | Element ID | length | flags | SNAP header | protocol | data
Octets: | 1 | 1 | 1 | 6 | 2 | 1 - 246
 | Element ID | length | flags | data (cont.) |  | 
Octets: | 1 | 1 | 1 |  | 1 - 254 | 
More IE fragment bit = 1
More IE fragment bit = 0
‘Request to be signed’ bit = 1

## Slide 14: Declare and check security status (cont.)
On sending:
Compare flags supplied by upper layer with current security status.
  If matched, a packet with IEs is sent.
  if not matched, the upper layer IE is removed or queued before sending packet and may inform upper layer program of this result.
On receiving:
Compare flags in a packet with current security status.
  if matched, upper layer data is re-built and passed to upper layer.
  if not matched, packet is discarded.

## Slide 15: Two types of MLME interfaces
MLME interface following .11 protocol
  This is the existing interface.
  Extended to have capability to pass ‘Upper Layer IE’
new MLME interface for upper layer protocols
  This interface resembles MAC data services (6.2.1)
  Extended to have additional capabilities

## Slide 16: Actual Upper Layers
IPv4
  DHCP should be modified.
    Original 4-way DHCP can run using Action frames.
    In order to reduce time, ‘timeout’ operation should be eliminated.
    For more efficiency, 2-way version is preferable.
IPv6
  RS and RA can be used as is.
    RFC6106 enables RA to carry DNS server information.
Another protocol? More higher layers??

## Slide 17: Discussion