## Slide 1: Supporting Large Number of STAs in 802.11ah
Date: 2011-07-20
Authors:

## Slide 2: Summary
A 802.11ah network must support up to 6000 STAs
  Smart Grid, long range data collection and monitoring system
11/0725r1 raised concerns about whether CSMA/CA channel access is able to support up to 6000 STAs
  Authentication and Association is based on contention access process
    The time it takes for STAs to join a BSS (association time) is an important performance metric
  The efficiency of CSMA/CA mechanism is unclear with 6000 STAs
Reporting simulation results for the following cases
  Transmission delay for large number of STAs based on CSMA/CA channel access
  Transmission delay for multiple rounds of frame exchange, for example Authentication and Association
Simulation tool – Estinet Network Simulator & Emulator
  The commercial version of the NCTUns simulator
    Additional information about the simulation methodology is available upon request

## Slide 3: Simulation of Max. Tx Delay
Simulation Goal: See how the maximum Tx delay varies as the number of STAs increases in a BSS.
Scenario
  The BSS system consists of n STAs and one AP
  Each STA sends one fixed sized, m byte, frame to the AP using a fixed rate of r kbps, followed by the AP responding with an ACK frame
    An STA stays silent after completing one transaction
  All STAs attempt to send data frame starting at the beginning of the simulation using DCF CSMA/CA

## Slide 4: Simulation Parameters
Channel access mechanism is DCF
  Maximum backoff window is 1024
  The MAC layer re-try is limited to seven times
  The application layer will keep re-trying until an STA successfully completes the transmission of one frame.
Other Parameters
    n: ranges from 50 to 2000
    m: 50 bytes
    r: 100 kbps (the minimum rate)
    DIFS: 34 us
    SIFS: 16 us
    timeslot: 9 us
    preamble: 16 us
    signal (PLCP header): 4 us
    service bits: 16 bits
    tail bits: 6 bits
    Ack frame size: 14 bytes

## Slide 5: Result – Tx Delay
# of STAs | Tx Delay (ms)
50 | 631.2677
250 | 3179.074
500 | 6495.147
750 | 10589.46
1000 | 19061.73
1250 | 30166.42
1500 | 42746.59
1750 | 58505.46
2000 | 71764.29
Chart: 
| 50 | 250 | 500 | 750 | 1000 | 1250 | 1500 | 1750 | 2000
 | 631.2677 | 3179.0742 | 6495.1471 | 10589.4612 | 19061.727 | 30166.4167 | 42746.5905 | 58505.4584 | 71764.2882
The time to complete n transactions increases at a rate of TBD.
The best case second order polynomial curve puts the max Tx delay at around 700 seconds for 6000 STAs

## Slide 6: Result – Number of MAC Layer re-tries
# of STAs | Total # of MAC Layer re-try count for all STAs
50 | 118
250 | 1093
500 | 2674
750 | 4749
1000 | 9678
1250 | 17525
1500 | 28345
1750 | 43546
2000 | 60149
Chart: 
| 50 | 250 | 500 | 750 | 1000 | 1250 | 1500 | 1750 | 2000
 | 118 | 1093 | 2674 | 4749 | 9678 | 17525 | 28345 | 43546 | 60149
The MAC layer re-try count increases at a rate of TBD
The slope of the curve grows continuously with number of STAs.
The high number of re-try count will be the source of issues such as higher power consumption

## Slide 7: Result – Tx Delay for Three Rounds of Frame Exchange
# of STAs | Tx Delay (ms)
50 | 2694.118
250 | 13624.01
500 | 27754.21
750 | 40795.22
1000 | 58313.73
1250 | 
1500 | 
1750 | 
2000 | 
The time to complete n rounds of frame exchange for m STAs at a rate of TBD.
Chart: 
| 50 | 250 | 500 | 750 | 1000
100Kbps | 2694.1183 | 13624.0127 | 27754.2054 | 40795.2196 | 58313.7253

## Slide 8: Conclusions
According to the simulation result,
  The DCF mechanism is capable of supporting up to 6000 STAs
    In the worst case where all STAs tx at the same time (e.g., due to a common event in a smart grid application), a STA can still send a report once every reporting cycle as long as the cycle time is greater than TBD.
  The worst case “association time” for 6000 STAs is yet to be determined
    This delay is acceptable if traffic load is low
  To reduce the number of MAC layer re-tries (reducing the probability of collision) and power consumption, the STAs can be grouped
    Example: Each group has 50 STAs and each group accesses the channel during staggered intervals.
Future Work
  Completing simulation Tx Delay of 6000 STAs to validate polynomial approximation.