## Slide 1: Singapore Sub 1GHz Frequency Bands for IEEE 802.11ah
Date: 2011-8-11
Authors:

## Slide 2: Abstract
This presentation is to provide information on Singapore Frequency Bands potential for 802.11ah devices.

## Slide 3: Short Range Devices
Intended for communications in confined areas of buildings as well as for localized on-site operations
Applications include Alarms, Identification systems, radio-detection, vehicle radar systems, wireless local area networks, remote controls, telecommand, telemetry and on-site paging systems
May be fixed, mobile or portable stations
May employ different types of modulation
May have speech application

## Slide 4: S1G Frequency Band Suitable for 11ah
Frequency Band (MHz) | RF Output power (e.r.p,) 1 | Typical Application Types | TX Spurious Emissions | Applicable Radio Standards
216-217 | <=100 mW | Medical and Biological; Telemetry | ≥ 32 dB below carrier at 3 m or EN 300 220-1 | FCC Part 15 or EN 300 220-1
312-316 | <=100 mW | Radio Detection, Alarm system |  | 
433.05 – 434.79 | <=10 mW | Radio Telemetry, Telecommand |  | 
866 – 869 920 – 925 | 2 ≤ 500 mW | Radio Telemetry, Telecommand, RFID | ≥ 32 dB below carrier at 3 m; EN 300 220-1 or EN 302 208 | FCC Part 15 ; EN 300 220-1 or EN 302 208
1 Effective Radiated Power (e.r.p.) refers to radiation of a half wave tuned dipole, which is used for frequencies below 1 GHz
2 RFID devices may transmit up to 2 W in 920 – 925 MHz upon approval

## Slide 5: Conclusions
There are about 15 MHz identified in Singapore that could potentially be used for IEEE 802.11ah devices

## Slide 6: References
IDA TS SRD Technical Specification for Short Range Devices, May 2011