## Slide 1: Use Cases For FILS
Date: YYYY-MM-DD
Authors:

## Slide 2: What is 802.11ai?
802.11ai — Will define the way artificially intelligent robots overtake the world using Wi-Fi. Actually, that’s a lie. No public info is yet available for 802.11ai.*
*https://www.cwnp.com/cwnp_wifi_blog/802-11-alphabet-soup

## Slide 3: Use Case Process
Prototypical use cases
  Establishes a small set reference use cases
  Provides summary all use cases accepted by TGai
  Sets criteria for 802.11ai submissions
Full set of use case in
  11-11-0238-19-00ai-Use-Case-Reference-List-for-TGai.docx

## Slide 4: Definitions (1 of 2)
FILS = Fast Initial Link Setup
For FILS, the device set is
  a mobile STA
  a network access point
The traits which differentiate the use cases are
  Link-Attempt Rate
  Media Load
  Coverage Interval
  Link Setup Time

## Slide 5: Definitions (2 of 2)
Link-Attempt Rate
  The number of STAs attempting to establish a link for the first time to an AP within an ESS as measured over a one second time interval.
Media Load
  “Busyness” of the wireless medium of the ESS. It is measured as the percentage of time the medium is in use.
Coverage Interval
  Time the STA is within the range of the AP
Link Setup Time
  Timing starts when the STA elects to perform Link Setup and ends when it gains the ability to send IP traffic with a valid IP address
Notes: NOTE: “link”, “association”, and “authentication” are as defined per 802.11

## Slide 6: Tokyo Central Station Use Case
A very large number of relatively slow-moving pedestrians attempt to connect at virtually the same time at Tokyo Central Train Station
  Link-Attempt Rate: 100s/second
  Media Load: 50%
  Coverage Interval <10 sec
  Link Setup Time 100 ms
Driver for the adoption of FILS.

## Slide 7: Tokyo Central Station
[picture of wall-to-wall people in a train station]

## Slide 8: Drive-by Use Case
Large number of vehicles uploading/downloading a large amount of information, only in range for a short time.
  Link-Attempt Rate <10
  Media Load 10 to 50%
  Coverage Interval <1 second
  Link Setup Time <100 ms
Without FILS the use case is not addressed well enough to be a viable use case for 802.11

## Slide 9: Drive-by Information
[picture of in-vehicle real-time information from local source being driven past]

## Slide 10: Emergency coordination Use Case
Establish a temporary IP network on-site at an emergency site
Includes: voice, text, graphics, video
  Link-Attempt Rate 10
  Media Load 10 - 50%
  Coverage Interval >10 sec
  Link Setup Time >2 seconds
Unlikely to be the reason for migration to FILS, but once it resides in the STA/AP, it will promote usage.

## Slide 11: Emergency Coordination
[picture of major fire or accident with audio/graphic/video communications devices]

## Slide 12: collage of other use cases
Pedestrian
  Electronic Payment
  Traveller Information
  Internet Access
  Mobile Accessible Pedestrian Signal System
Vehicle
  Electronic Payment
  Traveller Information
  Internet Access
  Emergency Services
  Inspections
  Resource Management
Transit
  Station arrival
  Passenger In-transit access
  Station Lobby
  Connection Protection
  Dynamic Transit Operations
Self-growing networking
  Handover between 3G and WLAN
  Energy-aware end-to-end delay optimization
  Purpose-driven network reconfiguration during an emergency situation
  Cognitive Coexistence and self-growing for white space operation

## Slide 13: References
11-10-1152-01-0fia-fast-initial-link-set-up-par.doc
11-11-0281-00-00ai-proposed-dynamic-mobility-use-cases-for-tgai.docx
11-11-0148-07-00ai-use-cases-for-tgai.docx
11-11-0122-00-00ai-3g-wlan-handover.pptx
11-11-0408-02-00ai-Use_Case_Characteristics_Discussion.pptx
11-11-0023-02-00ai-use-case-senario-for-tgai.pptx
11-11-0441-00-00ai-self-growing-use-cases-requiring-fast-initial-link-setup.docx
11-11-0746-00-00ai-discussion-on-how-many-aps-to-cover.ppt
11-11-0750-00-00ai-use-case-document-definitions.pptx
11-11-0619-00-00ai-use-case-network-mobility.pptx
11-11-0797-00-00ai-use-case-mobile-hotspot.pptx