## Slide 1: 802.11ah Channel Access Improvement
Date: 2012-05-14
Authors:

## Slide 2
Authors:

## Slide 3: Introduction
In 11/1230r0, we introduced a high level channel access concept that gives a sensor type of STAs the highest channel access priority.
This presentation is a follow up presentation with simulation results that supports the proposed channel access concept.

## Slide 4: 802.11ah Use Case Categories [1]
802.11ah defines three use case categories
  Use Case 1 : Sensors and meters
  Use Case 2 : Backhaul sensor and meter data
  Use Case 3 : Extended range Wi-Fi
Use Case 1 and 3 have different traffic characteristics
  Use Case 1: small packet size and low duty-cycle
  Use Case 3: large packet size and high duty-cycle
Coexistence issue between Use Case 1 and Use Case 3

## Slide 5: Coexistence Issue between Use Case 1 and Use Case 3
A low duty-cycle STA (Use Case 1) suffers from high duty-cycle STA (Use Case 3)
  When the channel utilization is high due to hotspot or cellular offloading applications, sensors may experience a long channel access delay  power consumption increases
Data-Ack
Sensor STA wakes up and tries to send a packet
DIFS
CW back-off =3
1) STA-2 waits until the channel is idle
(Idle Channel Wait Time)
DIFS
Data-Ack
2) STA-2 loses contention and waits again until the channel is idle
CW back-off =4
STA-1
(hotspot: high duty-cycle traffic)
STA-2
(sensor: low duty-cycle traffic)

## Slide 6: Proposed Channel Access Enhancement
Give the highest priority to low duty-cycle (sensor) traffic for channel access
  Sensor traffic has a very low duty-cycle compared to other hotspot or cellular offloading applications  does not hurt high-duty cycle applications
  Reducing the channel access delay is critical to sensors for a long battery life
  Redefine/remap EDCA access categories (AC) to give sensor traffic the highest priority
Data-Ack
Data-Ack
Data-Ack
1) Sensor STA wakes up and tries to send a packet
DIFS
CW back-off =3
2) STA-2 waits until the channel is idle
(Idle Channel Wait Time)
DIFS
3) STA-2 wins the contention
CW back-off =4
STA-1
(hotspot: high duty-cycle traffic)
STA-2
(sensor: low duty-cycle traffic)
AIFS[non-sensor]
AIFS[sensor]
DIFS
4) Sensor STA goes back to sleep until next packet transmission time
5) Hotspot STA continues transmissions

## Slide 7: Simulation Setup
Sensor + Extended Wi-Fi Scenario with more traffic flows (STAs)
  Extended range Wi-Fi traffic flows: 1~3
    Full-buffered traffic
    1500 bytes MPDU back-to-back
    Packet Tx time: ~20 msec @ 600 Kbps
    Use EDCA[BE] parameters with CWmin=15
  Sensor traffic flows: 5
    Low duty-cycle traffic
    256 bytes MPDU transmission at t ~ Uniform(10 sec), average Tx period = 5 sec
      Note: 5 sensor STAs with the average Tx period of 5 sec is equivalent to 30 sensor STAs with the average Tx period of 30 sec (the simulation results in the backup slide).
    Packet Tx time: ~3.7 msec @ 600 Kbps
    Use EDCA[Sensor]=EDCA[VO] parameters with CWmin=15
PHY/MAC parameters
  PHY rate: 600 Kbps
  Preamble: 240 usec (6 symbols x 40 usec)
  SIFS: 64 usec
  Slot-time: 45 usec (5usec+4usec x10)
  EDCA[Sensor]: AIFSN[VO]=2, CWmin[VO]=3, CWmax[VO]=7
  EDCA[BE] for Extended range Wi-Fi: AIFSN[BE]=3~6, CWmin[BE]=15, CWmax[BE]=1023

## Slide 8: Simulation Results
Tx delay [Sensor] and aggregated MAC throughput [BE]
  Case 4: 5 Sensor STAs, 1 BE STA
  Case 5: 5 Sensor STAs, 2 BE STAs
  Case 6: 5 Sensor STAs, 3 BE STAs
AIFSN[BE]=5 or 6 for the 2 or 3 BE STAs case
  20% ~ 26% Tx delay reduction gain for the low duty-cycle traffic (sensor) compared to AIFSN[BE]=3
  Less than 0.8 % MAC throughput drop for the best effort (BE) high duty-cycle traffic (Extended Wi-Fi)
BE MAC throughput
Sensor Tx delay
BE MAC throughput drop
Sensor Tx delay reduction

## Slide 9: Summary
802.11ah Use Case 1 (sensor) and Use Case 3 (extended range Wi-Fi) have different traffic characteristics
Need to address the coexistence issue between the sensor use case and the extended range Wi-Fi use case
We propose to redefine/remap EDCA access categories (AC) to give sensor traffic the highest priority
  AIFSN[BE]=5 or 6 for the 2 or 3 BE STAs case
    20% ~ 26% Tx delay reduction gain for the low duty-cycle traffic (sensor) compared to AIFSN[BE]=3
    Less than 0.8 % MAC throughput drop for the best effort (BE) high duty-cycle traffic (Extended Wi-Fi)

## Slide 10: Straw Poll
Do you support that the sensor type of STAs to have the highest channel access priority?

## Slide 11: References
[1] Rolf de Vegt, “Potential Compromise for 802.11ah Use Case Document,” 11-11/457r0.
[2] Minyoung Park, et. al., “802.11ah Channel Access Improvement,” 11-11/1230r0