## Slide 1: The better spectrum utilization for the future WLAN standardization
Date: 2011-11-08
Authors:

## Slide 2: Abstract
There are emerging use cases of the WLAN systems.
High quality video transmissions and cellular offload in a residential environment are important applications which requires more and more data rates and throughputs.
For the continuous success of WLAN, we need to find out the way to extend system capacity of WLANs.

## Slide 3: Background#1: Changes in the use case of WLAN
Recent important use cases of WLANs
  Wireless home networking:
    Many appliances such as digital TVs, VCRs and game machines have a WLAN interface.
    Applications using direct link need more spectrum resources
    There may be another opportunity for WLANs such as home automation and home security.
  Cellular data offload:
    Smartphones and slate PCs also have a WLAN interface.
    WLAN is expected to be an access method complementary to the cellular systems, especially in the urban areas.

## Slide 4: Background#2: Wireless LAN Evolution
Year
1G
10G
100M
Wireless LANs
10M
1M
100k
100G
Data Rate [bit/s]
Cellular
LTE-Advanced
2005
2010
2015
2000
1995
GSM
PDC
WCDMA
HSDPA
LTE
.11b
802.11
.11a
.11g
.11n
.11ad
.11ac
?
<Message of this slide>
Future WLANs need to have more speed, more bandwidth to support high speed applications and/or to be alternative to the cellular systems.

## Slide 5: The channelization in 5GHz bands
WLANs have traditionally increased data rate by extending channel bandwidth.
  802.11n specified the optional 40MHz channel operation in addition to the conventional 20MHz channel operation
  The 802.11ac is introducing 80MHz and optional 160MHz channel operations.
However, it does not seem to be a reasonable to introduce even wider channels such as 240 MHz and 320 MHz due to the limitation of total spectrum.
Although there are new frequency bands to be available for WLANs, it is important to enhance the spectrum utilization of existing frequency bands in order to offer the same user experiences.
5470
5650
5670
5725 [MHz]
5150
5350
5250
36
40
44
48
52
56
60
64
100
104
108
112
116
120
124
128
132
136
140
5560
20MHz channels
40MHz channels
80MHz channels
160MHz channels

## Slide 6: WLAN deployment
An example of deployment scenario - home networks in an apartment
  There will be 802.11a, 802.11n and 802.11ac BSS and devices coexisting on the same channel in the same location.
  Even in a BSS, there may be some kinds of client devices
    E.g., There may be a hand set or a tablet PC with 802.11a interface associated to a 802.11ac AP.
  Note: This is not a unique situation of the home networks Similar situation may be seen in other places such as hotspots.

## Slide 7: For the better use of space, time and frequency resources
For simplicity, let us assume that an 802.11a, an 802.11n and an 802.11ac BSSs are operating on the same channel and in the same location.
Those client devices have different capabilities, such as channel bandwidth and the number of supported antennas.
There may be unused frequency, the secondary channels, and/or spatial resources.
Ch #
time
…
56
52
48
44
40
36
.11a
.11ac
.11n
.11ac
.11a
.11n
Space
.11ac
.11n
.11ac
.11ac
.11
ac
Frequency
There will be some ways to utilize those unused resources
.11ac
.11
ac
11a
11n
11ac
11a
11n
11ac
APs
STAs
20MHz, 1SS
40MHz, 2SS
80MHz, 4SS

## Slide 8: Ideas to improve frequency and spatial resources
Frequency domain extension
  Multi-channel operation
    20MHz or 40MHz based flexible channel assignment including non-contiguous operations
    OFDMA like approach
  Flexible channel use across BSSs
    Enhance frequency utilization by exchanging information between APs
Spatial domain extension
  Uplink MU-MIMO
    Extend 802.11ac DL MU-MIMO
  Spatial multiplexing across BSSs
    Extend beamforming function of MU-MIMO to enhance system capacity across BSSs exchanging information between APs

## Slide 9: An example of frequency and spatial domain extension across BSSs
Ch #
time
…
48
44
40
36
.11a
.11ac
.11n
Space
.11ac
.11n
.11ac
.11*
.11*
.11ac
.11n
.11n
.11*
.11*
.11*
.11*
.11*
.11*
.11*
.11ac
.11n
.11*
.11n
.11ac
.11a
Ch #
time
…
48
44
40
36
.11a
.11ac
.11n
.11*
.11*
AP collaboration
Frequency domain extension
Frequency + Spatial domain extension

## Slide 10: Conclusions
For the continuous prosperity of WLANs, we need to extend system capacity.
To enhance the system capacity, we need to utilize space and frequency resources more efficiently.
We would like to start discussion to find out the image of next generation WLANs and technologies for consideration.