## Slide 1: Traffic Model
Date: 2011-11-09
Authors:

## Slide 2: Introduction
Use cases 1a (Smart Grid), 1c (Environ. Mon) and 1e (Indoor Healthcare) only specify a minimum supported data rate of 100 kbps
In practice, traffic data rate typically varies over time in event driven system
In this contribution, we propose a traffic data rate for heavy/bursty traffics

## Slide 3: High traffic data rate for use cases 1a, 1c and 1e
Max possible throughput with 2Mhz channel bandwith, BPSK ½, 250 byte data
  26 data bits/OFDM Symbol (BPSK 1/2), 40µs symbol duration
  SIFS=160µs, PLCP=400µs, MAC-Header=28bytes(344µs), ACK=18bytes (172µs)
  Max possible throughput without channel contention overhead:
  = 650kbps * Data / {(PLCP + MAC-Header + Data) + SIFS + ACK}
  = 478kbps
For evaluation purposes, 802.11ah should consider a data rate of 500kbps for heavy/bursty traffic in use cases 1a, 1c and 1e

## Slide 4: Conclusion
For evaluation purposes, 802.11ah should consider a data rate of 500kbps for heavy/bursty traffic in use cases 1a, 1c and 1e