## Slide 1: Extension of AID and TIM to Support 6000 STAs in 802.11ah
Date: 2011-11-08
Authors:

## Slide 2: Abstract
This presentation discusses the issue of supporting the number of associations beyond 2007 for smart metering applications
  Focus on the addressing mechanisms for power-saving STAs

## Slide 3: Background
The “smart grid - meter to pole” use case requires an 802.11ah AP to support up to 6000 STAs [1]
Current 802.11 standard can only support up to 2007 associations [2]
  The Association ID (AID) ranges from 1 to 2007
  The partial virtual bitmap in Traffic Indication Map (TIM) has a maximum length of 2008 bits

## Slide 4: Association ID
Current 802.11
  AID ranges from 1 to 2007
  Bits 2008-16383 are reserved
Propose
  Use reserved bits 2008-6000 for AIDs 2008-6000
  Little impact on the current standard
To support AID values beyond 2007, we need to expand the range of TIM coverage from 2007 to 6000
Bits 0-13 | Bit 14 | Bit 15 | Usage
0-32767 |  | 0 | Duration value
0 | 0 | 1 | Fixed value under PCF
1-16383 | 0 | 1 | Reserved
0 | 1 | 1 | Reserved
1-2007 | 1 | 1 | AID in PS-Poll
2008-16383 | 1 | 1 | Reserved
Duration / ID field encoding

## Slide 5: Traffic Indication Map
Element ID (1) | Length (1) | DTIM Count (1) | DTIM Period (1) | Bitmap Control (1) | Partial Virtual Bitmap (1-251)
The partial virtual bitmap of TIM element has a maximum length of 2008 bits
  Support broadcast / multicast (AID 0)
  Support unicast (AID 1 to AID 2007)
  Address any STA and an arbitrary number of STAs within a Beacon
TIM element format:
Max value = 255 bytes
Max length = 251 bytes

## Slide 6: IE repetition for TIM
Repeating IE to support up to 6000 STAs.
  Two more TIM elements are added and used together with the current TIM
  Each TIM addresses up to 2000 STAs
  Same Element ID can be used
Element ID
(1)
Partial Virtual Bitmap
(1-251)
Length
(1)
DTIM Count
(1)
DTIM Period
(1)
Bitmap Control
(1)
Element ID
(1)
Partial Virtual Bitmap
(1-251)
Length
(1)
DTIM Count
(1)
DTIM Period
(1)
Bitmap Control
(1)
Element ID
(1)
Partial Virtual Bitmap
(1-251)
Length
(1)
DTIM Count
(1)
DTIM Period
(1)
Bitmap Control
(1)
AID 1-2000
AID 2001-4000
AID 4001-6000

## Slide 7: Partial Virtual Bitmap
3 x bitmap size to support 6000 AIDs with ~750 bytes
Overhead is insignificant for longer beacon cycle
Introduce compression for shorter beacon cycle
  Reduced bitmap transmission with bitmap control (bitmap offset)
    Used in current 802.11
  Simple address encoding for smaller or moderate number of STAs
    e.g. using 13 bits to represent an active STAs
  Other possible low complexity compression schemes with a better compression ratio

## Slide 8: Summary
Using the reserved AID values has little specification impact
Existing IE can be repeated to extend the TIM to support 6000 AIDs
  Reuse the existing virtual bitmap in TIM
  Use compression schemes to reduce the transmission overhead

## Slide 9: References
[1] IEEE 802.11-11-0457r0: Potential compromise for 802.11ah use case document.
[2] IEEE 802.11-2007: IEEE Standard for Information technology—Telecommunications and information exchange between systems—Local and metropolitan area networks—Specific requirements—Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications.
[3] IEEE 802.11-11-0779r0: Device collective to share resources.
[4] IEEE 802.11-11-0725r0: Supporting large number of STAs in 802.11ah.
[5] IEEE 802.11-11-0762r0: Station group management for 802.11ah.
[6] IEEE 802.11-11-0088r1: Association ID management for TGah.