## Slide 1: Early Ack Indication
Date: 2012-01-16
Authors:

## Slide 3: Ack protection in current 802.11
Due to hidden terminal problem, an unintended STA that can receive a data frame correctly from a transmitter may not be able to detect the immediate response sent from the data frame receiver
The duration field in the MAC header of a data frame is used to provide protection for the immediate response and/or subsequence transmissions
  If an unintended STA decodes the duration field in MAC header correctly, it sets NAV according to the duration field value
If a STA receives the SIG of a PPDU correctly, but fails to decode the remaining part of the PPDU, it shall defer medium access EIFS or EIFS-DIFS+AIFS[AC] after the PPDU
SIG
MH
Data
Ack
Duration
EIFS

## Slide 4: Issues
In order to save power, an unintended STA may choose to check SIG field and/or MAC header (RA field) only, and skip the remaining portion of the frame; however, the STA cannot verify the correctness of the duration field and Ack policy field in MAC header
In some cases, an unintended STA can decode SIG field correctly, but cannot decode Data field
For aforementioned cases, the STA has to apply EIFS rule; however, it might be unfair or insufficient to use EIFS because
  an MPDU/MMPDU may not have an Ack
  EIFS accounts for the worse case Ack duration, which can be significant longer than the actual Ack duration
  EIFS protection may not be sufficient to protect a BA (32 bytes), which is much longer than an Ack (14 bytes)

## Slide 5: Our proposal
SIG
MH
Data
Ack
Add two-bit Ack Indication in SIG field to indicate whether an immediate response is requested right after the PPDU, and also the type of the response (e.g. 00: Ack; 01: BA; 10: No Ack; 11: reserved)
If a STA decodes the SIG correctly, but 1) decides to skip the remaining fields after SIG for power saving, or 2) is not able to decode /verify the MAC header, it can determine whether to defer medium access for Ack protection based on the Ack Indication in SIG
Ack Indication

## Slide 6: Conclusions
Ack protection based on duration field and EIFS is problematic
Early Ack indication in SIG field prvoides a relaible way for a receiving STA to decide whether to defer medium access in order to protect immediate Ack
  SIG is typically more reliable than MAC header
  The Ack indication can be quickly verified by SIG CRC

## Slide 7: Straw poll
Do you support to include 2-bit Ack Indication (00: Ack; 01: BA; 10: No Ack; 11: reserved) in SIG?