## Slide 1: GAS procedure in TGai
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Date: 2012-05-04
Authors:

## Slide 2: Abstract
This document proposes optimized GAS procedure by eliminating unnecessary GAS query.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: Background
The contribution 11-12-0151-07 (proposed-specification-framework-for-tgai) described GAS configuration-change element may include in Beacon/Probe Response to indicate changes in a set of static GAS parameters.
Inclusion of Configuration Change Element in Beacon and Probe Response is optional. If it is not included, STA may ask the AP whether or not it has to perform GAS procedure before the association.
  We propose to define Configuration Change Element in Association Request as an optional parameter.

## Slide 5: Example of proposal (i.e., GAS procedure skip)
STA caches GAS/ANQP configuration change counter.
When the STA associates to the AP, STA transmits the association request message with GAS configuration change counter to the AP.
(Configuration Change Counter is matched)  AP sends the association response message with status code ‘SUCCESS’ to the STA and then, STA skips the GAS procedure.
(Configuration Change Counter is mismatched)  AP defers the association and sends the association response message with updated GAS information IE.

## Slide 6: Proposed IE
GAS configuration change counter is included in association request message:
GAS information can be included in association response message:

## Slide 7: Motion 1
Move to add the following text to the clause 6 of the specification framework document:
STA may include a GAS configuration-change counter in the Association Request to check changes in a set of static GAS parameters.
Moved :
Seconded:
Yes: No: Abstain:

## Slide 8: Motion 2
Move to add the following text to the clause 6 of the specification framework document:
AP may include a GAS information in the Association Response when the GAS configuration change counter mismatches between STA and AP.
Moved :
Seconded:
Yes: No: Abstain: