## Slide 1: Reducing Probe Responses for faster AP discovery
Authors:
May 2012
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | Kiseon.ryu@lge.com

## Slide 2: Abstract
The submission proposes a general framework to improve the AP discovery for fast initial link set up.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4: Motivation
A number of proposals suggests methods to reduce the number of probe responses
  Most of the proposals focus on filtering mechanisms based on the network identity that the AP of interest belongs to
  While conflicting methods require a careful examination by the TG, most of the methods can be integrated in a structure manner
  However, there are possibly more filtering items that need to be included, considering user’s preference
  Two other filtering mechanisms are introduced in this perspective

## Slide 5: Probe Response Filtering
Proposals until today
  Filtering criteria proposed until today can be categorized as following:
  Whist list: The list specifies the HESSIDs, Mesh IDs, SSIDs and BSSIDs that prefer the request.
  Black list: The list specifies the HESSIDs, Mesh IDs, SSIDs and BSSIDs that ignore the request.

## Slide 6: But, something is missing
A user applies his/her preference in AP selection, not only the identity of AP or Network
  Such as the cost of the network usage and the quality of the signal
Thus, we need another category to incorporate this user behavior

## Slide 7: Considering the user (or station) behavior
Considering the user (or station) behavior, an additional filtering item to filter out unnecessary Probe Responses is proposed:
  Another filtering item is proposed: Received signal quality based filtering – A STA can select APs, which provide a signal quality above the threshold that STA specifies, to respond to the Probe Request.
    Signal quality (e.g., RCPI, RSNI) threshold can be included in Probe Request, when the STA discovers desired AP.

## Slide 8: Conclusion
Additional filtering item can be used to filter out unnecessary Probe Responses.
  Signal quality threshold of STA

## Slide 9: Motion 1
Move to add the following text to the clause 6 of the specification framework document:
6.1.9 Probe Response filtering
The 802.11ai shall support the Probe Response filtering to reduce the overhead of Probe Response transmission.
Moved :
Seconded:
Yes: No: Abstain:

## Slide 10: Motion 2
Move to add the following text to the clause 6 of the specification framework document:
6.1.9 Probe Response filtering
According to the Signal quality threshold (i.e., RCPI, RSNI) indicated in received Probe Request, AP may not send the Probe Response to STA which sent the Probe Request.
Moved :
Seconded:
Yes: No: Abstain: