## Slide 1: 1MHz Waveform in Wider BW
Date: 2012-03-12
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Abstract
This presentation proposes how to place 1MHz waveform when transmitted within a wider BW BSS.

## Slide 5: Introduction
In wider BW BSS, a device may transmit a 1MHz waveform for range extension.
Tone Plans in different BW:
  As introduced in [1], 1MHz tone plan has 3 guard tones on the left and 2 guard tones on the right.
  2MHz tone plan has 4 guard tones on the left and 3 guard tones on the right.
  4/8/16MHz tone plans have 6 guard tones on the left and 5 guard tones on the right.
This presentation proposes a rule to restrict the 1MHz waveform position in a wider BW BSS, according to the above tone plans.

## Slide 6: In 2MHz BSS
If a device is operated in 2MHz, the Tx/Rx filters may cut off between tones {-29: 28}, while the IFFT/FFT is between {-32:31}, i.e. leave out 3 tones on each side.
1MHz in upper side of 2MHz will occupy tones {3:29}, therefore to meet the spectrum mask at Tx or ACI reject at Rx, tone #29 may be scaled down or zeroed out—leading to performance loss.
We then prefer to always place 1MHz waveform in a 2MHz BSS on the lower side.
1MHz
0

## Slide 7: In 4/8/16MHz BSS
Similarly, if a device is operated in 4/8/16MHz, the Tx/Rx filters may cut off assuming 5 tones are left out on each side.
Therefore 1MHz waveform should avoid being at BOTH edges of the full channel (otherwise 2 or 3 tones are zeroed out or scaled down, and cause performance drop).
  Propose that in 4/8/16 MHz BSS, when primary 2MHz is at lower most of the overall band, then 1MHz is only allowed at upper side of the 2MHz primary channel; and if primary 2MHz is at upper most of the overall band, 1MHz is only allowed at lower side of the 2MHz primary channel.
  When 2MHz primary channel is in the middle of the overall BW in a 8/16MHz BSS, then 1MHz waveform location is TBD.
    E.g. we may still just fix it to one side of the 2MHz primary channel.
  Example in 4MHz BSS:
0
0
1MHz
0
0
0
1MHz
Primary 2MHz
Primary 2MHz
0

## Slide 8: References
[1] 11-11-1484-06-00ah-11ah-PHY-transmission-flow

## Slide 9: Straw poll (Pre-Motion)
Do you agree to add the following 1MHz transmission rule in the spec framework as a new subsection in section 3.1?
  “In 2MHz BSS, 1MHz waveform is only allowed at the lower side.
  In 4/8/16MHz BSS, when primary 2MHz is at lower most of the overall band, then 1MHz is only allowed at upper side of the 2MHz primary channel; when primary 2MHz is at upper most of the overall band, 1MHz is only allowed at lower side of the 2MHz primary channel; when primary 2MHz is in the middle of the overall band, 1MHz waveform position is TBD.”
  Yes
  No
  Abstain