## Slide 1: On The BSS Max Idle Period
Date: 2012-03-13
Authors:

## Slide 2: Motivation
BSS Max Idle Period indicates duration during which AP maintains association with a STA active even though it does not receive frames
  A STA can sleep for Max Idle Period without being disassociated
    Allows improved energy saving
    Allows improved resource management of the AP
Max Idle Period is = 65 535 seconds (units of 1000 TUs = 1s)
  Value zero is reserved
  Max Idle Period can be 1092.25 minutes or 18.20 hours
BSS Max Idle period is currently common for all STAs

## Slide 3: Motivation
In 802.11ah use case Smart Grid/Meter to Pole different STAs can have very different requirements
  Traffic
  Sleeping
Can be heterogeneous use cases
  Mobile stations and static sensors can be associated under the same AP
    E.g., Users exiting a metro as well as static sensors placed for surveillance
If STA needs to remain associated beyond 18.20 hours it has to send keep alive message to the AP
  This interrupts its sleep in case it is in power save mode
  It requires unnecessary transmissions for re-association
If it remains associated too long, it wastes the AP memory

## Slide 4: Prior Proposal
In [1] it was proposed to enlarge the unit length of Max Idle Period from ‘1000TU’ (1s) to ‘10000TU’ (10s)
  Max Idle Period can be extended from 18.20 hours to 182.0 hours (about 7.5 days)
This can lead to STAs being associated to an AP for more time than what is required
7.5 days may not be sufficient, depending on the frequency with which a sensor must report data

## Slide 5: Our Proposal
Introduce BSS Max Idle Period per STA
  Depends on STA type (mobile station, sensor)
  Traffic requirements
Different terminal types may have different requirements
  18.20 hours is too long for mobile STA especially in crowded places, e.g., metro stations
  Insufficient for static sensors that may take measurements daily, weekly, biweekly, or monthly even in crowded places.
Allow a finer granularity capability through different scalings
  How many bits to allocate and for which units
  More general than [1] or existing approaches

## Slide 6: BSS Max Idle Period Configuration
STA in Association Request indicates its preferred BSS Max Idle Period
  Can be through indicating one or multiple preferred scaling types
In Association Response the AP may
  Accept the request
    In case of multiple scalings it can choose the best with respect to the BSS
  Reject the request
    If e.g., it exceeds implementation maximum value
    Choose a different value that is preferred with respect to its own performance
      Return a smaller value e.g, based on its memory capacity
If STA does not indicate a value, the AP responds the best choice according to BSS

## Slide 7: Scalings
Scaling can be linear or exponential
Different scalings can be prespecified in the standard
x bits to indicate the scaling and 14-x for actual values
  E.g., x =1 or 2 (15 or 14 bits for the actual values)
Example of exponential scaling with x = 2 bits
  2 bits to indicate the scaling e.g.,
    00 - existing scaling (by 1)
    01 - scaling by 10
    10 - scaling by 100
    11 - scaling by 1000
  14 bits for values
Alternatively if x =1 it could signal existing method and scaling by 10

## Slide 8: Example of Scaling
00 – Indicate up to 16383 sec or 273.05 min or 4.55 hrs
01 – Indicate up to 163830 sec or 2730.5 min or 45.5 hrs or 1.89 days
10 – Indicate up to 1638300 sec or 27305 min or 455 hrs or 18.9 days
11 – Indicate up to 16383000 sec or 273050 min or 4550 hrs or 189 days
1
1
1
1
1
0
0
1
1
1st Octet
2nd Octet
Scaling factor
1
1
1
1
1
1
1
Data

## Slide 9: References
[1] 11-12-0069-02-00ah-consideration-on-max-idle-period-extension-for-11ah-power-save

## Slide 10: Conclusions
Use case 1a of 802.11ah can be heterogeneous in nature
  Different stations may have very different needs to be associated
A BSS Max Idle Period that is
  Too long can waste the AP resources
  Too short can interrupt the power save mode of a station and lead to unnecessary transmissions
BSS Max Idle Period that is STA dependent and allows different scalings provides
  Finer granularity in the BSS Max Idle Period
  Better resource utilization
  Improved energy saving for the stations

## Slide 11: Straw Poll 1
Do you support having different BSS Max Idle Periods per STA?
  Y: N: A:

## Slide 12: Straw Poll 2
Do you support allowing different scalings for the BSS Max Idle Period?
  Y: N: A:

## Slide 13: Straw Poll 3
Do you support the exponential scaling for BSS Max Idle Period?
  Y: N: A: