## Slide 1: Proposed SFD Text for 802.11ai Passive Scanning Improvement
Date: 2012-05-09
Authors:

## Slide 2: Abstract
This document proposes text to be inserted in TGai Specification Framework Document (SFD) regarding 802.11ai passive scanning improvements.
This document is also a place holder to keep track of passive scanning improvement related discussions.
(Notes: The main differences from 12/0406r1 to 12/0406r2 are the additions of Slide 11 to 15. Also, further technical discussions are expected before and during 2012-May meeting.)

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2
InterDigital, KDDI, Nokia, Huawei, Intel, Qcomm

## Slide 4
Background, related contributions
12/0191r0: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r2: Approved TGai SFD initial document; (12/0151r3 with page numbers)
Multiple contributions have been submitted to 802.11ai TG regarding passive scanning improvements, e.g.,
  11-12-0276-00-00ai-passive-scanning-comparison
  11-12-0277-00-00ai-hybrid-scanning
  11-12-0239-01-00ai-passive-scanning-enhancements
  11-12-0288-00-00ai-passive-scanning-requirement-for-sfd
  11-12-0042-01-00ai-fils-beacon-proposal
  11-12-0292-00-00ai-beacon-pointer

## Slide 5: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
In addition to regular/full beacon transmissions, a smaller frame is transmitted more frequently
  The smaller frame provides AP/Network information for initial link setup
The type of the frequently transmitted smaller MAC frame:
  (Modified) Measurement Pilot frame
  Newly designed management frame, e.g., Sub-beacon / FILS beacon
  Beacon frame with very restricted inclusion of information elements, i.e., only the essential info for link setup,

## Slide 6: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
Contents of such smaller/more-frequent MAC frame:
  SSID only;
  The current measurement pilot information elements plus some optional sub-elements;
  The current measurement pilot information elements plus time pointer fields to point to full/regular TBTT;
  All the essential info for link setup so that the scanning STA does not need to wait for regular beacon or probe request/response;
  Information of neighbor BSSs; Enabling the discovery of neighbor BSSs operating parameters

## Slide 7: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
Transmission intervals of smaller/more-frequent MAC frame
  The frame is transmitted after target transmission time
  The frame is transmitted if AP has not transmitted a Beacon, Probe Response or Measurement Pilot frame within a duration
  The frame is transmitted if AP has not transmitted or received a Beacon, Probe Response or Measurement Pilot containing its parameters within a duration

## Slide 8: Next steps
The group agreed on the objectives of the passive scanning
  As shown in the following slides
The discussions to understand and to analyse the operation of the passive scanning mechanisms is ongoing
  Target is to understand and review the details of the open issues and look for possibilities to merge the proposals
  Target is to compare the proposals against the objective for enhanced passive scanning

## Slide 9: The objectives of 802.11ai enhanced passive scanning
  To enable faster AP discovery
  To optimize the wireless medium occupancy of the scanning related MAC frames
  To reduce power consumption of the passive scanning non-AP STAs

## Slide 10: Motion for proposed text for SFD (in 2012-March meeting)
Motion: Add the following text to Clause 5 “Fast Network Discovery” of TGai SFD, 12/0151
The 802.11ai shall support improved passive scanning mechanisms to facilitate fast initial link setup, and/or to reduce the air time occupancy of MAC frames used for scanning.
Reducing power consumption of the passive scanning non-AP STAs is desirable.
Moved: Tom Siep
  Seconded: Lee Armstrong
  Results: Yes 29 No 0 Abstain 3

## Slide 11: Motions for proposed text for SFD (for 2012-May meeting)
Motion-1: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
In addition to full beacon transmissions, a lower wireless medium occupancy MAC frame is transmitted more frequently to support a quick AP/Network Discovery for a fast initial link setup.
Mover:
  Seconder:
  Results: Yes No Abstain_________

## Slide 12: Motions for proposed text for SFD (for 2012-May meeting)
Motion-2: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The lower wireless medium occupancy MAC frame is known as FILS Beacon, which is
a Modified Measurement Pilot frame, or
a newly designed MAC management frame, or
a beacon frame with restricted inclusion of information elements, i.e., only the essential info for link setup.
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 13: Motions for proposed text for SFD (for 2012-May meeting)
Motion-3: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS beacon frame may be transmitted at target transmission time periodically or non-periodically.
The time gap between regular beacon and FILS beacon should meet the minimum interval of guard time period as specified by dot11aiFILSBeaconMinimumInterval.
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 14: Motions for proposed text for SFD (for 2012-May meeting)
Motion-4: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS beacon frame shall at least include the information of the SSID of the transmitting AP.
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 15: Motions for proposed text for SFD (for 2012-May meeting)
Motion-5: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The contents of the FILS beacon frame also include:
The current measurement pilot information elements plus time pointer fields to point to full/regular TBTT;
All the essential info for link setup so that the scanning STA does not need to wait for regular beacon or probe request/response; and
Information of neighbor BSSs; Enabling the discovery of neighbor BSSs operating parameters
Mover:
  Seconder:
  Results: Yes No Abstain________