## Slide 1: Proposed SFD Text for 802.11ai Passive Scanning Improvement
Date: 2012-05-16
Authors:

## Slide 2: Abstract
This document proposes text to be inserted in TGai Specification Framework Document (SFD) regarding 802.11ai passive scanning improvements.
This document is also a place holder to keep track of passive scanning improvement related discussions.

## Slide 3: Revision History
12/0406r0: Initial joined contribution about passive scanning enhancements, in 2012-March meeting;
12/0406r1: added the motion voting results in 2012-March meeting;
12/0406r2: added slide 11 to slide 15 with proposed motions based on further harmonization discussions before 2012-May meeting submission deadline;
12/0406r3: revised slide 12 to slide15 based on further harmonization discussions before 2012-May meeting;
12/0406r4: revised based on the outcome of passive scanning ad hoc discussions on May 14, 2012;
12/0406r5: revised based on further harmonization discussions before and during 2nd session of passive scanning ad hoc discussions on May 16, 2012;

## Slide 4
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2
InterDigital, KDDI, Nokia, Huawei, Intel, Qcomm

## Slide 5: Discussions during 2012-March Meeting

## Slide 6
Background, related contributions
12/0191r0: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r2: Approved TGai SFD initial document; (12/0151r3 with page numbers)
Multiple contributions have been submitted to 802.11ai TG regarding passive scanning improvements, e.g.,
  11-12-0276-00-00ai-passive-scanning-comparison
  11-12-0277-00-00ai-hybrid-scanning
  11-12-0239-01-00ai-passive-scanning-enhancements
  11-12-0288-00-00ai-passive-scanning-requirement-for-sfd
  11-12-0042-01-00ai-fils-beacon-proposal
  11-12-0292-00-00ai-beacon-pointer

## Slide 7: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
In addition to regular/full beacon transmissions, a smaller frame is transmitted more frequently
  The smaller frame provides AP/Network information for initial link setup
The type of the frequently transmitted smaller MAC frame:
  (Modified) Measurement Pilot frame
  Newly designed management frame, e.g., Sub-beacon / FILS beacon
  Beacon frame with very restricted inclusion of information elements, i.e., only the essential info for link setup,

## Slide 8: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
Contents of such smaller/more-frequent MAC frame:
  SSID only;
  The current measurement pilot information elements plus some optional sub-elements;
  The current measurement pilot information elements plus time pointer fields to point to full/regular TBTT;
  All the essential info for link setup so that the scanning STA does not need to wait for regular beacon or probe request/response;
  Information of neighbor BSSs; Enabling the discovery of neighbor BSSs operating parameters

## Slide 9: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
Transmission intervals of smaller/more-frequent MAC frame
  The frame is transmitted after target transmission time
  The frame is transmitted if AP has not transmitted a Beacon, Probe Response or Measurement Pilot frame within a duration
  The frame is transmitted if AP has not transmitted or received a Beacon, Probe Response or Measurement Pilot containing its parameters within a duration

## Slide 10: Next steps
The group agreed on the objectives of the passive scanning
  As shown in the following slides
The discussions to understand and to analyse the operation of the passive scanning mechanisms is ongoing
  Target is to understand and review the details of the open issues and look for possibilities to merge the proposals
  Target is to compare the proposals against the objective for enhanced passive scanning

## Slide 11: The objectives of 802.11ai enhanced passive scanning
  To enable faster AP discovery
  To optimize the wireless medium occupancy of the scanning related MAC frames
  To reduce power consumption of the passive scanning non-AP STAs

## Slide 12: Motion for proposed text for SFD (in 2012-March meeting)
Motion: Add the following text to Clause 5 “Fast Network Discovery” of TGai SFD, 12/0151
The 802.11ai shall support improved passive scanning mechanisms to facilitate fast initial link setup, and/or to reduce the air time occupancy of MAC frames used for scanning.
Reducing power consumption of the passive scanning non-AP STAs is desirable.
Moved: Tom Siep
  Seconded: Lee Armstrong
  Results: Yes 29 No 0 Abstain 3

## Slide 13: Discussions before/during 2012-May Meeting

## Slide 14
Background, related contributions
12/0191r0: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r2: Approved TGai SFD initial document; (12/0151r3 with page numbers)
Multiple contributions have been submitted to 802.11ai TG regarding passive scanning improvements, e.g.,
  11-12-0276-00-00ai-passive-scanning-comparison
  11-12-0277-00-00ai-hybrid-scanning
  11-12-0239-01-00ai-passive-scanning-enhancements
  11-12-0288-00-00ai-passive-scanning-requirement-for-sfd
  11-12-0042-01-00ai-fils-beacon-proposal
  11-12-0292-00-00ai-beacon-pointer
  Two contributions from 2012-May meeting are recommended to be incorporated into this joined contribution discussions:
    11-12-0545-01-00ai-access-control-mechanism-for-fils
    11-12-0567-00-00ai-multiple-frequency-channel-scanning

## Slide 15: Straw Poll for proposed text for SFD (for 2012-May meeting)
Straw-Poll-1: Do you support Inserting the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
In addition to full beacon transmissions, a lower wireless medium occupancy MAC frame may be transmitted more frequently to support a quick AP/Network Discovery for a fast initial link setup.
  Results: Yes 31 No 0 need more info 8

## Slide 16: FILS Beacon over time
The periodicity of the FILS Beacon may change over operation time of FILS AP
time
Case 1
Case 2
Case 3
Case 4
T1
T2
time
time
time
time
Beacon
FILS Beacon
T2

## Slide 17: Straw Polls for proposed text for SFD (for 2012-May meeting)
Straw-Poll-2: Do you support Inserting the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The AP may transmit a MAC frame, to be defined as “FILS Discovery Frame”, between full Beacon instances to support a quick AP/Network Discovery for a fast initial link setup.
The FILS Discovery Frame may be transmitted periodically and/or non-periodically.
If transmitted periodically, the periodicity of the FILS Discovery Frame may be changed.
The interval between regular beacon and FILS Discovery Frame shall be no less than dot11aiFILSBeaconMinimumInterval.
  Results: Yes 25 No 2 Need more info:_______0__

## Slide 18: Motions for proposed text for SFD (for 2012-May meeting)
Motion-1: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The AP may transmit a MAC frame, to be defined as “FILS Discovery Frame”, between full Beacon instances to support a quick AP/Network Discovery for a fast initial link setup.
The FILS Discovery Frame may be transmitted periodically and/or non-periodically.
If transmitted periodically, the periodicity of the FILS Discovery Frame may be changed.
The interval between regular beacon and FILS Discovery Frame shall be no less than dot11aiFILSBeaconMinimumInterval.
Mover:
  Seconder:
  Results: Yes No Abstain_________

## Slide 19: Straw Polls for proposed text for SFD (for 2012-May meeting)
Straw-Poll-3: Do you support Inserting the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS Discovery Frame is a public action frame, which is one of the following:
a Modified Measurement Pilot frame, or
a Modified 11ah short beacon frame, or
a newly designed MAC public action frame.
  Results: Yes 26 No 0 Need more info____3____

## Slide 20: Motions for proposed text for SFD (for 2012-May meeting)
Motion-2: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS Discovery Frame is a public action frame, which is one of the following:
a Modified Measurement Pilot frame, or
a Modified 11ah short beacon frame, or
a newly designed MAC public action frame.
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 21: Straw Polls for proposed text for SFD (for 2012-May meeting)
Straw Poll-4: Do you agree Inserting the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS Discovery frame from an AP provides info to enable fast AP/Network discovery.
  Results: Yes 11 No 3 abstain___17_____

## Slide 22: Straw Polls for proposed text for SFD (for 2012-May meeting)
Straw Poll-5: Do you agree Inserting the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS Discovery frame from an AP provides enough info to initiate association to that AP.
  Results: Yes 11 No 3 Abstain_____15___

## Slide 23: Motions for proposed text for SFD (for 2012-May meeting)
Motion-3: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS Discovery frame from an AP provides one of the following:
enough info to initiate association to that AP; or
info to enable fast AP/Network discovery.
(Notes: discussed in May 16 passive scanning ad hoc meeting; saw different opinions based on the straw polls; need further discussions.)
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 24: Motions for proposed text for SFD (for 2012-May meeting)
Motion-4: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The FILS beacon frame shall at least include the information of the SSID of the transmitting AP.
(notes: had a quick discussion in May 16 ad hoc meeting; suggested to first discuss the previous motion about the purpose of FILS discovery frame.)
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 25: Motions for proposed text for SFD (for 2012-May meeting)
Motion-5: Insert the following text to Section 6.2.1 on page 7 of TGai SFD, 12/0151r7
The contents of the FILS beacon frame also include:
The current measurement pilot information elements plus time pointer fields to point to full/regular TBTT;
All the essential info for link setup so that the scanning STA does not need to wait for regular beacon or probe request/response; and
Information of neighbor BSSs; Enabling the discovery of neighbor BSSs operating parameters;
Information of the FILS beacon transmission time of other BSSs;
(notes: did not discuss this one in the passive scanning ad hoc sessions in May, due to time limitation.)
Mover:
  Seconder:
  Results: Yes No Abstain________

## Slide 26: Open issues for FILS enhanced passive scanning (further discussion needed /ongoing)
One recommendation from Passive Scanning ad hoc discussion on May 14, 2012, evening session:
  Improve passive scanning by making changes to the full/regular Beacon frame.

## Slide 27: Straw Polls for proposed text for SFD (for 2012-May meeting)
Straw-Poll-2: Do you agree TGai should consider:
  The full/regular Beacon frame maybe extended to carry the information that indicates how many STAs the AP can continue to accept to support a better AP discovery/selection in FILS scenario.
  (notes: did not discuss this item in the Passive Scanning ad hoc discussion session on May 16, due to time limitation.)
  Results: Yes No Need more info: ______