## Slide 1: [place presentation subject title text here]
Date: 2012-04-03
Authors:

## Slide 2: Abstract
Proposed introductory text for 11ai Draft

## Slide 3: Introduction
IEEE 802.11 devices are increasingly becoming more mobile devices. The Project 802.11ai Task Group (TGai) primary need comes from an environment where a large number of mobile users are constantly entering and leaving the coverage area of an extended service set (ESS). Every time the mobile device enters an ESS, the mobile device has to do an initial set-up with an access point (AP) to establish wireless local area network (LAN) connectivity. (continued next slide)

## Slide 4: Introduction: paragraph 1 (cont’d)
Full link establishment works well when the number of new stations (STAs) in a given time period is small. It also works well when the number of choices for the STA for connection is small. In highly situations where there are a very high number of STAs and APs, current association mechanisms over-the-air association inefficiencies limit access to network resources.

## Slide 5: Introduction: paragraph 2
Efficient mechanisms that scale well when a high number of users simultaneously enter a complex AP environment are needed. This requires the ESS to minimize the time the STAs spend in initial link setup, while maintaining secure authentication. The purpose of Fast Initial Link Setup (FILS) is to enable efficient high-volume initial access to network services.