## Slide 1: Proposed SFD Text for 802.11ai AP/STA Initiated FILS Optmizations
Date: 2012-05-03
Authors:

## Slide 2: Abstract
This document proposes additional text to be inserted in Subsection 3.1 of the TGai Specification Framework Document (SFD), 12/0151r7, regarding a FILS procedure that allows 802.11ai AP and STA to initiate link setup optimizations.
This is a follow-up contribution with next level of details for existing text in the current TGai SFD.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2,3, 4

## Slide 4
Background
12/0191r3: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r7: Approved TGai SFD document up-to 2012 March meeting;
Text in Subsection 3.1 of TGai SFD, 12/0151r7:
A TGai solution may allow AP and STA to initiate link setup optimizations.

## Slide 5: Discussions
AP-Initiated vs. STA-Initiated Link Setup Optimizations:
  Currently, only STA-initiated!
In the current link setup process, all the function phases, e.g., Network Discovery, TSF, 802.11 Authentication, Association, etc., are initiated by the STA, which means:
  STA can choose and pick, not AP;
  AP only passively responds.
There are cases where the AP has the proper or even better knowledge to initiate link setup optimizations, e.g.,
  AP knows the services that can be provided by the network behind it;
  AP knows the required air link transmission adjustment of the STA based on the reception of the frames from the STA;
  AP knows its own capacity and loading, so AP can proactively inform STAs its capacity limitation;
  AP may pre-acquired certain knowledge about the STA, e.g., a pre-established security association of STA with the network.

## Slide 6: Discussions – con’t
To allow both AP and STA to initiate link setup optimization, procedure and signaling supports are needed;
Proposed procedural actions and Signaling support considerations:
  FILS capability indication: Essentially an one-bit flag, provided in the earlier messages of the link to be setup .  this has been already included in the current TGai SFD at page 6, section 6.1.2.
  Negotiation of link setup optimizations:
    a procedure for the two STAs of the link to be setup to negotiate or synchronize the applied link setup optimizations;
    Can be initiated by AP and/or STA;
  Signaling support for the negotiation of link setup optimizations:
    FILS-Initiation: containing the suggestions of link setup optimizations proposed by the transmitter of this initiation signal, e.g., skip 802.11 Open Auth step, uese EAP-RP for authentication, use 3-way handshaking for Key provisioning, etc.;
    FILS-Response: containing the responses to the received link setup optimization suggestions, e.g., full-confirmation, partial-confirmation, or rejection.
  Signaling efficiency considerations, e.g.,
    Piggyback on existing message round;
    Pre-defined a set of 11ai supported link setup optimizations.

## Slide 7: Discussions – con’t Example of AP-Initiated FILS Negotiation

## Slide 8: Motions for Proposed Text for SFD
Motion-1: add the following text to Subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7
  A TGai solution should support a procedure for the two STAs of the link to be setup to negotiate or synchronize the applicable link setup optimizations, called as FILS negotiation procedure.
    The FILS negotiation procedure can be initiated by AP and/or STA.
Mover:
Seconder:
Result Yes NO Abstain_______________

## Slide 9: Motions for Proposed Text for SFD
Motion-2: add the following text to Subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7
  A TGai solution should provide signaling support for the negotiation of link setup optimizations between the two ends of the link to be set up.
  The signals used in the negotiation of link setup optimizations may include:
    FILS-Initiation: containing the suggestions of link setup optimizations proposed by the transmitter of this initiation signal, which can be either end of the link to be set up.
    FILS-Response: containing the responses to the received link setup optimization suggestions, e.g., full-confirmation, partial-confirmation, or rejection.
Mover:
Seconder:
Result Yes NO Abstain_______________