## Slide 1: Scanning and FILS requirements
Date: 2012-05-03
Authors:

## Slide 2: Abstract
The presentation discusses on the delay requirement to be able to setup Initial Link within 100ms.
The presentation contains simulation results of AP discovery with scanning duration fulfilling the FILS requirements. The simulation results show:
  Passive scanning upper bound delay does not meet the FILS delay requirements
  The scanning STA needs to have means to request scanning responses and to indicate that it is scanning
    The request may be cancelled, if it is not needed

## Slide 3: FILS overview
The most fundamental FILS requirement is to establish Initial Link Setup within 100 ms
  To simplify the requirements one may assume common delay limit for discovery and setup signaling
    AP discovery
    Network discovery
    Upper layer setup
    Authentication, association
  First, the optimal AP and network for initial link setup is discovered
  Then, the setup signaling associates, authenticates and configures the higher layer parameters

## Slide 4: FILS delay requirements
The message exchange for higher layer setup is hard to speed-up
  The messages exchange takes time and servers require response time
  Depending on the locations of the servers, the signaling may require up to 60 ms
The discovery operation should discover the optimal AP for initial link creation
  The discovery operation shall be faster than 40 ms

## Slide 5: Discovery alternatives
The STA may use passive or active scanning for AP discovery
  These scanning mechanisms are described more details in the following slides
The STA may use GAS signaling for network discovery
  The STA should avoid transmitting unnecessary GAS requests
  The probe response and beacon frames should contain information to avoid unnecessary GAS requests

## Slide 6: Passive scanning is upper bound delay is long
A passive scanning STA listens at a channel for a time period which is random from the surrounding beaconing device timing perspective
  Many non-FILS APs transmit only Beacons with 100 TU interval, thus the passive scanning upper bound delay is at least 100 TU per channel
  All (periodically) transmitted frames may not be received
  Longer listening period ensures the reception of the frames
    For instance, it takes 100 TU to ensure that the channel is Idle / empty
    For instance, scanning of 5 Idle channels takes 5 * 100 TU = 500 TU (~500 ms)
These delays are not acceptable for FILS!
Passive scanning duration
Time

## Slide 7: Passive scanning enhancements create large overhead
In the passive scanning enhancements beaconing devices are made to transmit FILS beacon, Beacon or Measurement Pilot frame more frequently:
  In order to meet FILS requirements an AP should transmit a scanning frame every 5 to 10 ms.
  Very frequent transmissions may cause race between APs, every AP aims to be the most easy to find and transmit very often FILS beacon
    Frequent, possibly unneeded transmissions waste resources, especially when many APs operate in the same area
    AP power consumption is increased

## Slide 8: The reliability of the scanning needs to be ensured
When the channel is Idle, the STA can easily transmit a Probe Request
  A Probe Response will be transmitted within 5 ms from Probe Response transmission as specified in Wi-Fi tests
  Precise request reduces the number of responses and lead to fast initial link setup (FILS)
  The scanning STA easily detects Idle channel
  No need to consume extra transmission resources for passive scanning frames transmission
The active scanning is ideal solution!

## Slide 9: The reliability of the scanning needs to be ensured
When congestion of the media is high, the STA shall ensure the discovery of desired AP
  The scanning STA tries to obtain TXOP for Probe Request transmission
  The Probe Request transmission should be cancelled, if
    An acceptable AP is discovered before the Probe Request is transmitted
    A copy of similar Probe Request is detected
  Probe Request transmission ensures that responses will be transmitted within reasonable upper delay bound
    The scanning STA doesn’t need to rely purely on the good will and frequent transmission of the scanning frame from the desired AP
    The scanning STA trusts only to itself; it transmits request and the scanning responses are transmitted within acceptable delay

## Slide 10: The reliability of the scanning needs to be ensured
As commonly known, the Probe Response shall be transmitted within 5 ms from the Probe Response in idle channel
  The passive scanning frames are transmitted accoridng their transmission principle
    The variation in transmission time is much higher
    Upper delay bound may be long
  Typical maximum channel listening time to receive Probe Responses is less than 10 ms

## Slide 11: Simple implementation of scanning STA
A FILS capable scanning STA shall always try to transmit a Probe Request to discover APs
  The scanning STA cannot know the load in the channel or availability of the APs before it scans the channel
  Cancelling unnecessary Probe Requests is always possible
    No need to discover APs, if an acceptable AP is discovered
    No need to transmit duplicate requests
  A request enables a scanning STA to specify what it is looking for: AP, the Roaming ID, or the Network ID
  FILS STAs will directly associate with appropriate AP, the device will not request from end user which network to use  too slow!
    The discovery of the APs to which the STA is not allowed to associate is waste of time and power

## Slide 12: Simple implementation of APs
The APs shall rely that scanning STAs transmit Probe Request
  This avoids race condition of frequent transmissions of scanning frames, the APs do not compete for discoverability
    This avoids overhead of frequent frames transmission
    APs know when to transmit discovery frames
    The requests ensure that scanning frames are available at the scanning time

## Slide 13: Selecting the next scanned channel
Beacon and Measurement Pilot frames do not hint the candidate for the next scanned channel
  No help to select the scanning order from frames transmitted for passive scanning
The Probe Responses indicate the BSSs in other channels
  Help to decide the next scanned channel to discover suitable candidate AP faster

## Slide 14: Simulation of the active and passive scanning performance

## Slide 15: Simulation overview
A simulation scenario was defined and simulations were run to compare active and passive scanning performance with FILS delay requirements
  It is assumed that one channel scanning is done at maximum in 16 ms
Performance of the passive and active scanning was compared in the same simulation scenario as introduced in 11-12-279r0
  The following slides recapture the scenario in details
The simulations measured the success of AP discovery

## Slide 16: Simulation scenario
10000 STAs were created to random positions within the room at random intervals
    The STAs were created with mean of 1 ms, 10 ms and 100 ms intervals
    This results to 3 different real time simulation lengths (10s, 100s and 1000s)
Following steps were taken for each created STA:
  Performed scanning to discover AP with the best RxP level
    Passive scanning STA listens to the channel for 16 ms
    Active scanning STA listens to the channel for 10 ms after it has transmitted a Probe Request.
      Total Active scanning duration is 10 – 16 ms
  Select the AP with the highest RxP level, and transmit a frame of 200 octets to the selected AP that will subsequently transmit a frame of 200 octets to the STA
  The STA is removed from the simulation

## Slide 17: Simulation scenarios
Three different scenarios were simulated:
  1.Scenario: All scanning STAs use legacy active scanning (no enhancements in active scanning)
  2.Scenario: 50% of STAs use passive scanning and 50% use active scanning
    The STAs make random selection to use active or passive scanning
  3.Scenario: All STAs use passive scanning

## Slide 18: Simulation scenarios
A single room indoor scenario with 4 APs and 4 background traffic STAs
When background traffic was present, each background STA transmitted and received 2Mbps data (4Mbps per STA)
  802.11ac 40MHz, 2*2 MIMO
The TGac propagation model was used
30m
30m
10m
10m
10m
10m
10m
AP
AP
AP
AP
3m
3m
STA
STA
STA
STA

## Slide 19: Simulation scenarios
The management frames used the AC 3, background data used the AC1
  The default EDCA parameters were used
  Beacon, Probe Request and Probe Response were transmitted at the lowest MCS with the 20 MHz transmission bandwidth (6 Mbit/s)
    Beacon frame is 145 octets, TX ON 220 micro seconds
    Probe Request is 101 octets, TX ON 156 micro saeconds
    Probe Response is 165 octets, TX ON 240 microseconds
Probe Delay is 6 ms

## Slide 20: Simulation results
The output parameters are as follows:
  The proportion of cases in which the parameters of the best AP was discovered
    Successful scanning 
  The proportion of cases in which the parameters of the best AP were not discovered
    Erroneous scanning, Non-optimal / wrong AP was selected for association 
  The proportion of cases in which parameters of any AP were not discovered
    Total failure of the scanning 

## Slide 21: Simulation results

## Slide 22: Simulation results
Results show solid performance for active scanning and disasterous performance for passive scanning
Active scanning discovers the best AP in more than 95% of the simulation cases
  Typically < 2% of the scanning terminals do not find the best AP
Passive scanning discovers the best AP in 16% of the simulation cases
  Over 60% of the cases no AP parameters were discovered

## Slide 23: Summary
Passive scanning upper bound delay does not meet FILS delay requirements
The scanning STA shall request scanning responses and to indicate that it is scanning
  The transmission of request shall be cancelled, if it is not needed. When the request is cancelled, the scanning operation is close to passive scanning
When scanning STA tries to transmit the scanning request, the AP and STA implementation may be simplified

## Slide 24: Strawpoll
Do you agree that the scanning STA has no control of the upper delay bound of the passive scanning?

## Slide 25: Strawpoll
Do you agree that a scanning STA shall try to transmit a Probe Request and cancel the Probe Request transmission, if:
    Acceptable AP is discovered
    Similar Probe Request is received ?

## Slide 26: Motion
Do you agree adding to specification framework document the following sentence:
”A scanning STA shall initiate the AP discovery by transmitting a Probe Request frame. If an acceptable AP is discovered or a similar Probe Request is received before the Probe Request is transmitted, the STA shall cancel the Probe Request transmission.”