## Slide 1: Fast passive scan for FILS
Date: 2012-04-21
Authors:
Name | Affiliations | Address | Phone | email
Dapeng Liu | China Mobile | 32 Xuanwumen West Street Beijng, Xicheng District, 100053 China | +86-13911788933 | liudapeng@chinamobile.com

## Slide 2: Abstract
This proposal aims to reduce the time used for passive scan in FILS scenario.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Problem of passive scan
The problem
STA need to switch to different channels and stay on that channel monitoring for a period of time.
In the above example, the scanning time would be: T1+T2+T3, where T1 and T2 is wasted.
CH1
CH2
CH3
Monitoring window
T1
T2
T3

## Slide 5: Possible solution
Solution : 802.11ai can use a pre-configured/dedicated channel for passive scan
CHx
APs send beacons use a pre-configured channel.
The beacons should contain more information than regular ones:
  E.g.: The channel that it really used for data transmission.
STA monitoring that particular channel instead of scanning all the channels.
Scanning time is reduced since not necessary to change channels and wait.
Beacon 1: AP1 use channel 1 for transmission
Beacon 2: AP2 use channel 2 for transmission

## Slide 6: Problems need be solved
How does the STA and AP know which is the channel for beacon scanning and monitoring?
  11ai can specify a default channel for passive scan
How to avoid the confliction of the beacons sent by different APs?
  Need further study

## Slide 7
Questions?