## Slide 1: Clarification of the STA’s listening duration for Probe Response monitoring
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Date: 2012-05-16
Authors:

## Slide 2: Abstract
This contribution clarifies the Probe Response omission and Probe Response broadcasting procedure.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background
Probe Response Omission and Probe Response broadcasting
  IEEE802.11-12/0151r7 describes “An FILS (Fast Initial Link Setup) Capable AP may omit transmission of Probe Response frame to FILS capable STA(Station)s if the TBTT occurs within a predefined time interval.”
  IEEE802.11-12/0151r7 describes “ An AP may respond to multiple Probe Requests from one or more FILS capable STAs with a single broadcast addressed response frame.”
  For Probe Response omission AP shall know the STA’s Probe Timer (i.e., Min listening duration, max listening duration) for Probe Response omission and Probe Response broadcasting.
  Current SFD only described max listening duration for which the STA indicates it will wait for Probe Response transmission.
    STA may include a wait-time-for-Probe-Response element to Probe Request.
  AP shall know STA’s min listening duration as well as max listening duration.

## Slide 5: Proposal
STA may include a wait-time-for-Probe-Response element to Probe Request to provide a min listening duration for which the STA indicates it will wait for Probe Response transmission.

## Slide 6: Example
Example of Probe Response Omission
Figure1 . Omission of the Probe Response

## Slide 7: Conclusion
Knowing the STA dependent time window (i.e., min listening duration, max listening duration) allows AP to omit or broadcast the Probe Response.

## Slide 8: Straw poll
Modify the text of SFD 6.1.7 as following:
“STA may include a wait-time-for-Probe-Response element to Probe Request to provide a min and max listening duration for which the STA indicates it will wait for Probe Response transmission.”

## Slide 9: Motion 1
Modify the text of SFD 6.1.7 as following:
“STA may include a wait-time-for-Probe-Response element to Probe Request to provide a min and max listening duration for which the STA indicates it will wait for Probe Response transmission.”
Moved :
Seconded:
Yes: No: Abstain: