## Slide 1: Probe Response Broadcasting
Name | Affiliations | Address | Phone | email
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Date: 2012-05-xx
Authors:

## Slide 2: Abstract
This document proposes enhancement of active scanning by reducing the Probe Response transmission of AP.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background
Existing Active Scanning Procedure
  Wait until the ProbeDelay time has expired or a PHYRxStart.indication primitive has been received.
  Perform the Basic Access procedure as defined in 9.3.4.2.
  Send a probe request to the broadcast destination address, with the SSID and BSSID from the MLME-SCAN.request primitive. When the SSID List is present in the MLME-SCAN.request primitive, send one or more probe request frames, each with an SSID indicated in the SSID List and the BSSID from the MLME-SCAN.request primitive.
  Set to 0 and start a ProbeTimer.
  If PHY-CCA.indication (busy) primitive has not been detected before the ProbeTimer reaches MinChannelTime, then set NAV to 0 and scan the next channel, else when ProbeTimer reaches MaxChannelTime, process all received probe responses.
  Set NAV to 0 and scan the next channel.

## Slide 5: Motivation (1/2)
In IEEE802.11ai SFD (12/0151r7),
  An FILS Capable AP may omit transmission of Probe Response frame to FILS capable STAs if the TBTT occurs within a predefined time interval.
  An AP may respond to multiple Probe Requests from one or more FILS capable STAs with a single broadcast addressed response frame.
  STA may include a wait-time-for-Probe-Response element to Probe Request to provide a max listening duration for which the STA indicates it will wait for Probe Response transmission.
AP may broadcast Probe Response after receiving multiple Probe Requests
After sending Probe Request, STA should receive Probe Response (or Beacon) before the wait-time-for-Probe-Response expires.
In the previous slide, STA switches to other channel when Probe Timer reaches MinChannelTime (PHY-CCA.indication with ‘busy’ not detected) or MaxChannelTime (otherwise).

## Slide 6: Motivation (2/2)
In order to broadcast Probe Response (or Beacon) instead of unicasting Probe Response, AP has to know whether STA sending a Probe Request waits on the channel till either MinChannelTime or MaxChannelTime.

## Slide 7: Proposal
The parameter to inform the AP of whether the STA has received any MAC frame (or detected any PHY signal) before sending Probe Request on the channel can be included in Probe Request.
Based on this information, AP can send Probe Response by either STA’s MaxChannelTime or MinChannelTime.
MinChannelTime may be set to predefined time interval as preconfigured parameter of both STA and AP. Otherwise MinchannelTime can be can be informed AP by using wait-time-for-Probe-Response element included in Probe Request.
The values of STA’s MaxChannelTime can be informed AP by using wait-time-for-Probe-Response element included in Probe Request.

## Slide 8: Example (1/2)
Figure1 . Probe response broadcasting

## Slide 9: Example (2/2)
Before sending Probe Request, STA checks whether or not the medium is idle during the certain time interval (i.e., ProbeDelay and DIFS, etc).
If medium is busy, STA perform backoff operation before sending Probe Request based on Basic Access procedure.
STA may receive MAC frame from any STA (non-AP STA or AP) before sending Probe Request.
  STA 2 may receive any MAC frame (e.g., Probe Request from STA 1) before sending Probe Request. Also, Probe Request sent from STA2 can be received by STA 1 which is waiting Probe Response.
  In this case, STA 1 sets ProbeTimer to MaxChannelTime.
  If STA2 informs the AP of its reception of any MAC frame (e.g., Probe Request) before Probe Request by using its Probe Request, AP can know that STA 1 sets ProbeTimer to MaxChannelTime. And AP may broadcast Probe Response within STA 1’s MaxChannelTime.

## Slide 10: Conclusion
Proposed active scanning allows AP to broadcast the Probe Response to multiple STAs which sent the Probe Request.

## Slide 11: Motion
Move to add the following text to the clause 6 of the specification framework document:
6.1.9 Probe Response Monitoring
802.11ai shall support that STA informs AP whether STA sending a Probe Request waits on the channel till either MinChannelTime or MaxChannelTime.
Moved :
Seconded:
Yes: No: Abstain: