## Slide 1: Probe Response Broadcasting
Name | Affiliations | Address | Phone | email
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Date: 2012-05-16
Authors:

## Slide 2: Abstract
This contribution proposes the mechanism of simplifying the Probe Response transmission.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Motivation
IEEE802.11ai SFD (12/0151r7) describes,
  An AP may respond to multiple Probe Requests from one or more FILS capable STAs with a single broadcast addressed response frame.
If the AP receives the Probe Request from only one STA, AP sends the unicast Probe Response.
If the AP knows that two or more STAs sent the Probe Request, AP may send the broadcast addressed Probe Response.
If the STA receives the Probe Request sent by other STA before sending the Probe Request, STA informs the AP that other STA sent the Probe Request by including the Probe Request Detection Indication in Probe Request.
  Based on this information, AP can broadcast the Probe Request.

## Slide 5: Proposal
Probe Request Detection Indication may be included in Probe Request.

## Slide 6: Example
Figure1 . Probe response broadcasting

## Slide 7: Conclusion
If the STA receives the Probe Request sent by other STA before sending the Probe Request, STA informs the AP that other STA sent the Probe Request by including the Probe Request Detection Indication in Probe Request.
  Based on this information, AP can broadcast the Probe Request.

## Slide 8: Straw Poll
Do you support adding the following text to the clause 6 of the specification framework document:
6.1.9 Triggering the broadcast Probe Response Transmission
Triggering information for broadcast Probe Response transmission may be included in the Probe Request

## Slide 9: Motion
Move to add the following text to the clause 6 of the specification framework document:
6.1.9 Triggering the broadcast Probe Response Transmission
Triggering information for broadcast Probe Response transmission may be included in the Probe Request
Moved :
Seconded:
Yes: No: Abstain: