## Slide 1: Triggering the Broadcast Probe Response
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Date: 2012-09-17
Authors:

## Slide 2: Abstract
This contribution proposes the mechanism of simplifying the Probe Response transmission.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background (1/2)
IEEE 802.11ai SFD (12/0151r8) describes,
  Probe Response Collision Avoidance (11-12/0153r9)
    An AP may respond to multiple Probe Requests from one or more FILS capable STAs with a single broadcast addressed response frame.
Based on the above SFD,
  Unicast Probe Response transmission
    If the AP receives the Probe Request from only one STA, AP sends the unicast Probe Response to the STA.
    If the AP receives the Probe Request from more than two STAs and each Probe Requests are including the different contents, AP may send the Probe Response to the each STAs via unicast manner.
  Broadcast Probe Response transmission
    If the AP receives the Probe Request from more than two STAs and there are several number of Probe Request having same contents, AP may send the Probe Response to the STAs which having same Probe Request contents via broadcast manner.

## Slide 5: Background (2/2)
IEEE 802.11ai SFD (12/0151r8) describes,
  Omission of Probe Request(11-12/0655r5)
    STA may omit a probe request due to reception of , for example,
    Broadcast probe requests
    Broadcast probe responses
    Beacon
Based on above SFD,
  When the STA receives the Broadcast Probe Request from other STA, if the contents of the received Broadcast Probe Request are same as its Probe Request contents, STA may omit its Probe Request transmission.

## Slide 6: Proposal
The ‘triggering information for broadcast Probe Response transmission’ may be included in Probe Request for helping the broadcast Probe Response transmission of AP.
  When the STA receives the Broadcast Probe Request from other STA, if the contents of the received Broadcast Probe Request are same as its Probe Request contents and ‘triggering information for broadcast Probe Response transmission’ is included in received broadcast Probe Request, STA may omit its Probe Request transmission.
  If the AP receives the Probe Request including ‘triggering information for broadcast Probe Response transmission’ from STA, AP sends the broadcast Probe Response to the STAs instead of unicast Probe Response.

## Slide 7: Example of the proposal (1/2)
STA 1 sends the Probe Request which is not including the ‘triggering information for broadcast Probe Response transmission’ to the AP.
STA 2 overhears the Probe Request sent by STA 1. Because overheared Probe Request is not including the ‘triggering information for broadcast Probe Response transmission’, STA 2 sends the Probe Request which including the ‘triggering information for broadcast Probe Response transmission’ to the AP.
STA 3 overhears the Probe Request sent by STA 2. Because overheared Probe Request is including the ‘triggering information for broadcast Probe Response transmission’, STA 3 cancels the Probe Request transmission.
AP sends the broadcast Probe Response to the STAs because the AP has received the Probe Request which is including the ‘triggering information for broadcast Probe Response transmission’ from the STA 2.

## Slide 8: Example of the proposal (2/2)
Figure1 . Probe response broadcasting

## Slide 9: Straw Poll 1
Do you agree to add the sentence to TGai SFD, 12/0151r8.
  To trigger the broadcast Probe Response transmission of the AP, the source address (SA) of the non-AP STA included in the received Probe Request may be included in the Probe Request.
Yes:
No:
Abstain:

## Slide 10: Straw Poll 2
Do you agree to add the sentence to TGai SFD, 12/0151r8.
  A non-AP STA, before transmitting its Probe Request frame to an AP, may receive other non-AP STAs’ Probe Request frame(s). After receiving other non-AP STA’s Probe Request frame(s) which is including source address of the Probe Request frame which was received from other STA , the non-AP STA may omit the Probe Request transmission.
Yes:
No:
Abstain:

## Slide 11: Motion 1
    Move to add the following text to Section 6.2.3 of SFD?
    6.2.3 Probe Response
“To trigger the broadcast Probe Response transmission of the AP, the source address (SA) of the non-AP STA included in the received Probe Request may be included in the Probe Request.”
    Mover:
    Seconder:
    Result
    Yes No Abstain_______________

## Slide 12: Motion 2
    Move to add the following text to Section 6.2.9 of SFD?
    6.2.9 Omission of Probe Request
  “A non-AP STA, before transmitting its Probe Request frame to an AP, may receive other non-AP STAs’ Probe Request frame(s). After receiving other non-AP STA’s Probe Request frame(s) which is including source address of the Probe Request frame which was received from other STA , the non-AP STA may omit the Probe Request transmission.”
    Mover:
    Seconder:
    Result
    Yes No Abstain_______________