## Slide 1: Response Criteria of Probe Request
Date: 2012-05-04
Authors:

## Slide 2: Abstract
The presentation describes the response criteria to avoid transmission of unnecessary Probe Responses.
The following criteria are considered:
  The Inclusion List and Inclusion Parameters set criteria for STAs that are obliged to respond to the Probe Request.
  The Exclusion List sets criteria for STAs that shall not respond to the Probe Request.

## Slide 3: Solved problem
The presentation describes mechanism to avoid unecessary Probe Response transmissions
  The reduced amount of Probe Responses makes discovery reliable and fast
  The congestion and collisions in the channel are reduced
Without precise response criteria the Probe Response transmission create high traffic load and delay the transmission of the responses
  This is visible especially in densely populated area

## Slide 4: Advantages
Faster scanning
Reduced scanning overhead and transmission collisions
Simple to implement, no complicated processing
Improved discovery of new, unkonwn APs
  Responses from already known APs are avoided
  Better opportunity to discover other/all available APs
AP with desired capabilities and performance is discovered

## Slide 5: Related presentations
The response criteria has been discussed in many related presentations:
  11-1619 Active Scanning
  12-63 Selective transmission of Probe responses
  12-259 Reducing Probe Responses for faster AP discovery
  12-265 Selective transmission of Probe responses
  12-279 Scanning Simulations
This presentation collects the main response criteria concepts of these presentations

## Slide 6: The response criteria
The response criteria defines the STAs that are obliged to respond to Probe request. The Response Criteria consists of:
  Inclusion list; the MAC addresses and SSIDs os STAs that shall respond
  Inclusion parameters; the capabilities and/or performance criteria that responding STA shall fulfill
  Exclusion list; the MAC Addresses and SSIDs of STAs that shall not respond

## Slide 7: Inclusion List
The Inclusion List indicates the STAs that are obliged to respond to the Probe Request
  Multiple SSIDs and MAC addresses in a single Probe Request frame eliminate unnecessary transmissions of Probe Request frames
The Inclusion List includes:
    MAC Address List
    SSID / Mesh ID List
The SSID List is already present in Probe Requests
  The list may be shortened, i.e. The list may contain only the last 2 octets of MAC addresses

## Slide 8: Exclusion List
The Exclusion List indicates STAs that shall not respond to the Probe Request
  The scanning STA may already know the specific APs and avoid transmissions of unnecessary probe responses
The Exclusion List contains:
    MAC Address List
    SSID / Mesh ID List
The Exclusion and Inclusion Lists may have the same format
  The implementation is simple, no added complexity

## Slide 9: Inclusion Parameters
AP Capability criteria ensures performance of the AP
  The responses are requested from only HT, VHT or FILS capable APs
    The HT and VHT APs provide higher throughput for the device
    The FILS capability enables faster link setup
Link Quality criteria avoids poor quality link
  RSSI limit requests responses from APs that receive the request above the RSSI threshold
  Link performance is key criteria in AP selection

## Slide 10: Summary
With proposed response criteria the discovery becomes faster and it generates less overhead
The response criteria is simple to implement
  No additional complexity to discovery
  The most relevant parameters are already available for discovery

## Slide 11: Motion 1
Add the following sentence to the Specification Framework document:
” Probe Request may contain Inclusion List that specifies the MAC Addresses and SSIDs of hte STAs that shall respond to the request.”

## Slide 12: Motion 2
Add the following sentence to the Specification Framework document:
” Probe Request may contain Exclusion List that specifies the MAC Addresses and SSIDs of hte STAs that shall not respond to the request.”

## Slide 13: Motion 3
Add the following sentence to the Specification Framework document:
” Probe Response may contain Inclusion Parameters that specify the criteria of AP capabilites and link performance that the responding STAs shall fulfill.”