## Slide 1: Network Selection Optimization
Date: 2012-05-04
Authors:

## Slide 2: Abstract
Currently, STAs do Network Discovery by sending unicast GAS requests to APs this mechanism is very inefficient and time consuming, as shown in 11-1015r2
Prior to Network Discovery, STAs have to perform scanning, to learn the MAC address of the candidate APs. Most STAs on the market perform active scanning to save time.
Therefore, a STA ends up in most cases transmitting a broadcast Probe Request, followed by unicast GAS requests to all APs; this process is time consuming and wastes radio resources
This submission proposes to combine Probe request and GAS Requests

## Slide 3: Prior discussions
The time consuming aspect of the current Network Discovery procedure was documented in 11/1015r0 and its revisions, and discussed extensively in the TG
A broadcast based GAS request proposal was presented, however, it resulted in a discussion on combining GAS request with Probe Request.
There was one concern expressed for combining Probe Response with GAS Response, that a long GAS Response frame may not fit in a Probe Response frame

## Slide 4: Proposal
Combine Probe Request with GAS Request by including GAS Request IE into the Probe Request
Define a possibility to combine Probe Response with GAS Response
  If the GAS Response frame is too long, or not immediately available indicate in the Probe Request that a separate GAS Comeback Request Mechanism could be used to pull the responses from the AP. Otherwise include the GAS Response into the Probe Response

## Slide 5: Motion
Add the following text to section 6.3 of the SFD
For faster network discovery, STAs may combine Probe Requests and GAS Requests. AP STAs may combine Probe Response and GAS Response frames