## Slide 1: Selection of the AP for Scanning: 11ai Spec Framework Proposal
Date: 2012-05-04
May 2012

## Slide 2: Abstract
In active scanning, a STA transmits Probe Request frame in Broadcast, usually using wildcard SSID to find APs
It can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
This proposal reduces the overhead of active scanning by providing precise selection mechanism of the AP s to respond with Probe Response
Approach:
  Add Exclusion List to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response
    Substring of the SSIDs or Mesh IDs can be used in the List to indicate the APs or STAs to be excluded
Jae Seung Lee, ETRI
May 2012

## Slide 3: Background
This contribution is based on the following documents that have been presented at the previous IEEE 802.11 meeting
  11-12/0263r2 Spec Framework Proposal: Selection of the AP for Scanning
  11-12/0059r1 Selection of the AP for Scanning
  11-12/0060r0 Text for Selection of the AP for Scanning
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
Proposed Spec Framework text is included in the Motion section at the end of this contribution
Jae Seung Lee, ETRI
May 2012

## Slide 4: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI
May 2012

## Slide 5: Selection of the AP to Scan – Background (1/3)
To discover the AP to associate, a STA transmits Probe Request in Broadcast with wildcard SSID
APs transmit Probe Response  too many probe responses
AP 1
AP 2
AP 3
AP 4
AP n
STA
Probe Request on channel x (broadcast)
Probe Response
flooding
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Jae Seung Lee, ETRI
May 2012

## Slide 6: Selection of the AP to Scan – Background (2/3)
In many cases, STA has prior knowledge on which APs it does not want to receive Probe Response from
  It is not necessary for a STA to receive Probe Response from APs deployed by specific Service Providers if the user does not subscribe to the Service Providers
    Usually, specific substring is included in the SSID of such APs deployed by a specific Service Provider
    There are many users who do not have any WiFi Subscription for paid WiFi services provided by Service Providers
Jae Seung Lee, ETRI
May 2012

## Slide 7: Selection of the AP to Scan – Background (3/3)
  Usually, it is not necessary for a STA to receive Probe Response from the APs whose SSID include “_nomap”
    Google has announced a way for WiFi router owners to stop Google from including them in the company’s location database – by adding “_nomap” at the end of the SSID
    It is highly probable that AP whose SSID contains substring “_nomap” is not a public AP
 It will be beneficial if we can exclude such APs with specific known substrings from responding Probe Request
Slide 7
Jae Seung Lee, ETRI
May 2012

## Slide 8: Selection of the AP to Scan - Approach
Exclusion List is added to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response frame
Substring can be used in the List to indicate SSIDs or Mesh IDs
  helps to reduce the size of the Exclusion List
  Not necessary to include individual IDs in the Exclusion List
  Efficiently filter the APs with IDs with known substring
Exclusion List with substring capability can provide precise
selection of the AP to transmit Probe Response frame
Jae Seung Lee, ETRI
May 2012

## Slide 9: Selection of the AP to Scan – Example (1/3)
Example 1-1: Using existing active scanning method
. The user does not know the SSID. He does not have any WiFi subscription,
so he does not want to get response from APs deployed by Service Providers such as KT or SKT
SKT0002
SKT0003
Xx_nomap
Aa_nomap
SKT0006
KT0002
KT0003
KT0004
KT0005
Bb_nomap
KT0003
KT0004
KT0005
SKT_xy
SKT_zz
Hyatt_1
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(wildcard SSID)
Too many Probe Response frames !!
(Probe Responses from many APs are not helpful
for association)
.
.
.
Home_nomap
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
Private AP
Private AP
Private AP
Private AP
Jae Seung Lee, ETRI
May 2012

## Slide 10: Selection of the AP to Scan – Example (2/3)
Example 1-2: Selection of the AP to respond using Exclusion List with substring
. The user does not know the SSID. He does not have any WiFi subscription,
so he does not want to get response from APs deployed by Service Providers such as KT or SKT
include Exclusion list containing substring KT and _nomap into the Probe Request
 Do not need to list all the SSIDs to be filtered. Do not need to know full SSID to be filtered
KT0002
KT0003
KT0004
KT0005
Bb_nomap
KT0003
KT0004
KT0005
SKT_xy
SKT_zz
Hyatt_1
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(Exclusion List with SSID substring)
Reduced Probe Responses
x
x
x
x
x
x
x
x
x
x
SKT0002
SKT0003
Aa_nomap
SKT0006
Home_nomap
x
x
x
x
x
x
Xx_nomap
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
Private AP
Private AP
Private AP
Private AP
Jae Seung Lee, ETRI
May 2012

## Slide 11: Selection of the AP to Scan – Example (3/3)
Example 2: Exclusion List with substring – using substring type information
The user does not subscribe to KT but SKT
SKT0002
SKT0003
SKT0004
SKT0005
SKT0006
SKT0001
KT0002
KT0003
KT0004
KT0005
KT0003
KT0004
KT0005
VeriLAN
Hyatt_2
Hyatt_2
STA
SKT000x
SKT000z
SKT000y
Probe Request
(ExclusionList with substring)
Add substring KT and indicate
“starts with” in the substring type information
(SKT is not filtered in this example)
x
x
x
x
x
x
x
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
Aa_nomap
Home_nomap
x
Private AP
Private AP
x
Jae Seung Lee, ETRI
May 2012

## Slide 12: Exclusion List element
May Include SSID List element, BSSID List element, and MESHID List element
Optionally included in the Probe Request frame
Substrings can be used in SSID elements or MESHID elements
  Interpretation of the strings are indicated in the SubstringInfo field
  Several substring type can be indicated (substring starts with, ends with, or contains, and whether it is a substring or a full string)
Octets: 1 1 1 variable variable variable
Element ID | Length | SubstringInfo | SSID List | BSSID List | MESHID List
Jae Seung Lee, ETRI
May 2012

## Slide 13: Conclusion
Legacy active scanning can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
In this proposal:
  Exclusion List is added to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response frame
  Use of substring in the Exclusion List to indicate SSIDs or Mesh IDs
    helps to reduce the size of the Exclusion List
    Not necessary to include individual IDs in the Exclusion List
    Provides flexible substring matching
   helps to reduce the unnecessary exchange of Probe Request frame thus increasing the efficiency of the active scanning
Jae Seung Lee, ETRI
May 2012

## Slide 14
Motion 1
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  STA may include Exclusion List in the Probe Request frame that indicates the STAs that should not transmit probe responses.
Moved:
Seconded:
Yes
No
Abstain

## Slide 15
Jae Seung Lee, ETRI
Slide 15
Motion 2
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  Substrings of SSIDs or Mesh IDs can be used in the Exclusion List to indicate the STAs that should not transmit probe responses.
Moved:
Seconded:
Yes
No
Abstain

## Slide 16
References
11-12/0059r1 Selection of the AP for Scanning
11-12/0060r0 Text for Selection of the AP for Scanning
  11-12/0263r2 Spec Framework Proposal: Selection of the AP for Scanning