## Slide 1: Selective transmission of the Probe Response for 11ai Spec Framework
Date: 2012-05-04

## Slide 2: Abstract
In active scanning, Probe Response can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
We propose the selective transmission of the Probe Response frame to reduce the unnecessary Probe Response frame
Approach:
  Filter the Probe Request by the responding STAs based on Preferences and/or Capabilities of the STA that has sent the Probe Request frame
    can reduce the traffic caused by Probe Response frames
    helps the selection of appropriate AP to be associated
Jae Seung Lee, ETRI

## Slide 3: Background
This contribution is based on the following documents that have been presented at the previous IEEE 802.11 meeting
  11-12/265r7 Spec Framework Proposal – Selective transmission of the Probe Response
  11-12/0063r1 Selective transmission of the Probe Response
  11-12/0064r0 Text for Selective transmission of the Probe Response
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
Proposed Spec Framework text is included in the Motion section at the end of this contribution
Jae Seung Lee, ETRI

## Slide 4: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI

## Slide 5: Selective Probe Response - Background
STAs respond to the Probe Request even if the requesting STA cannot or will not associate with the responding STAs
  Requesting STA cannot be associated due to the lack of its capability
  Requesting STA will not associate due to its preference of the STA
    The STA wants or does not want to use certain features, or requires certain capabilities of the responding STA
  Requesting STA cannot be associated due to the responding STA’s operating condition
   Sending Probe Response to such STAs is not necessary
Jae Seung Lee, ETRI

## Slide 6: Active Scanning - Problem
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
AP 3-1
AP 3-2
AP 3-3
AP 3-…
AP 3-n
AP 5-1
AP 5-2
AP 5-3
AP 5-…
AP 5-n
Probe Request on channel 1 (broadcast, wildcard SSID)
Channel 1
Channel 2
(idle)
Probe Request on channel 3 (broadcast, wildcard SSID)
Probe Request on channel 5 (broadcast, wildcard SSID)
Probe Request on channel 2 (broadcast, wildcard SSID)
Probe Request on channel 4 (broadcast, wildcard SSID)
Probe Request on channel n (broadcast, wildcard SSID)
Channel 3
Channel 5
Channel 4
(idle)
Channel n
Probe Response
.
.
.
Probe Response
.
.
.
Probe Response
.
.
.
Sequential
Scanning
of all
Channels
Jae Seung Lee, ETRI
APs respond to the Probe Request
although the STA cannot associate with
some of the APs

## Slide 7: Selective Transmission – Approach (1/2)
Filtering Information including preferences and/or capabilities of the STA is included in the Probe Request frame
  STA’s capability information such as security capability is included in the Probe Request frame
  STA’s preference information such as its security processing requirements, and/or its required AP’s capabilities is included in the Probe Request frame
Jae Seung Lee, ETRI

## Slide 8: Selective Transmission – Approach (2/2)
The Responding STAs can check the preferences and/or capabilities of the STA that transmitted the Probe Request
  If the preferences of the requesting STA is not acceptable by the responding STAs
  If the capabilities of the requesting STAs is not acceptable by the responding STAs
  If the responding STAs cannot accept the STA because of its current
  condition (e.g., high Load)
  The responding STAs do not transmit Probe Response frame
AP Channel Report element received in the probe responses is used to help the selection of the next channel to be scanned during active scanning
Jae Seung Lee, ETRI

## Slide 9: Selective Probe Response – Example (1/2)
Jae Seung Lee, ETRI
Example: Using existing active scanning method
The requesting STA is a VHT STA and only wants to associate with a VHT AP
The STA requires management frame protection
STA
Probe Request
(Broadcast)
Receives Probe Responses
although the STA cannot,
or will not associate with the APs
.
.
.
STA41
(non-HT, no security)
STA11
(HT, No Security)
STA 28
(non-HT,
no security)
STA05
(VHT, Security,
MFPC=1,MFPR=1)
STA09
(VHT, No Security)
STA07
(HT, Security,
MFPC=1,MFPR=1)
STA40
(VHT, Security,
MFPC=0, MFPR=0)
STA29
(VHT, Security,
MFPC=1,MFPR=1)
STA03
(VHT, no security)
High Load!
STA39
(VHT, Security,
MFPC=1,MFPR=1)

## Slide 10: Selective Probe Response – Example (2/2)
Jae Seung Lee, ETRI
Example: Using FilterInfo in Probe Request
The requesting STA is a VHT STA and only wants to associate with a VHT AP
The STA requires management frame protection
STA41
(non-HT, no security)
STA
Probe Request (Broadcast)
Reduced Probe Responses!
STA11
(HT, No Security)
STA 28
(non-HT,
no security)
STA05
(VHT, Security,
MFPC=1,MFPR=1)
STA09
(VHT, No Security)
STA07
(HT, Security,
MFPC=1,MFPR=1)
STA40
(VHT, Security,
MFPC=0, MFPR=0)
STA29
(VHT, Security,
MFPC=1,MFPR=1)
STA03
(VHT, no security)
High Load!
x
x
x
x
x
x
x
x
O
O
Require VHT, Require Security,
MFPC=1, MFPR=1
(in the FilterInfo)
STA39
(VHT, Security,
MFPC=1,MFPR=1)

## Slide 11: Preference and/or Capability based Filtering
FilterInfo element is added to the Probe Request frame
  Specifies options required for Probe Request filtering by the responder of the probe request based on the preferences and/or capabilities of the requesting STAs
Jae Seung Lee, ETRI
Slide 11
Element ID | Length | AP Preference | STA security capability element (or fields) | Other TBD capability/preferences elements
Octets: 1 1 2 variable variable

## Slide 12: AP Preference - Example
Bits: 1 1 1 1 1 11
Require Security | Require No Security | Require HT | Require VHT | Require non-HT | Reserved
Specifies the preferences of the requesting STAs including
    STA’s security processing requirement
    STA’s required AP’s capabilities
    Other TBD subfields
Jae Seung Lee, ETRI

## Slide 13: STA’s capability information
STA security capability element specifies the security capabilities of the requesting STAs
    RSN IE or RSN Capabilities field in RSN IE (2 octets) may be used as a security capability element
    Many elements that specifies STA’s capabilities are already included in the current Probe Request frame  can also be used to check the capabilities of the requesting STA
Jae Seung Lee, ETRI

## Slide 14: Selective Scanning
In current 802.11 Spec, AP Channel Report element is included in Probe Response Frame
  AP Channel Report element contains a list of channels in an operating class where a STA is likely to find an AP, excluding the AP transmitting the AP Channel Report (From 802.11 Revmb)
   can help to perform selective channel scanning
AP Channel Report element included in the most recently received Probe Response may be used to select the next channel to be scanned during active scanning
  If AP Channel Report element is included in the received probe responses, then a channel in the ChannelList that is also included in the AP Channel Report element that is not scanned yet may be selected as the next channel to be scanned during active scanning
Jae Seung Lee, ETRI

## Slide 15: Selective Probe Response & Selective Scan
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
AP 3-1
AP 3-2
AP 3-3
AP 3-…
AP 3-n
AP 5-1
AP 5-2
AP 5-3
AP 5-…
AP 5-n
Probe Request on channel 1
Channel 1
Probe Request on channel 3
Probe Request on channel
Channel 6
Channel 11
Probe Response
Probe Response
Probe Response
Probe Response
No response
Check the Preference and Capability of the
requesting STA in the Probe Response
Selective Scanning
Of the Channel
Jae Seung Lee, ETRI

## Slide 16: Conclusion
We proposed the selective transmission of the Probe Response frame to reduce the unnecessary Probe Response frame
  Responding STAs Filter the Probe Request using preferences and/or capabilities of the requesting STA
Selective transmission of the probe response helps to reduce the traffic caused by Probe Response frames
It helps to select appropriate AP to be associated with in advance
Selective Scanning of the channels based on the channel information can reduce the scanning time
Jae Seung Lee, ETRI

## Slide 17
Motion 1
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  Non-AP STA may include its preferences and/or capabilities information in the Probe Request frame. If the preferences and/or capabilities of the STA are not acceptable by the responding STA, then the responding STA may not transmit Probe Response.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 18
Slide 18
Slide 18
Motion 2
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  If the non-AP STA that has sent the Probe Request is not acceptable by the responding STA because of the responding STA’s current operating condition, then the responding STA may not transmit Probe Response.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 19
Slide 19
Slide 19
Motion 3
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  Non-AP STA may include its security processing requirements and/or security capability in the Probe Request frame for Probe Request filtering.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 20
Slide 20
Motion 4
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  Non-AP STA may include its required AP’s capabilities in the Probe Request frame for Probe Request filtering.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 21
Slide 21
Slide 21
Motion 5
Update the spec framework document with the following text under subsection “6.1 Active Scanning”:
  AP Channel Report element included in the most recently received Probe Response may be used to select the next channel to be scanned during active scanning.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 22
References
11-12/0063r1 Selective transmission of the Probe Response
11-12/0064r0 Text for Selective transmission of the Probe Response
  11-12/265r7 Spec Framework Proposal – Selective transmission of the Probe Response
Jae Seung Lee, ETRI