## Slide 1: Scalable Authentication
Date: 2012-5-6
Authors:

## Slide 2: Overview
This submission looks requirements for security mechanisms based on requirements for scalability:
  Scaling to very large number of devices
  Scaling to low power long battery life devices
  Scaling to minimize or distribute the requirements of authentication services
These requirements were first presented in 802.11ah as 11-12-0585-00-00ah-ieee-802-11ah-and-security

## Slide 3: Additional Use Case of Interest
Use Case : Smart objects, kiosks, ATM machines, sensors, meters, location markers [2]
  Of particular interest since the traffic has characteristics that are not typical of most wireless LANS
  [2] - 11/457r0, 11/17r5, 11/253, 11/241r0

## Slide 4: Characteristics of Use Case
Devices in network may be procured from many vendors.
The number of STAs/APs may be very large.
Devices may have very long lifetime (20-30 years).
Devices may be mobile over their lifetime, be recycled or replaced, or be redeployed.
Installed devices may operate in spread-out locations, without physical protection or oversight by personnel.

## Slide 5: Characteristics of Use Case
Traffic is periodic with a small amount of data.
Power consumption is a large concern. So sleep times will be larger than normal.
The number of STAs per AP will be large and go beyond the current maximum AID range of 2007.
Always-on connectivity to remote devices may not be guaranteed.
Full Internet connectivity and access to remote AAA may not be guarenteed.

## Slide 6: Implications of Use Case to Security
Power consumption is a large concern. Need to try and keep security setup traffic to not be much larger than data.
  Implication: Initial security establishment should be efficient in its use of the number of transmissions.
  Implication: It will be desirable for security establishment to be valid across long client sleep time.
  Implication: Initial security establishment should avoid involvement of remote network devices with unpredictable response times during the protocol.
  Implication: Initial security establishment should avoid involvement of an on-line and remote network device.

## Slide 7: Implications of Use Case to Security (2)
APs will be concerned with the amount of memory required per STA. This is because there can be many STAs per AP. Also it is expected that many clients will desire traffic to be buffered over long sleep times.
  Implication: Should look for ways to minimize memory needs on an AP.

## Slide 8: Use Case Implications to Security
Configuration and maintenance cost is a large concern. So devices should be easy to install, without need for shielded set-up, pre-planning, or expensive personnel.
Implication: Initial security establishment should minimize assumptions on coordination of security capabilities between devices (since this would reduce flexibility of deployment).
Implication: Initial security establishment should not reduce flexibility of (re)deployment over lifetime.
Implication: Initial security establishment should be carried out in operational network (“hot swap”).

## Slide 9: Use Case Implications to Security cont.
STAs and APs will be concerned about computational cost of initial security establishment. Ill behaved devices may cause excessive calculations and consume energy.
Implication: Should look for ways to increase efficiency of security calculations, in terms time latency and energy cost.

## Slide 10: Security and Specification Framework
Straw Poll The draft specification shall define authentication mechanisms that may be used to avoid involvement of an on-line and remote network services.
Results: (15 yes/8 no /21 more info)