## Slide 1: IEEE 802.11ah and Security
Date: 2012-5-6
Authors:

## Slide 2: Activity in TGah
This submission looks at P802.11ah use cases and requirements and how they are related to security.

## Slide 3: Use Cases
The approved TGah use cases are documented in [1] 11/457r0. There are 3 main use cases and they are,
  Use Case 1 : Sensors and meters
  Use Case 2 : Backhaul Sensor and meter data
  Use Case 3 : Extended range Wi-Fi
Use case 1 is of particular interest since this category has traffic characteristics that is not typical of wireless LANs.
Use cases 1 and 2 may introduce traffic between devices that are not all owned or managed by the same entity.
  Consumers access to meter data is different than utility access to meter data.

## Slide 4: Use Case 1: Sensors and Meters
1a: 11/17r5, slide 7 Smart Grid - Meter to Pole
1c: 11/253 Environ./Agri. Monitoring
1d: 11/260r1, slide 4 Industrial Process Sensors
1e: 11/17r5, slide 17 Healthcare
1f: 11/241r0, slide 3 Healthcare
1g: 11/241r0, slide 5 Home/Building Automation
1h: 11/242r0, slide 2 Home Sensors

## Slide 5: Characteristics of Use Case 1
Traffic is periodic with a small amount of data.
Power consumption is a large concern. So sleep times will be larger than normal.
The number of STAs per AP will be large and go beyond 2007.
Always-on connectivity to remote devices may not be guaranteed.

## Slide 6: Use Case 1 Implications to Security
Power consumption is a large concern. Also want to avoid security traffic to be much larger than the data being transferred.
Implication: Initial security establishment should be efficient in its use of the number of transmissions.
Implication: It will be desirable for security establishment to be valid across long client sleep time.
Implication: Initial security establishment should avoid involvement of remote network devices with unpredictable response times during the protocol.
Implication: Initial security establishment should avoid involvement of an on-line and remote network device.

## Slide 7: Use Case 1 Implications to Security (cont.)
APs will be concerned with the amount of memory required per STA. This is because there can be many STAs per AP. Also it is expected that many clients will desire traffic to be buffered over long sleep times.
Implication: Should look for ways to minimize memory needs on an AP.

## Slide 8: Characteristics of Use Cases 1 and 2
Devices in network may be procured from many vendors.
The number of STAs/APs may be very large.
Devices may have very long lifetime (20-30 years).
Devices may be mobile over their lifetime, be recycled or replaced, or be redeployed.
Installed devices may operate in spread-out locations, without physical protection or oversight by personnel.

## Slide 9: Use Cases 1 and 2 Implications to Security
Configuration and maintenance cost is a large concern. So devices should be easy to install, without need for shielded set-up, pre-planning, or expensive personnel.
Implication: Initial security establishment should minimize assumptions on coordination of security capabilities between devices (since this would reduce flexibility of deployment).
Implication: Initial security establishment should not reduce flexibility of (re)deployment over lifetime.
Implication: Initial security establishment should be carried out in operational network (“hot swap”).

## Slide 10: Use Cases 1 and 2 Implications to Security cont.
STAs and APs will be concerned about computational cost of initial security establishment. Ill behaved devices may cause excessive calculations and consume energy.
Implication: Should look for ways to increase efficiency of security calculations, in terms time latency and energy cost.

## Slide 11: References
[1] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document.pptx
[2] 11-11-0905-05-00ah-tgah-functional-requirements-and-evaluation-methodology.doc