## Slide 1: SIG Field 4-Bit CRC
Date: 2012-05-15
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Abstract
This presentation relates to the CRC used in SIG Fields.

## Slide 5: Overview
May 2012
Current 11ah spec framework uses 4-bit CRC in 1MHz SIG and 2MHz SIG(A), and uses 8-bit CRC in 2MHz SIGB (long preamble).
Propose to use the 4 LSB of the 8-bit CRC as the 4-bit CRC in SIG fields.
  Simulations show strong enough false positive probability compared with the SIG field decoding error rate (refer to next slide).
  Easy for implementation for “multi-clock” devices, and for devices that support both short and long preambles.

## Slide 6: CRC Simulation
1MHz SIG Field, 6 symbols, modulated using MCS0-Rep2.
4-bit CRC uses 4 LSB of 8-bit CRC, similar scheme is applied for 6-bit CRC.

## Slide 7: Discussions
Results in the previous slide show that the false positive prob. of 1MHz SIG when using 4-bit CRC is approximately one magnitude lower than the error rate of 1MHz SIG field.
False positive happens at such a low SNR where most likely packet detection and timing synchronization will fail anyway.

## Slide 8: Straw Poll-1
Do you agree to use the 4 LSB of the 11n HTSIG field 8-bit CRC for the 4-bit CRC in 11ah 2MHz and 1MHz SIG(A) fields, and use the same 11n HTSIG field 8-bit CRC in SIGB field of the >=2MHz long preamble?

## Slide 9: Motion-1
Move to use the 4 LSB of the 11n HTSIG field 8-bit CRC for the 4-bit CRC in 11ah 2MHz and 1MHz SIG(A) fields, and use the same 11n HTSIG field 8-bit CRC in SIGB field of the >=2MHz long preamble?