## Slide 1: TGah Spec Development Process
Date: 2012-05-14
Authors:

## Slide 2
Authors:

## Slide 3: Introduction
In the last TGah ad hoc meeting, the group started to discuss on how to develop a 11ah spec
802.11ah is inheriting both PHY and MAC from 802.11ac heavily, but 802.11ac spec is not completed yet
The group needs to find the cleanest/easiest way to develop an 802.11ah spec that incorporates many parts of a draft 802.11ac spec
This presentation includes
  TGah Spec development process in IEEE

## Slide 4: PHY
For 802.11ah PHY, create a separate new PHY clause
  E.g. Clause 2x: Sub 1 GHz (S1G) PHY specification
    Clause number should be chosen not to conflict with 11af
The new 11ah PHY clause contains delta between 11ah and 11ac PHYs
Incorporate necessary parts of 802.11ac PHY/MAC by reference
  Just point to sections of the 802.11ac draft spec that the new 802.11ah spec needs to include
    This way, 802.11ah STA doesn’t support Clause 22 (VHT PHY) directly
  Reference should be based on the latest 802.11ac draft at the time of writing a 802.11ah draft spec
  The editor/members of TGah should track changes in a newer draft spec of 802.11ac, which may affect/break the current draft spec of 802.11ah that refers to the older version of 802.11ac draft spec

## Slide 5: PHY (cont.)
TGac is not designed to be easily re-clockable
  Difficult to reuse terminology from VHT PHY that is specific to the “non-clock reduced” channel widths
    E.g.: secondary40, secondary80, 20 MHz, 40 MHz, 80 MHz …
  Possible solutions:
    Start the 11ah PHY clause with an explanation of the down-clocking and then simply refer to 11ac PHY with the understanding that every mentioning of the 20/40/80/160 in 11ac is used with the appropriate down-clocked BW
      E.g. secondary40 is treated as secondary4 when used in 11ah
    Have a table that shows all the mappings between the parameters in 11ac and 11ah
      secondary40  secondary4,
      secondary80  secondary8,
      20MHz/40MHz/80MHz/160MHz  2MHz/4MHz/8MHz/16MHz

## Slide 6: MAC
Make necessary additions/changes to the MAC clauses for 11ah PHY and new MAC features
  E.g. Clause 8: Frame formats, Clause 9: MAC sublayer functional description , Clause 10: MLME

## Slide 7: 802.11ah Specification Development
Draft 11ah spec
11ah Spec Framework
Separate new 802.11ah PHY clause (e.g. Clause 23 or 24)
PHY sections
MAC sections
Existing MAC related clauses (e.g. Clause 8,9,10)
Clause 8: Frame formats
Clause 9: MAC sublayer functional description
Clause 10: MLME
VHT PHY clause (Clause 22)
Reference to
802.11ac PHY/MAC
text
text
text
text
text
text
text
text
text
text
text
text
text
text
text
Reference to VHT PHY Section 22.x.x
Create draft texts for PHY/MAC clauses in PHY/MAC ad hoc groups
Section 22.x.x

## Slide 8: Straw Poll
Do you support the 802.11ah specification development process shown in Slide 4-6 in TGah?
  Y/N/A: