## Slide 1: Uplink Channel Access
Date: 2012-05-14
Authors:

## Slide 2
Authors:

## Slide 3: Introduction
11ah use case includes a large outdoor network [1]
  For an outdoor smart grid network, the number of STAs can be 2007+
  TIM element may cover few hundreds to few thousands STAs
  Bits set to one in the TIM element may trigger too many PS-Poll/trigger frame transmissions from the STAs within a short period of time
  Many stations at the edge of the coverage area could be hidden from each other for uplink transmissions due to a much higher path loss between STA-STA than AP-STA [2]
This presentation proposes a uplink channel access scheme using information from an AP (e.g. TIM information) to mitigate the hidden node problem

## Slide 4: TIM Triggered Hidden Node Problem
Too many bits set in the TIM element may trigger too many PS-Poll/trigger frame transmissions right after the beacon frame within a short period of time
  Increase collisions between the hidden nodes
STA1
STA2
AP
STA2’s transmission range
STA1’s transmission range
TIM
(n bits set to 1)
Beacon interval
STA1
STA2
STAn
…
PS-Poll/trigger frame
n transmissions within a short period of time
(e.g. few mS)

## Slide 5: Basic Concept
Utilize information from an AP (e.g. TIM element) to spread uplink transmissions over a period of time so that the uplink transmissions are not overlapping with each other
TIM
(n bits set to 1)
Beacon interval
STA1
STA2
STAn
…
PS-Poll/trigger frame
Spread n transmissions over a much longer time period
…

## Slide 6: Option 1
Randomly spread uplink transmission over a period of time
  The total number of time slots, N, may be determined based on the number of paged (and unpaged) stations, n, indicated in the received TIM (e.g. N = f (n))
  The time slot duration T may be chosen to be large enough to complete PS-Poll/trigger+SIFS+DATA+SIFS+ACK (e.g. 20 ~ 40 mS)
  A STA randomly chooses a time slot to start its uplink channel access
    If two or more hidden STAs choose the same time slot, they may collide
TIM (n paged STAs)
Total N time slots, each time slot duration = T
STA 10
STA 2,8 (may collide)
STA 3
STA 7
STA 5
STA 1
STA 4
STA 9
STA 6
T

## Slide 7: Option 2
Deterministically spread uplink transmission over a period of time
  The total number of time slots, N, may be determined based on the number of paged stations, n, indicated in the received TIM (e.g. N = n)
  The time slot duration T may be chosen to be large enough to complete PS-Poll/trigger+SIFS+DATA+SIFS+ACK (e.g. 20 ~ 40 mS)
  AP assigns a time slot for a STA
    Example: AID bit position of TIM may be used to determine the assigned time slot
  Each STA starts to access the channel at the assigned time slot following EDCA
STA 1, 2, 3, 4, 5, 6, 7, 8, 9, 10
Total N time slots, each time slot duration = T
…
TIM bitmap
1
1
1
0
1
0
0
1
STA10
STA1

## Slide 8: Simulation Setup 1
1 AP and 10 STAs
  STAs transmit Data frames
  AP replies with Ack frame
Parameters
  PHY rate = 600Kbps, packet size = 260 bytes
  Packet Tx time = ~3.7msec
  Use AC_VO, max number of retransmissions = 11
Uplink channel access schemes
  CW32 20mS Slot: each STA randomly chooses a 20mS time slot out of 32 time slots for uplink channel access
  CW64 20mS Slot: each STA randomly chooses a 20mS time slot out of 64 time slots for uplink channel access
  Deterministic 20mS Slot: a 20mS time slot for uplink channel access is determined by each STA’s AID bit position of the TIM bitmap
  Deterministic 40mS Slot: a 40mS time slot for uplink channel access is determined by each STA’s AID bit position of the TIM bitmap
STA1
AP
STA2
STA3
STA4
STA5
STA6
STA7
STA8
STA9
STA10
STA5,6,7 are hidden to STA1 for ~55% of time
STA4 is hidden from STA1 for ~30% of time
STA3 is hidden from STA1 for ~10% of time

## Slide 9: Uplink Channel Access Schemes - Examples
TIM
TIM
32 time slots, each time slot duration = 20 mS
64 time slots, each time slot duration = 20mS
TIM
10 time slots, each time slot duration = 20mS
TIM
TIM
Each STA starts to access channel at time t chosen from ~Uniform(5mS)
STA 1
2
3
4
5
6
7
8
9
10
STA 1, 2, 3, 4, 5, 6, 7, 8, 9, 10
STA 10
STA 2
STA 3
STA 7
STA 5
STA 1
STA 4
STA 9
STA 6
STA 8
STA 10
STA 2,8 (may collide)
STA 3
STA 7
STA 5
STA 1
STA 4
STA 9
STA 6
STA 1~10 uplink channel access
…
TIM bitmap
1
1
1
0
1
0
0
1
Uniform(5mS)
CW32 20mS Slot
CW64 20mS Slot
Deterministic (D)
20mS Slot
Deterministic (D)
40mS Slot
10 time slots, each time slot duration = 40mS

## Slide 10: Comparisons 1 (AC_VO)
Average number of retransmissions
Average Tx delay (=active duration) = medium access delay + time until successful packet transmission
STA active time reduced by 94%
99% less retransmissions
CWmin[AC_VO]=3, CWmax[AC_VO]=7
Effect of hidden nodes
When hidden nodes are present in the network, spreading the uplink channel accesses over a much longer period of time significantly reduces
  the transmission delay by 94%* and
  the retransmissions by 99%*.
  *) D 20mS slot gain over U(5mS)
Effect of hidden nodes

## Slide 11: Uplink Channel Access using TIM Information -OBSS Example
OBSS case
  If a STA’s uplink channel access is delayed to the next time slot due to OBSS transmissions, the STA may contend with the other station in the next time slot.
AID1
3
4
5
6
7
8
9
10
11
12
13
14
15
16
TUT of STA with AID6
TIM bitmap information of
AID1~16
…
1
1
1
0
1
0
0
1
PS-Poll or
Null-Data or
Data frame
Slot Time T
(e.g. 20-40mS)
t0
Un-paged STAs may also have uplink
data to transmit
6
OBSS transmissions
2
2

## Slide 12: OBSS Scenarios Simulation Setup 2
1 AP and 10 STAs + 2 STAs (OBSS)
  10 STAs transmit Data frames, AP replies with Ack frame
    AC_VO
  OBSS: STA12  STA11
    AC_BE
Parameters
  PHY rate = 600Kbps, packet size = 260 bytes
  Packet Tx time = ~3.7msec
  Max number of retransmissions = 11
  OBSS traffic:
    PHY rate=600Kbps
    Packet size=1500 bytes, Tx time~20mS
    Packet inter-arrival time:
      Uniform(.1S)  occupies ~40% channel
      Uniform(.2S)  occupies ~20% channel
      Full buffered traffic
STA1
AP
STA2
STA3
STA4
STA5
STA6
STA7
STA8
STA9
STA10
STA5,6,7 are hidden to STA1 for ~55% of time
STA4 is hidden from STA1 for ~30% of time
STA3 is hidden from STA1 for ~10% of time
STA12
STA11

## Slide 13: OBSS Scenarios 2 - Comparisons
Average number of retransmissions
Average Tx delay (=active duration) = medium access delay + time until successful packet transmission
STA active time reduced by 78 ~91%
92-98%% less
retransmissions
Observation
  From the comparison between U(5mS) without OBSS and U(5mS) with OBSS shows that contentions between the hidden nodes are the major contributor for the large transmission delay and retransmissions.
  Spreading the uplink channel accesses over a longer period of time reduces both the transmission delay and the number of retransmissions significantly even when there is OBSS traffic.
Effect of OBSS traffic

## Slide 14: OBSS Scenario Setup 3 – Hidden Node
1 AP and 10 STAs + 2 STAs (OBSS)
  10 STAs transmit Data frames, AP replies with Ack frame
    AC_VO
  OBSS: STA12  STA11
    AC_BE
Parameters
  PHY rate = 600Kbps, packet size = 260 bytes
  Packet Tx time = ~3.7msec
  Max number of retransmissions = 11
  OBSS traffic:
    PHY rate=600Kbps
    Packet size=1500 bytes, Tx time~20mS
    Packet inter-arrival time:
      Full buffered traffic
STA1
AP
STA2
STA3
STA4
STA5
STA6
STA7
STA8
STA9
STA10
STA5,6,7 are hidden to STA1 for ~55% of time
STA4 is hidden from STA1 for ~30% of time
STA3 is hidden from STA1 for ~10% of time
STA12
STA11
Full buffered
traffic
interference
BSS1
BSS2

## Slide 15: OBSS Scenarios 3 - Comparisons
Observation
  STA1, STA2, STA3, STA10 are hidden from STA12
  The hidden nodes (STA1, STA2, STA3, STA10) suffer from very high packet drop rate (45-62%)
  Even in the OBSS with a hidden node with full buffered traffic, spreading the uplink channel accesses over a longer period of time reduces both the transmission delay and the number of retransmissions significantly.
Tx delay, retransmissions, and packet drop rate
  STA1, STA2, STA3, STA10 are hidden from STA12

## Slide 16: Summary
11ah use case includes a large outdoor network
  Many stations at the edge of the coverage area could be hidden from each other
    The 11ah channel model [2] shows that the channel between STA-STA experiences a higher path loss than the channel between AP-STA.
  Bits set in the TIM element may trigger collisions between the hidden nodes
  Uplink data transmissions from the hidden nodes within a short period of time (e.g. ~ few mS) also result in collisions at the AP
When hidden nodes are present in the network, spreading the uplink channel accesses over a period of time so that the uplink transmissions are not overlapped with each other significantly reduces
  the transmission delay (STA active time) by 94%* and
  the number of retransmissions by 99%*.
  *) Deterministic 20mS time slot gain over Uniform(5mS)
We propose to utilize the information from the AP to spread out the uplink transmissions (e.g. PS-Poll/Data) over a period of time to mitigate the hidden node problem
  The exact definition of the information from the AP is TBD (e.g. TIM element)
  The definition of the period of time is TBD
    E.g. DTIM interval or (the number of STAs in a TIM bitmap) x (the slot time duration) may be used

## Slide 17: Straw Poll 1
Do you support the concept of utilizing information from an AP to spread out uplink transmissions over a period of time to mitigate the hidden node problem?
  Y:
  N:
  A:

## Slide 18: Motion 1
Move to accept the concept of utilizing information from an AP to spread out uplink transmissions over a period of time to mitigate the hidden node problem in the TGah Specification Framework document.
  Y:
  N:
  A:

## Slide 19: Reference
[1] Potential compromise of 802.11ah use case document, 802.11-11/457r0
[2] TGah Channel Model, 802.11-11/968r3

## Slide 20: Backup

## Slide 21: Comparisons 1 (AC_BE)
CWmin[AC_BE]=15, CWmax[AC_BE]=1023
Average number of retransmissions
Average Tx delay (= active duration) = medium access delay + time until successful packet transmission
STA active time
reduced by 93%
99% less
retransmissions