## Slide 1: Non-TIM Stations in 11ah
Name | Affiliations | Address | Phone | email
George Calcev | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 x 310 | George.Calcev@huawei.com
Bin Chen | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 | Bin.Chen@huawei.com
Lin Cai | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 x 379 | Lin.Cai@huawei.com
Minyoung Park | Intel Corp. |  |  | minyoung.park@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel Corp. |  |  | emily.h.qi@intel.com
Thomas Kenney | Intel Corp. |  |  | 
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Raja Banerjea | Marvell |  |  | 
Authors:

## Slide 2
Name | Affiliations | Address | Phone | email
Yongho Seok | LG Electronics |  |  | 
Seunghee Han | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jinsam Kwak | LG Electronics |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Authors:

## Slide 3
Name | Affiliations | Address | Phone | email
Matthew Fischer | Broadcom |  |  | 
Eric Wong | Broadcom |  |  | 
Simone Merlin | Qualcomm |  |  | 
Zhi Quan | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI |  |  | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Heejung Yu | ETRI |  |  | heejung@etri.re.kr
Hyoung Jin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Authors:

## Slide 4: Cheap Low Duty Cycle Sensors
A typical specification (from an actual product in 915MHz [2]):
      “The X Sensor monitors temperature, relative humidity and wood moisture content. It combines environmental sensors, wireless transceiver, microcontroller, and battery into a compact enclosure designed to be embedded into structures at common points of moisture failure. Sensors are small enough to be mounted anywhere and their ultra long (15+ year typical) battery life mean the sensors can be mounted in areas that are inaccessible after construction is complete. …Sensors are programmed to periodically wakeup from an ultra low power sleep state, take measurements, and open a communication session with the gateway such that the gateway can read the measurement data out of the sensor. The Gateway can also update the Sensor’s time of day, read out the Sensor’s stored GPS position, and even perform an in-service firmware upgrade of the Sensor’s operating firmware.”
There is a category of cheap sensors that wake up at very low duty cycle
These sensors receive DL traffic very seldom ( e.g. time of day or some software update), which does not require immediate delivery

## Slide 5: Reducing TIM signaling overhead
TIM signaling overhead can be an issue in large sensor networks due to the low rate of beacon transmission [1]
For instance 8000 bits TIM at 1Mbit/s would require almost 8ms
We propose to reduce the number of entries in TIM signaling
SOLUTION:
  Some sensors (cheap, very low duty cycle) do not use TIM signaling
  These sensors do not check the TIM map and AP does not provide TIM info for them
  These sensors request the DL data from the AP when they wake up

## Slide 6: Sensor DL traffic
They can get the DL data via the PS-Poll mechanism already specified in the standard
These sensors will not require a TIM signaling for DL traffic
The AP needs to be aware about their existence and store the DL traffic until they requested it
The AP needs to be aware that these sensors will not require TIM signaling and therefore avoid unnecessary signaling
The sensor could inform their DL preference at the association, or via management frames

## Slide 7: Straw Poll 1
Do you support to add the following text to the framework document? “11ah stations can choose to not have a TIM entry for the DL traffic signaling. For these stations, the AP will store the DL data and deliver it when the STA requests it.”
Yes:
No:
Abstain:

## Slide 8: Straw Poll 2
Do you support to add the following text to the framework document? “11ah stations inform AP if they do not need a TIM entry for the DL signaling traffic during the association process.”
Yes:
No:
Abstain:

## Slide 9: References
[1] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology document
[2] OmniSense S-900-1 Wireless Sensor Product Brief

## Slide 10: Motion 1
Move to add the following text to the framework document. “11ah stations can choose not to have a TIM entry for the DL traffic signaling. For these stations, the AP will store the DL data and deliver it when the STA requests it.”
Yes:
No:
Abstain:

## Slide 11: Motion 2
Move to add the following text to the framework document. “11ah stations shall inform AP if they do not need a TIM entry for the DL signaling traffic during the association process.”
Yes:
No:
Abstain: