## Slide 1: Serivice Type Indication in Association
Date: 2012-05-xx
Authors:
Name | Affiliations | Address | Phone | email
Wu Tianyu | Huawei |  |  | wutianyu@huawei.com
Li Yunbo | Huawei |  |  | liyunbo@huawei.com
David Xun Yang | Huawei |  |  | David.yangxun@huawei.com
Osama Aboul-Magd | Huawei |  |  | Osama.Aboulmagd@huawei.com
Yunsong Yang | Huawei |  |  | yangyunsong@huawei.com
George Calcev | Huawei |  |  | George.calcev@huawei.com
Yongho Seok | LG Electronics |  |  | 
Seunghee Han | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jinsam Kwak | LG Electronics |  |  | 
Matthew Fischer | Broadcom |  |  | 
Eric Wong | Broadcom |  |  | 
Simone Merlin | Qualcomm |  |  | 
Zhi Quan | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 

## Slide 2
Authors:
Name | Affiliations | Address | Phone | email
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Raja Banerjea | Marvell |  |  | 
Minyoung Park | Intel Corp. |  |  | 
Tom Tetzlaff | Intel Corp. |  |  | 
Emily Qi | Intel Corp. |  |  | 
Thomas Kenney | Intel Corp. |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Sun, Bo | ZTE |  |  | 
Lv, Kaiying | ZTE |  |  | 
Huai-Rong Shao | Samsung |  |  | 
Chiu Ngo | Samsung |  |  | 
Minho Cheong | ETRI |  |  | 
Jae Seung Lee | ETRI |  |  | 
Heejung Yu | ETRI |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Chittabrara Ghosh | Nokia |  |  | 
Esa Tumaala | Nokia |  |  | 

## Slide 3: Motivation
Different Service type has different requirements
AP can optimize the system parameters based on the service type
 | Sensor | Offloading
Duty Circle | Long | Short
Packet Size | Short | Normal
Power save Req | Higher | Lower
DL/UL | UL dominated | More DL traffic
Periodicity | Mostly Periodic | Mostly bursty
Parameters
Service Type

## Slide 4: Parameter Optimization based on Service Type
AP can:
  Optimize the DTIM interval for STAs with different service type
    Assign a longer DTIM interval for sensors can enhance the power save performance
  Optimize the Max Idle Period for STAs with different service type
    Sensor STAs may need a longer Max Idle Period
  Assign appropriate AID for STAs with different service type
    If AIDs for sensor STAs with low duty circle are assigned contiguously, there is higher chance for the TIM to have long contiguous 0s.
    If AIDs for sensor STAs with same periodic duty circle are assigned contiguously, there is higher chance for the TIM to have long contiguous 1s.
    This may help TIM compression.

## Slide 5: Service Type indication during Association
STA provide service type information to the AP during association
Add the service type field in Association request frame as shown below:

## Slide 6: Example of Service Type Element
An example of the service type element can be:
  In the service Type byte, we can use a bitmap for the supported service types:
1 1 1

## Slide 7: Straw Poll
Do you support indicating service type during association?
  Y/N/A: