## Slide 1: Short CTS
Date: 2012-05-14
Authors:

## Slide 4: Short Ack
 | MCS | ACK ID | Reserved | CRC | Tail
Bits | 4 | TBD | TBD | 4 | 6 (TBD)
STF
LTF1
SIG
22 bits (1MHz)
34 bits (2MHz)
It is natural to use the same short Ack format [1] for short CTS also

## Slide 5: Short CTS SIG
Short CTS indication
  use a reserved MCS value different from the short Ack indication
CTS ID
Bandwidth
  indicate available bandwidth at receiver side (see next slide)
Duration
  if time unit = 40us, 10 bits can indicate 40.96ms
CRC – 4 bits
Tail – 6 bits (TBD)
other subfields TBD

## Slide 6: Bandwidth subfield
11ac bandwidth negotiation scheme can be used in 11ah also:
  RTS indicates the available bandwidth at the transmitter side
  CTS indicates the available bandwidth at the receiver side (within the bandwidth indicated by RTS)
  Subsequent transmissions within the TXOP cannot occupy a bandwidth wider than that indicated by CTS

## Slide 7: CTS ID (1)
Bit calculation
  1MHz: 36 bits – MCS (4 bits) – bandwidth (2-3 bits) – duration (9-10 bits) – CRC and tail (10 bits) = 9 – 11 bits
   2MHz: 48 bits – MCS (4 bits) – bandwidth (2-3 bits) – duration (9-10 bits) – CRC and tail (10 bits) = 21 – 23 bits
Is it ok to have a shorter CTS ID than Ack ID?
  Short CTS is sent less frequent than short Ack => the possibility of false CTS is extremely low
  A false short CTS may potentially cause some interference to the medium, but its impact is much less severe than a false short Ack

## Slide 8: CTS ID (2)
RTS/CTS
  CTS ID: Partial FCS and scramble seed information from the received RTS (same as Ack ID but with fewer bits)
CTS-to-Self
  CTS ID: partial TA of the transmitter

## Slide 9: Straw poll
Do you support to define a short CTS format as following with SIG field design TBD
STF
LTF1
SIG

## Slide 10: Reference
[1] 11-12-0324-02-00ah-short-ack