## Slide 1: Extended Sleep mode for battery powered STAs
Date: 2012-05-15
Authors:

## Slide 2
Introduction
Some Use Cases of 802.11ah only require the STAs to report back periodic data at very long intervals. This is especially true for battery powered devices that are expected to run for very long time without replacing the battery. Potential Use Case:
  Gas/Water Meters that only need to report the meter value weekly, bi-weekly or even monthly.
This presentation introduces possible mechanism to extend the WNM-Sleep Interval of battery powered STAs.

## Slide 3
Typical WSN Reporting Interval
Application | Reporting Interval
Volcano Monitoring | 30 ~ 60 seconds
Underwater Sensor Network | 10 minutes
Forest Fire Detection | 1 minutes
Air Pollution Monitor | < 10 seconds
Remote Environment/Habitat Monitoring | 20 minutes
Soil Temperature & Humidity | 15 minutes
Long term Structural Health monitoring | 1 day
Health Monitoring | 1 second
Gas Meter, Water Meter | Weekly, Bi-weekly, monthly
Typical reporting Interval for various applications:

## Slide 4
Background: WNM Sleep Mode
AP
STA
Association Request
Association Response
WNM Sleep Mode Request
WNM Sleep Mode Response
⁞
1) Max Idle Period negotiation:
STA indicates to the AP that it supports WNM-Sleep Mode by setting the WNM-Sleep Mode field to 1 in the Extended Capabilities IE in the Association Request Frame.
AP decides the Max Idle Period it can support based on the available resources and notifies the STA in the Association Response Frame.
2) WNM-Sleep Mode Setup:
STA requests permission to enter WNM-Sleep Mode and optionally also indicates the actual wake up time in the “WNM-Sleep Interval” field in the WNM-Sleep Mode Request frame if the STA wishes to receive group-addressed traffic indicated in the DTIM.
AP grants/denies permission to enter WNM-Sleep Mode.
WNM-Sleep mode enables a non-AP STA to signal to an AP that it will be sleeping for a specified length of time. This enables a non-AP STA to reduce power consumption and remain associated while the non-AP STA has no traffic to send to or receive from the AP.

## Slide 5
Prior Proposals
[11-12-0069-05] has introduced mechanism to address the first topic (Max Idle Period Negotiation).
With the proposed mechanism, the Max Idle Period can be extended to days and even months.
AP can support multiple Max Idle Periods extension to support multiple device categories.
This proposal addresses the second topic (WNM-Sleep Mode setup) and introduces mechanism to extend the WNM-Sleep Interval.

## Slide 6
WNM Sleep Mode Setup
The WNM-Sleep Interval field (16 bits) indicates to the AP how often a STA in WNM-Sleep Mode wakes up to receive Beacon frames, defined as the number of DTIM intervals.

## Slide 7
Motivation
Since the Beacon Interval and DTIM Interval are decided by the AP, there might be cases where even though the BSS Max Idle Period allocated to a STA is very long, the actual sleep period that a STA can request is restricted by WNM-Sleep Interval.
An Example:
If we assume a Beacon Interval of 100ms and
DTIM Interval = Beacon Interval = 100ms,
we can calculate that with 16 bits of WNM-Sleep Interval field, the maximum WNM-Sleep period that a STA can achieve is:
(216-1)*100ms = 6553.5 seconds = 1.82 hours

## Slide 8
Proposal: WNM-Sleep Interval Extension
Similar to Max Idle Period extension, WNM-Sleep Interval can be extended by using one or two bits to represent different types of units for WNM-Sleep Interval and the remaining bits for the actual value.
16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Value
Scaling
WNM-Sleep Interval
B1 | Unit
0 | D.I.
1 | 10 D.I.
B1B2 | Unit
00 | D.I.
01 | 10 D.I.
10 | 100 D.I.
11 | 1000 D.I.
Depending on its specific needs, a STA can choose the unit that enables it to achieve the desired Sleep Interval.
D.I. = DTIM Interval
The scaling factors illustrated above is for example only, and the actual values are T.B.D.

## Slide 9
Conclusion
By using different scaling factors of “WNM-Sleep Interval” for different STA types, we can extend the sleep duration of battery powered STAs.

## Slide 10
References
[1] 11-12-0069-02-00ah-consideration-on-max-idle-period-extension-for-11ah-power-save
[2] 11-12-0376-01-00ah-on-the-bss-max-idle-period
[3] 11-12-0069-05-00ah-consideration-on-max-idle-period-extension-for-11ah-power-save
[4] IEEE 802.11-2012

## Slide 11
Straw Poll 1
Do you agree that mechanisms must be considered to extend the WNM-Sleep Interval?
Y: N: A:

## Slide 12
Straw Poll 2
Do you support having different scaling factors for WNM-Sleep Interval as explained in slide #8, the actual scaling being TBD?
Y: N: A: