## Slide 1: Supplemental Information for HLCF
Date: 2012-05-17
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi Morioka | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@gmail4.trans-nt.com

## Slide 2: Abstract
This presentation shows some example sequenses of HLCF as a supplemental information of 11-12/273r9.

## Slide 3: DHCPv4
With Rapid Commit Option (RCO), DHCPv4 can complete IP layer configuration in 1 round-trip packet exchange.
DHCP
Client
DHCP
Server
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST
DHCPACK
DHCP
Client
DHCP
Server
DHCPDISCOVER w/RCO
DHCPACK w/RCO

## Slide 4: IPv6 Stateless Address Autoconfiguration
Host
Router
(Router Solicitation)
Router Advertisement
Neighbor Solicitation
(for DAD)
Duplicate Address Detection (DAD) is mandatory.
IPv6 Stateless Address Autoconfiguration can configure only IP address and default gateway.
It cannot configure other items such as DNS server addresses.

## Slide 5: DHCPv6
Duplicate Address Detection (DAD) is mandatory.
Host determines whether DHCP to be used or not by the flag in RA.
DHCPv6 cannot carry default gateway address.
So DHCPv6 must be used with RA.
Host
Router
(Router Solicitation)
Router Advertisement
Neighbor Solicitation(for DAD)
DHCP
Server
DHCP Solicit
DHCP Advertise
DHCP Request
DHCP Reply
Host
Router
(Router Solicitation)
Router Advertisement
Neighbor Solicitation(for DAD)
DHCP
Server
DHCP Solicit w/RCO
DHCP Reply w/RCO

## Slide 6: IPv6 configuration issues
In both case (stateless autoconfiguration and DHCPv6), IPv6 configuration cannot complete in 1 round-trip packet exchange which initiated by STA.
Modifying IPv6 configuration mechanism is not our business.
So we have no choice but to give up 1 round-trip higher layer configuration for IPv6 at this time. (without modification of IPv6 configuration mechanism)

## Slide 7: Per STA Information
AP keeps the following information per STA during association.
  HLCF message
    Higher Layer Configuration packet(s) piggybacked by Association Request.
  HLCF state
    State of the HLCF, for example
      Wait for authentication
      Transmitted to server (wait for reply)
      Received from server
      Transmitted to STA

## Slide 8: Authentication Success & DHCPv4 w/RCO in time
STA
AP
AS
DHCP
Server
FILS Assoc. Req.
Auth. Req.
AP Keeps
DHCP
Message
Auth. Resp.
DHCPOFFER w/RCO
DHCPACK w/RCO
(Inform dot11AssociationResponseTimeOut)
(piggyback DHCP)
(piggyback DHCP)
< dot11AssociationResponseTimeOut
VLAN Setup
AP Keeps
HLCF State
Association Completes
FILS Assoc. Resp.

## Slide 9: Authentication Success & DHCPv4 w/RCO not in time
STA
AP
AS
DHCP
Server
AP Keeps
DHCP
Message
(Inform dot11AssociationResponseTimeOut)
(piggyback DHCP)
< dot11AssociationResponseTimeOut
VLAN Setup
AP Keeps
HLCF State
(as normal data frame)
Association Completes
FILS Assoc. Req.
Auth. Req.
Auth. Resp.
DHCPOFFER w/RCO
DHCPACK w/RCO
(piggyback DHCP)
FILS Assoc. Resp.

## Slide 10: Authentication Success & IPv6 stateless address autoconfiguration
ICMPv6 RS
(piggyback ICMPv6 RA)
FILS Assoc. Resp.
FILS Assoc. Req.
STA
AP
AS
Router
AP Keeps
RS
(Inform dot11AssociationResponseTimeOut)
(piggyback ICMPv6 RS)
< dot11AssociationResponseTimeOut
VLAN Setup
AP Keeps
HLCF State
Association Completes
DAD by Data Frames
Auth. Req.
Auth. Resp.
ICMPv6 RA

## Slide 11: Authentication Success & IPv6 stateful address autoconfiguration
STA
AP
AS
Router
AP Keeps
RS
(Inform dot11AssociationResponseTimeOut)
(piggyback RS)
< dot11AssociationResponseTimeOut
VLAN Setup
AP Keeps
HLCF State
Association Completes
DHCP
Server
DHCP by Data Frames
ICMPv6 RS
(piggyback ICMPv6 RA)
FILS Assoc. Resp.
FILS Assoc. Req.
Auth. Req.
Auth. Resp.
ICMPv6 RA

## Slide 12: Authentication Failure
STA
AP
AS
FILS Req.
FILS Resp. (fail)
Auth. Req.
AP Keeps
HLFC Message
Auth. Resp. (fail)
(Inform dot11AssociationResponseTimeOut)
(piggyback DHCP)
AP Keeps
HLCF State

## Slide 13: References
11-12/273r8: SFD Text for Upper Layers
RFC2131: Dynamic Host Configuration Protocol
RFC4039: Rapid Commit Option for DHCPv4
RFC4862: IPv6 Stateless Address Autoconfiguration
RFC3315: Dynamic Host Configuration Protocol for IPv6