## Slide 1: Discussions about 802.11ai FILS Discovery Frame (DF) Content Design
Date: 2012-07-04
Authors:

## Slide 2: Abstract
This document is intended to facilitate further discussions about passive scanning enhancement, by presenting some considerations and analysis about the design of the FILS Discovery Frame contents.
This is a follow-up contribution with regarding to 802.11ai passive scanning enhancements as discussed in the contributions, 12/0406r5 and 12/0669r1. Also, it is about further details for a feature that has been accepted in the 802.11ai SFD.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
Straws poll conducted in 2012-May meeting about FILS Discovery Frame content design clearly shows two different opinions:
  Enough info for initiating association
  Certain info for assisting scanning, but need to receive more info for initiating association
This contribution will focus on further discussions about the 11ai FILS Discovery frame content design.
Another related but separate contribution, 12/0742, focuses on the discussions about the 11ai FILS Discovery frame format design.

## Slide 5: Basic Approach of FD Frame Content Design
Investigating Existing Reference Materials
  802.11ah Short Beacon
  Measurement Pilot Frame
  Beacon Frame / Probe Response frame
  11ai relevant contributions
Identifying FD Frame contents based on its basic functions:
  Advertize the presence of the AP on the channel
  Synchronize the STAs
  Provide necessary information for a fast AP/Network selection
  Provide necessary information to enable STA to transmit
  Anything else ???

## Slide 6
Recap of 802.11ah Short Beacon Frame
802.11ah has introduced a Short Beacon Frame into 11ah SFD (11/1137r9), based on proposals presented in contributions, 11/1503r2 and 12/129r3;
Overview of 11ah short beacon:
  A short beacon allows for reduced medium occupancy
    reduced power consumption for TX at AP and RX at STAs
  Or, for the same overhead as a ‘normal’ beacon, allows for shorter Beacon Intervals, improving synchronization and power save at the STAs
    Asynchronous STAs waking up at a random time can get in synch quickly
  The short beacon is not meant to displace the normal beacon
    AP may e.g. send a normal ‘full’ beacon every N short beacons
    Short beacon is an additional frame for optimized operation
  Frame Format and Contents of 802.11ah Short Beacon Frame:

## Slide 7: Investigation of 802.11ah Short Beacon Frame
Information | description / Notes | size (bytes) | Apply to 11ai FILS Discovery (FD) frame? | size in 11ai FD frame | Notes
Short Timestamp | used for Time Synchronization Function (TSF); mandatory in 11ah-SB. | 4 | yes, | 4 | Based on slide 11 on the 11ah-short beacon contribution, 11/1503r1, it shows it is sufficient to have 4 bytes TSF field, not 8 bytes.
Change sequence | used to Signal if network information has changed; Mandatory in 11ah-SB; mainly for power saving operations, e.g., sleep mode, after STA's initial association. | 1 | no, but debatable. | 0 | mainly for power saving operations, e.g., sleep mode, after STA's initial association.
time of next full beacon | Informs the STA of the arrival time of the next full beacon; optional in 11ah-SB; | 3 | Yes, but could be designed to use only 1 byte. | 1 | could be designed as an offset value for the FD frame Tx time, so that only need 1 byte in size
conpressed SSID | The SSID element indicates the identity of an ESS or IBSS. optional in 11ah-SB; | 4 | Yes, | 4 | 11ah Proposal 12/0129r3: Compressed SSID should be a hash of the full SSID; and Hashing function should be standardized
Access network options | indicate access services provided by AP/Network; optional in 11ah-SB; | 1 | Yes, | 1 | can use the same format as Figure 8-352, in 802.11-2012
BSS bandwidth | mandatory in 11ah-SB; inside FC field of the new MAC header design | 3bits | yes, but not as a separate parameter. | 0 | should be considered as part of the Channel descriptor along with other channel parameters

## Slide 8: Recap of Measurement Pilot (MP) Frame
Based on 802.11-2012, the Measurement Pilot (MP) frame
  is a compact Action frame transmitted pseudo-periodically by an AP at a small interval relative to a Beacon Interval;
  provides reduced information relative to a Beacon frame to allow for the required small interval.
The purpose of the Measurement Pilot frame is to assist a STA with the following functions:
  Rapid discovery of the existence of a BSS via passive scanning;
  Rapid collection of neighbor AP signal strength measurements via passive scanning;
  Enable transmission of a Probe Request.

## Slide 9: Recap of Measurement Pilot (MP) Frame – con’t
Frame Format and Contents of Measurement Pilot (MP) frame

## Slide 10: Investigation of 802.11 Measurement Pilot Frame
Information | description / Notes | size (bytes) | Apply to 11ai FILS Discovery (FD) frame? | size in 11ai FD frame | Notes
MP interval | basic periodicity of MP frames | 1 | yes, but it should be changed to FD interval | 1 | ** in units of TUs (i.e., 1024us) ** is it really needed, considering STA already received the FD frame?
Capability | only two bits are used: spectrum management; short slot time. | 1 | yes, but should be re-designed to cover more. | 2 | to cover critical initial link setup capabilities, based on MP capability and beacon/probe response capability, further capability considerations, e.g., IPv4/IPv6, security capabilities
Country | MP-frame uses a 2-byte condensed country string; although 3 bytes in dot11CountryString | 2 | Yes, | 2 | 
operation class | indicates the operating class value for the operating channel, as defined in Annex E. | 1 | yes | 1 | 
operation channel | indicates the operating channel, as defined in Annex E. | 1 | yes | 1 | 

## Slide 11: References in Beacon, Probe Response, and 11ai Contributions
Lots of additional information items in Beacon and Probe Response frames, as well as in other 11ai contributions;
A fundamental consideration: what other information items are really needed to be transmitted to STA in the first AP-to-STA message for setting up the link?
  Channel descriptors
  PHY specific info
  Security info
  BSS/AP load info
  Neighbor AP info
  What else????

## Slide 12: Investigation of Beacon, Probe Response, 11ai Contributions, …
Category | Information | description / Notes | size (bytes) | Apply to 11ai FILS Discovery (FD) frame? | size in 11ai FD frame
channel descriptors (beyond Country, Operation class, Operation channel) | power constraints | the information necessary to allow a STA to determine the local maximum transmit power in the current channel. | 1 | yes | 1
 | channel bandwidth | the channel bandwidth info is actually provided by the operation class and operation channel. | 0 | no, don't need a separate parameter | 0
PHY specific info | ERP (Extended Rate PHY) | 11g PHY, 1 byte as used in ERP IE in beacon frame; page 487, | 3 | yes, PHY dependant | 1
 | HT operation/HT capability | 11n PHY, current HT operation IE, HT capability IE, Overlapping BSS scan IE, and 20/40 coexistence IE | 77 | yes, PHY dependant, defined a compressed version | 2
BSS load info | BSS load / average delay / channel unitlization … | there are 5 BSS load related IEs in current beacon and probe response frame, i.e., 1) BSS load IE: 2+5 bytes 2) BSS Available Admission Capacity IE: 2+2+2*n bytes; 3) QoS Traffic Capability IE: 2+1+n bytes; 4) BSS Average Access Delay IE: 2+1 bytes 5) BSS AC Access Delay IE: 2+4 bytes | 35 | yes, should be compressed, e.g., an 1-byte indication, either using the average access delay or channel utilization | 1

## Slide 13: Investigation of Beacon, Probe Response, 11ai Contributions, … -- Con’t
Category | Information | description / Notes | size (bytes) | Apply to 11ai FILS Discovery (FD) frame? | size in 11ai FD frame
Security info | secuirty info | Security capability; info from the current RSNE; any other security related info? | 48 | Yes, should be very selective and compressed. | 4
Neighbor AP info | Neighbor AP info | references in 802.11-2012: 1) Neighbor report element, in Figure 8-215 2). Beacon timing IE, page 695, section 8.4.2.107; for neigbhor's next becon Tx time; 3). AP channel report IE, page 580, section 8.4.2.38 | 13+ per neighbor | yes, should be designed in a very compressed way. | Variable, 3*n; n is the number of neighbors

## Slide 14: Discussions about FILS Discovery (FD) Frame Contents
  Basic FD Frame Functions vs. Required Info Contents:
  Advertize the presence of the AP on the channel:
    BSSID, SSID, Channel descriptors, e.g., Country, Operation class, and Operation channel
  Synchronize the STAs
    Timestamp for Time Synchronization Function (TSF)
  Provide necessary information for a fast AP/Network selection
    Capabilities; Time to next TBTT; BSS load; Security; Access Network options; neighbor info; etc.
  Provide necessary information to enable STA to transmit
    PHY specific parameters; power constraint; etc.
  FD frame information content selection considerations :
  Minimize the mandatory info contents, e.g., only the AP presence parameters are mandatory;
  Include additional info contents in a flexible and incremental way.

## Slide 15: Summary of FILS Discovery Frame Content Considerations
Index | Information | description / Notes | size (bytes) | mandatory / optional
1 | compressed SSID | The SSID element indicates the identity of an ESS or IBSS. | 4 | mandatory
2 | Short Timestamp | used for Time Synchronization Function (TSF) | 4 | Optional
3 | Condensed Country string | uses the same 2-byte condensed country string as in MP frame; although 3 bytes in dot11CountryString | 2 | mandatory
4 | operation class | indicates the operating class value for the operating channel, as defined in Annex E. | 1 | mandatory
5 | operation channel | indicates the operating channel, as defined in Annex E. | 1 | mandatory
6 | power constraints | the information necessary to allow a STA to determine the local maximum transmit power in the current channel. | 1 | optional
7 | time of next TBTT | Informs the STA of the arrival time of the next full beacon, an offset value in unit of Tus from the FD frame Tx time | 1 | mandatory
8 | Access network options | indicate access services provided by AP/Network | 1 | optional
9 | FILS Discovery (FD) Interval | basic periodicity of FILS Discovery frames, in units of TUs (i.e., 1024us) | 1 | optional

## Slide 16: Summary of FILS Discovery Frame Content Considerations -- Con’t
Index | Information | description / Notes | size (bytes) | mandatory / optional
10 | Capability | used to indicate requested or advertised capabilities; covering critical initial link setup capabilities, based on MP capability and beacon/probe response capability, further capability considerations, e.g., IPv4/IPv6, etc. | 2 | optional
11 | PHY Info | PHY specific parameters, e.g., ** 11g PHY, 1 byte as used in ERP IE in beacon frame; page 487, **11n PHY, current HT operation IE, HT capability IE, Overlapping BSS scan IE, and 20/40 coexistence IE | variable | optional
12 | Security info | indicate security related capabilities, and further security info that requires early provisioning, e.g., info abstracted from the current RSNE | 4 | optional
13 | BSS load Info | Compressed indication of the BSS load info, e.g., average access delay and/or Channel utilization | 1 | optional
14 | Neighbor AP info | provide a list of neighbor APs/Channels and their TBTTs, e.g., just list the channel class / channel number and next beacon time. | Variable | optional
15 | Other optional IEs | used to include other additional IEs | variable | optional

## Slide 17: Straw-Polls
Straw-Poll-1: Do you support including the following information items in the FILS Discovery Frame body?
  Compressed SSID
  Condensed Country String
  Operation Class
  Operation Channel
  Time of Next TBTT
Result Yes No Abstain_______________

## Slide 18: Straw-Polls
Straw-Poll-2: Do you support optionally including the following information items in the FILS Discovery Frame body?
  Short Timestamp
  Power Constraints
  Access Network Options
  FILS Discovery frame interval
  Capability information
  Security Information
  BSS Load Information
  PHY information
  Neighbor AP information
Result Yes No Abstain_______________

## Slide 19: Motions for Proposed Text for SFD
Motion-1: add the following text to Subsection “6.2.1 General Approach”, on page 8, in the TGai SFD, 12/0151r8
The FILS Discovery frame shall include the following information fields:
  A Compressed SSID field
  A Condensed Country String field
  An Operation Class field
  An Operation Channel field
  A Time of Next TBTT field
Mover:
Seconder:
Result Yes No Abstain_______________

## Slide 20: Motions for Proposed Text for SFD
Motion-3: add the following text to Subsection “6.2.1 General Approach”, on page 8, in the TGai SFD, 12/0151r8
The FILS Discovery frame may include the following information items:
  Short Timestamp
  Power Constraints
  Access Network Options
  FILS Discovery frame interval
  Capability
  Security Information
  BSS Load Information
  PHY information
  Neighbor AP information
Mover:
Seconder:
Result Yes No Abstain_______________

## Slide 21
References:
IEEE Std 802.11™-2012
11-12-0191-03-00ai-call-for-contributions-to-the-tgai-specification-framework
11-12-0151-07-00ai-proposed-specification-framework-for-tgai
11-12-0406-05-00ai-passive-scanning-improvements-draft
11-12-0669-01-00ai-passive-scanning-improvements-ad-hoc-report
11-12-0742-00-00ai-FILS-Discovery-Frame-Format-Discussions
11-11-1137-09-00ah-specification-framework-for-tgah
11-11-1503-02-00ah-short-beacon
11-12-0129-03-00ah-short-beacon