## Slide 1: Beacon Pointer in Probe Response
Date: 2012-07-10
Authors:

## Slide 2: Abstract
This submission proposes a new mechanism for AP discovery.
It doesn’t help the fast AP discovery for FILS directly. But it may provide a reduction method of probe exchanges in order to improve circumstances of WLAN communications.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Motivation
It has been discussed in TGai that reduction method of unnecessary probe exchanges would be required in order to obtain better effectiveness of FILS.
Preventing probe request is one of the solutions.

## Slide 5: Proposal (case 1)
Probe Response includes Beacon Pointer.
STA can know the time offset to the next Beacon by this information.
AP
STA
Probe Request
Probe Response
w/ Beacon Pointer
t
t
Beacon
Probe Delay
Initiate active scanning
Obtain Beacon Pointer from Probe Response
Time offset

## Slide 6
“Connection Manager”
Wi-Fi communications are not only for certain PC geek in these days.
3G operators provide “Connection Manager” for Wi-Fi connection to ease setting of required configurations and associations with APs.
This function may refrain from initiating association with discovered AP because of low signal level, etc. This behavior may prevent users from having a negative impression by low quality.

## Slide 7
Graphic - 1
STA executes intermittent active scanning for power saving.
STA receives Probe Response from a desired AP in fringe area of its coverage.
STA refrains from association with that AP because of some reason, e.g. low signal level.
Desired AP
Probe req.
Probe req.
Probe req.
Probe res.
(low signal level)
fringe area

## Slide 8
Graphic - 2
STA already knows the Beacon timing of the AP. So the STA can verify whether it is approaching the AP or not by observing Beacon frames, without sending Probe Requests.
This behavior will mitigate packet congestion by probes.
Desired AP
Probe req.
Probe res.
(low signal level)
fringe area
Beacon

## Slide 9: Proposal (case 2)
STA detects Probe Response from a desired AP. But the STA refrains association with that AP because of some reason.
STA executes Active scanning at the certain timing for receiving Beacon. If received Beacon at that timing, Probe Request will be omitted.
STA can go into power saving mode up to the timing of Beacon reception.
AP
STA
Probe Request
Probe Response
w/ Beacon Pointer
t
t
Beacon
Probe Delay
Beacon
Beacon Interval * N
Obtained Beacon Pointer from the desired AP
Omit
Probe Request
Probe Delay
Time offset
STA may go into power saving mode.
Wake up.

## Slide 10
Example of STA’s behavior
t
STA
Probe req.
Probe delay
Power saving
Listening
Power saving
5 sec
5 sec
AP
t
Probe res.
Power saving
Beacon
5 sec +
Time offset
Beacon
5 sec
(depends on BI)
Power
saving
Omit
Probe req.

## Slide 11
Comment at teleconference (1)
Q1:
Why new information is needed in the probe response as the probe response today includes a time stamp and information on the beacon interval which could be used to deduce the required information.
A1:
The probe response today includes a time stamp and a beacon interval. But in my understanding, the time offset to the next beacon cannot be deduced from these information.

## Slide 12
Comment at teleconference (2)
Q2:
Why should a STA not try to set up a link at the first time it sees an AP but instead wait longer. This is in contrast to what TGai wants to achieve.
A2:
Off course, the STA can try to set up a link at that time. It depends on policy whether a STA does so or not.

## Slide 13
Comment at teleconference (3)
Q3:
How tight oscillator constrains have to be to guarantee long synchronization for longer sleep periods.
A3:
Adequately longer listening (probe delay) duration of beacon may compensate fluctuation of oscillator by longer sleep periods. But I don’t believe that fluctuation is so big.
A STA can also send a probe request when lost beacon timing of desired AP.

## Slide 14
Straw poll
Do you agree to add the following text to Section 6.1 of SFD?
Yes: No: Need more info:
6.1.X Beacon pointer
TGai compliant AP may include Beacon Pointer in Probe Response which indicates time offset to the next Beacon.
TGai compliant STA may execute Active/Passive scanning at the Beacon timing guessed by Beacon Pointer.

## Slide 15
Motion
Move to add the following text to Section 6.1 of SFD?
Yes: No: Abstain:
6.1.X Beacon pointer
TGai compliant AP may include Beacon Pointer in Probe Response which indicates time offset to the next Beacon.
TGai compliant STA may execute Active/Passive scanning at the Beacon timing guessed by Beacon Pointer.