## Slide 1: AP operational status
Date: 2012-07-02
Authors:

## Slide 2: Abstract
This submission proposes inclusion of concept to SFD. It’s relating to AP discovery.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Motivation
It is preferred for STAs to avoid associations with APs which the performance of communication is supposed to be poor, even if the required time for association is very short by FILS.
It may be good for STAs to compare supposed performance between detected APs.
<Image>
AP1
AP2
AP3
Channel is congested.
Latency is big.
No problem
AP3 is good for association.

## Slide 5: Proposal
AP may include some performance related indicators in Beacon and Probe Response.
STA can determine whether it goes to association process with that AP or not, by verifying these indicators.

## Slide 6: Straw poll
Do you agree to add the following text to Section 6.1 of SFD?
6.1.X AP Operational Status
TGai compliant AP may include Operational Status information in Beacon and Probe Response. The information may be, for example:
  BSS load,
  BSS average access delay,
  BSS available admission capacity
Yes: No: Need more info:

## Slide 7
Motion
Move to add the following text to Section 6.1 of SFD?
Yes: No: Abstain:
6.1.X AP Operational Status
TGai compliant AP may include Operational Status information in Beacon and Probe Response. The information may be, for example:
  BSS load,
  BSS average access delay,
  BSS available admission capacity

## Slide 8: References
11/1565r0 AP status broadcast (KDDI)
12/0011r0 Coarse BSS metric IE (KDDI)
12/0545r0 Access control mechanism for FILS (China Mobile)