## Slide 1: Non-HT Duplicate PPDU FILS Advertisement Frame
Date: 2012-07-04
Authors:

## Slide 2: Abstract
The very high throughput (VHT) enables transmission bandwidths of 20, 40, 80 and 160 MHz
  Currently BSS is discoverable only at the primary channel (20 MHz), even if BSS transmits frames at 80 MHz
  The BSS should be discoverable at the whole bandwidth in which the BSS operates
The larger scanned bandwidth per operation reduces the number of scanning operations speeds-up the scanning
  This ensures initial link setup within 100 ms

## Slide 3: Background
The discovery delay may be calculated:
  Number of scanning operations * time per scanning operation
    It is important to reduce the number of scanning operations as well as shorten the time per scanning operation
The 802.11ai has provided solutions to speed-up discovery in a scanned channel
  However, one channel is scanned at a time
The scanning messages may hint the next channel to be scanned

## Slide 4: Motivation, channels at 5 GHz
5 GHz has many channels to be scanned
  Some mechanism to reduce the number of scanning operations is needed to speed-up the scanning
The turquoise colour shows the channelization of the VHT STA
  VHT STA is capable to use 20, 40, 80 and 160 MHz transmission bandwidths as shown
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
5170
MHz
5330
MHz
5490
MHz
5710
MHz
5735
MHz
5835
MHz
Weather radars
only in US

## Slide 5: Recap, VHT transmissions summary as defined in 802.11ac
Each STA obtains TXOPs in its primary channel
  The channel status (busy /idle) of other channels does not affect to backoff calculation
Larger transmission bandwidth may be used, if CCA of the indicates channel idle a PIFS before the TXOP
The channels are taken into use on specific order
  The primary channel may be freely selected
  The primary channel defines the secondary20 and secondary40 channels as shown in previous slide

## Slide 6: Recap, VHT receptions summary as defined in 802.11ac
Each transmission has a preamble that is transmitted as separate copy for each 20 MHz band
  The preamble indicates the PPDU type and transmission bandwidth
The STA obtains a copy of preamble on its primary channel
  The VHT PPDU payload is receivable (decoded correctly) only if the receiver has the same primary channel as the transmitter
Preamble
Preamble
Preamble
Preamble
Payload / Data

## Slide 7: Recap, Non-HT Duplicate PPDU as defined in 802.11n/ac
802.11n defines non-HT duplicate PPDU
  The PPDU duplicates the 20 MHz wide MPDUs to larger bandwidth making, each 20 MHz is receiveable as separate frame
    40MHz wide non-HT duplicate PPDU consist of two 20MHz PPDUs
    80 MHz wide non-HT duplicate PPDU consist of four 20MHz PPDUs
  The reception of the frame is the same as 20MHz PPDU
    The receiver need not to have the same primary channel as the transmitter
    802.11ac uses RTS and CTS frames that are non-HT duplicate PPDUs
Payload
Payload
Payload
Payload
Primary channel of the transmitter
Preamble
Preamble
Preamble
Preamble

## Slide 8: Non-HT Duplicate PPDU to enhance passive scanning
FILS Advertisement frame has been discussed to speed-up the passive scanning of the BSS
  The FILS Advertisement frame transmitted as non-HT Duplicate PPDU makes the BSS discoverable for its whole transmission bandwidth
  Larger bandwidth is the only differentiating feature for FILS Advertisement frame from Measurement Pilot or Probe Response frames
Payload/FILS Advertisement
Payload/FILS Advertisement
Payload/FILS Advertisement
Payload/FILS Advertisement
Primary channel of the transmitter
Preamble
Preamble
Preamble
Preamble

## Slide 9: Link Setup after reception of FILS Advertisement
A STA may transmit frames to FILS Advertisement frame transmitter, when it has the same primary channel as FILS Advertisement transmitter
  Normal FILS signaling is performed at the same primary channel

## Slide 10: Advantages
More channels are scanned in a single scanning operation
  The discovery is faster, for instance 80 MHz may be scanned instead of 20 MHz
  The amount of scanning operations is reduced
    This makes discovery delays acceptable to FILS Requirements, i.e. initial link setup < 100ms
The mechanism is simple, no PHY changes
  No new PPDU type is needed
  Transmission and reception are already defined in 802.11ac

## Slide 11: Motion
Move to add the following text to the clause 6 of TGai Specification Framework document (11-12/0151r08):
” 802.11ai shall enable scanning frames transmission as non-VHT duplicate PPDUs at 20, 40, 80 and 160 MHz”