## Slide 1: Fast Authentication in TGai : Updates to EAP-RP
Name | Affiliations | Address | Phone | email
George Cherian Santosh Abraham Jouni Malinen | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | +1 (858)-651-6645 | gcherian@qualcomm.com sabraham@qualcomm.com jouni@qca.qualcomm.com
Date: 2012-07-16
Authors:

## Slide 2: Goal
Updated options on EAP-RP (from 11/1160r9) for discussion (based on feedback received during last meeting)
What’s different from earlier proposal?
  Explicit unicast ANonce
  Optional PFS
July 2012

## Slide 3: Option-1: Fast Association for FILS [Deferred ANonce]
Sending of ANonce to STA is deferred until step-7
Step-2: STA generates rMSK based on [RFC 5296]
rMSK = KDF (K, S), where K = rRK and
S = rMSK label | "\0" | SEQ | length
AP generates PTK at step-6
IP-addr assignment req sent at step-9

## Slide 4: Option-2: Fast Association for FILS
[step-3] STA generates rMSK based on [RFC 5296]
rMSK = KDF (K, S), where K = rRK and
S = rMSK label | "\0" | SEQ | length
[step-3a] PTK is generated using rMSK, ANonce & SNonce
Key Confirmation:
[step-4]: STA applies message integrity on the combined payload that include EAP-Re-Auth, DHCP-Discover & Snonce using KCK
[step 8b] AP verifies & performs message integrity check for DHCP & SNonce and decrypt DHCP
July 2012

## Slide 5: Comparison between Option 1 & 2
Option-1 is cleaner from messaging standpoint
  IP address assignment request initiated after EAP-RP signaling
Option-2 enables ANonce filtering that can be applied at AP before forwarding packets to AS
  May help reduce the likelihood of DoS attack on AS
July 2012

## Slide 6: PFS addition (based on option-1)
PublicKeys are assumed to be ephemeral Diffie Hellman (DHE) public keys
Public Key of STA: KSTA-pub sent at step-3
Public Key of AP: KAP-pub sent at step-7
Shared Key : KSA generated by AP at step-6
Shared Key : KSA generated by STA at step-8
Computation of PTK includes rMSK, Snonce, Anonce & KSA

## Slide 7: PFS addition (based on option-2)
PublicKeys are assumed to be ephemeral Diffie Hellman (DHE) public keys
Public Key of STA: KSTA-pub sent at step-2a
Public Key of AP: KAP-pub sent at step-2b
Shared Key : KSA generated by AP at step-8a
Shared Key : KSA generated by STA at step-3a
Computation of PTK includes rMSK, Snonce, Anonce & KSA
July 2012

## Slide 8: Motion-1
Add the following text to Subsection 4.1 “Pre-established security context”
  The draft specification shall include
    support for the EAP-RP [as defined in IETF RFC 5295/5296] for fast key establishment.
    a nonce exchange and key confirmation that does not degrade the security of the 4-way handshake.
Moved :
Seconded:
Yes
No
Abstain

## Slide 9: Motion-2
Add the following text to Subsection 4.1 “Pre-established security context”
  The draft specification shall include optional support of PFS as part of key establishment.
Moved :
Seconded:
Yes
No
Abstain