## Slide 1: Q Matrix Requirement for 1MHz/2MHz detection
Date: 2012-07-16
Authors:
Slide 1

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:
Slide 3

## Slide 4: Outline
  LTF based classification of 1MHz vs. 2MHz preambles uses an orthogonal LTF sequence design as explained in 11/1482r4 and 12/0115 and defined by the orthogonality metric in Appendix-A of 12/0115 copied in the Appendix here for convenience.
  The classification metric inherently assumes a smooth channel. In order to ensure proper classification when multiple antenna transmitters precode the transmit signal with a spatial mapping matrix Q we provide a recommendation for the values of Q . We further revise the text in section R.3.2.1.1.C (auto-detection) to better explain the two auto-detections
Slide 4

## Slide 5: Proposal
Propose to rewrite the text in section R.3.2.1.1.C as follows:
R.3.2.1.1.C: Auto-detection between 1MHz and 2MHz and between >=2MHz short and long preambles
  Auto-detection between short and long >=2MHz preambles is facilitated by having a 90 degrees phase rotation on the 2nd SIG symbol as shown in the figure below.
  Auto-detection between 1MHz and 2MHz preambles is facilitated using two options as shown in the figure below
    The first auto-detection method uses the property of orthogonal LTF sequences as described in 11/1482r4 and 12/0115 and defined by the orthogonality metric in Appendix-A of 12/0115.
    The second auto-detection method is facilitated by noting that for >=2MHz short preamble and long preamble the 1st SIG symbol is always QBPSK whereas the corresponding time-wise symbol of the 1MHz preamble (in the figure below) is BPSK modulated - refer to 11/1482r3.
Slide 5

## Slide 6: Cont
Add a new section with the following text
3.6 Spatial Mapping Matrix
The auto-detection between 1MHz and 2MHz preambles as described in sub-section 2a of section R.3.2.1.1.C assumes channel smoothness. It is recommended that the spatial mapping matrix Q applied to LTF1 is chosen such that it preserves the smoothness of the physical channel. This can, for example, be achieved by minimizing the amplitude and phase variation of each element of Q in successive tones. Examples:
  The following Q may be used: Q as defined for cyclic shift diversity using the values specified in the corresponding tables
  The following Q should not be used – antenna hopping as described in 802.11REVmb section 20.3.11.11.2 (C)-(2) - the values of Q on successive tones flip between 1 and 0
Slide 6

## Slide 7: Pre-Motion
Do you support the proposal in slides 5 and 6?
Y
N
A
Slide 7

## Slide 8: Appendix A - LTF Orthogonality Metric
The orthogonality metric used for searching for an optimal 32FFT LTF sequence is
  are the LTF sequences for 32FFT and the upper and lower portions of the 64FFT
  The index k is limited to indices [-16:-1 1:15] (skipping 32FFT DC)
The metric enables a frequency domain cross correlation to be performed
    Where y(k) is the final received and averaged LTF value (used for channel estimation), p(k) is the transmitted LTF sequence belonging to a 64FFT or 32FFT.
Slide 8

## Slide 9: Cont.
Cross correlation with the transmitted sequence finds the most likely transmitted sequence and autocorrelation of successive tones removes the effect of the channel (implicitly assuming smoothness, or small variation from tone to tone)
  For the correct sequence we get a large positive number
  For the incorrect sequence we get a small number – the sum of random numbers
Slide 9