## Slide 1: Channelization Selection for 802.11ah
Date: 2012-07-16
Slide 1
Name | Affiliations | Address | Phone | email
Huai-Rong Shao | Samsung Electronics | 75 West Plumeria Dr, San Jose, CA 95134 | +1-408-544-2754 | hr.shao@samsung.com
Chiu Ngo | Samsung Electronics |  |  | chiu.ngo@samsung.com
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jin Sam Kwak | LG Electronics |  |  | 
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | james.wang@mediatek.com
Jianhan Liu | MediaTek |  |  | jianhan.liu@mediatek.com
Vish Ponnampalam | MediaTek |  |  | vish.ponnampalam@mediatek.com
James Yee | MediaTek |  |  | james.yee@mediatek.com
Thomas Pare | MediaTek |  |  | thomas.pare@mediatek.com
Kiran Uln | MediaTek |  |  | kiran.uln@mediatek.com
Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA | +1 408 543 3370 | mfischer@broadcom.com
Eric Wong | Broadcom |  |  | ewong@broadcom.com
Fei Tong | CSR | Churchill House, Cambridge business park, CB4 0WZ | 0044-1223692160 | fei.tong@csr.com
Stefan Aust | NEC | 1753 Shimonumabe, Nakahara-ku, Kawasaki, Kanagawa 211-8666, Japan | +81 44 435 1177 | aust.st@ncos.nec.co.jp

## Slide 2
Authors continued:
Slide 2
Name | Affiliations | Address | Phone | email
Minyoung Park | Intel Corp. |  |  | minyoung.park@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel Corp. |  |  | emily.h.qi@intel.com
Yong Liu | Marvell |  |  | yongliu@marvell.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Simone Merlin | Qualcomm | 5775 Morehouse Dr, San Diego, CA | 8588451243 | smerlin@qualcomm.com
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
George Calcev | Huawei | Rolling Meadows, IL USA |  | George.Calcev@huawei.com
Osama Aboul Magd | Huawei |  |  | Osama.AboulMagd@huawei.com
Young Hoon | Huawei |  |  | Younghoon.Kwon@huawei.com
Betty Zhao | Huawei |  |  | Betty.Zhao@huawei.com
David Yangxun | Huawei |  |  | David.Yangxun@huawei.com
Bin Zhen | Huawei |  |  | ZhenBin@huawei.com
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn

## Slide 3
Authors continued:
Slide 3
Name | Affiliations | Address | Phone | email
Minho Cheong | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Hyoungjin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Heejung Yu | ETRI |  |  | heejung@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Sayantan Choudhury | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com
Shoukang Zheng | I2R | 1 Fusionopolis Way, #21-01 Connexis Tower, Singapore 138632 | +65-6408 2000 | skzheng@i2r.a-star.edu.sg
Haiguang Wang | I2R |  |  | hwang@i2r.a-star.edu.sg
Wai Leong Yeow | I2R |  |  | wlyeow@i2r.a-star.edu.sg
Zander Lei | I2R |  |  | leizd@i2r.a-star.edu.sg
Jaya Shankar | I2R |  |  | jshankar@i2r.a-star.edu.sg
Anh Tuan Hoang | I2R |  |  | athoang@i2r.a-star.edu.sg
Joseph Teo Chee Ming | I2R |  |  | cmteo@i2r.a-star.edu.sg
Shusaku Shimada | Yokogawa Co. | 2-9-32 Nakacho Musashino-shi, Tokyo 180-8750 ,Japan | +81 42 252 5558 | shusaku@ieee.org
Mitsuru Iwaoka | Yokogawa Electric Co. |  |  | Mitsuru.Iwaoka@jp.yokogawa.com

## Slide 4: Motivation
After channelization is done in US and other countries
Channel selection rules need to be defined
  Minimize interference between BSS
  Maximize the usage of channels for different applications
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 5
Slide 5
Among 26 MHz totally, only 4 MHz is being used in the above example
But neither 8 MHz nor 16 MHz channels available, and only three 4 MHz channel available
Problem Statement
902
MHz
928
MHz
1 MHz
2 MHz
4 MHz
8 MHz
16 MHz
: Channel is being used
: Channel not available
: Channel available

## Slide 6
Slide 6
If two 1 MHz channels are allocated to other positions
One 16 MHz channel, two 8 MHz channels , and five 4 MHz channels available
Problem Statement
902
MHz
928
MHz
1 MHz
2 MHz
4 MHz
8 MHz
16 MHz
: Channel is being used
: Channel not available
: Channel available

## Slide 7: Channel selection at BSS setup
Among all available channels, the new BSS should select a idle channel which can help keep maximum number of idle (available) wider bandwidth channels after it is selected
  The selected channel has least overlap with other wider bandwidth channels
Channel availability is decided by channel scanning results
  PHY design such as Mask may affect channel availability, for example, interference between adjacent channels
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 8: Example of channel selection at BSS setup
If adjacent channels are not treated as available from channel scanning results
902 MHz
928 MHz
1 MHz
2 MHz
4 MHz
8 MHz
16 MHz
: Channel is being used
: Channel not available
: Channel available
Choose one from these three if a new 1 MHz BSS needs to be set up
: Channel not preferred due to adjacent channel interference
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 9: Example of channel selection at BSS setup
If interference between adjacent channels is low
902 MHz
928 MHz
1 MHz
2 MHz
4 MHz
8 MHz
16 MHz
: Channel is being used
: Channel not available
: Channel available
Choose one from these two if a new 1 MHz BSS needs to be set up
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 10: Conclusion
Channel selection rules need to be defined
  Minimize interference between BSS
  Maximize the usage of channels for different applications
Channel selection at BSS setup stage
  New BSS should select a channel which can help keep maximum number of available wider bandwidth channels

## Slide 11: Straw Poll
Do you support to include the following channel selection rule in the 802.11ah specification framework document?
  Among all available channels, the new BSS should select an idle channel which can help keep maximum number of idle (available) wider bandwidth channels after it is selected (Details TBD).
Y
N
A