## Slide 1: 802.11ah - CSD Table Values
Date: 2012-07-16
Authors:

## Slide 4: Abstract
Proposal for CSD framework and CSD table values for 802.11ah 1MHz and >=2MHz Tx.

## Slide 5: Background for Cyclic Shift Delays (CSDs)
Fixed and periodic STF sequence transmitted across multiple spatial streams/antennas can have effect of being unintentionally beamformed
  RxAGC is set according to power measurement on STF
  AGC setting will determine quantization/saturation effects for the ADC
    Can negatively affect SIG/Data field decoding performance
  CSDs across spatial streams/antennas reduce RxPower fluctuations during STF

## Slide 6: Framework for CSD Application in 11ah
  CSD design criteria for 11ah should follow that used for 11ac:
      See Appendix for detailed information on Frame-specific Tx Structures
Defined frame formats for 11ah:
  1MHZ Preamble, >=2MHz Short Preamble
    1 set of CSDs applied for entire frame
  >=2MHz Long Preamble
    Separate STFs means different sets of CSDs can be used for Omni and Data portions
Data Portion

## Slide 7: Framework Summary for CSDs
Use per-space-time-stream CSD tables for
  1MHz frame format
  >=2MHz Short frame format
  >=2MHz Long frame format, Data portion
    Restart CSD application afresh for each user’s space time streams (Same as in 11ac).
For >=2MHz Long frame format, Omni Portion:
  Use per-antenna CSD table
Construct table of CSDs for each case that minimizes unintentional beamforming effect:
  Nested structure constraint desirable if no impact on performance
    3Tx case shares 2 of its CSDs with the 2Tx case, and the 4Tx case shares 3 CSDs with the 3Tx case.
    Facilitates cleaner implementation in hardware

## Slide 8: CSD Evaluation Metric
  To minimize quantization/saturation at ADC, difference between measured STF and Data (or SIG) power should be low, and CDF of metric should be tight.
    STF is fixed periodic sequence, same for each stream
1MHz STF and 2MHz STF
  CSD values from 11n/11ac (2MHz) were chosen w.r.t. D-NLOS channel.
    Re-examine CSD choice with SCM UMa also taken into consideration
  1MHz STF is no longer simple downclock of 20MHz 11n/11ac STF, therefore perform full search to find best CSD choices

## Slide 9: CSD Evaluation Metric (cont.)
Example:
  1MHz, 2 Tx Streams
  CSD = [0 -3]μs
  Consider
    AWGN (rand phase),
    DNLOS (stretched),
    SCM Urban Macro
Choose CSD that minimizes following metric:
  ABS(MIN(5th ptile)) + ABS(MAX(95th ptile))
  Where MAX and MIN look over the channel models being considered
  Metric is sum of dotted RED distances
Saturation
Quantization
95th%-tile
5th%-tile
Slide 9

## Slide 10: 1 and 2MHz CSD Selection
Simluation Setup
  1 and 2MHz Channel Bandwidths
    Estimate STF RxPower over STF field duration
    Estimate Data RxPower (BPSK modulated) over same duration
  NumTxStreams = [2:4], w/ Rand. Phase Offsets {0, π} per stream
  2x2, 3x3, 4x4 Channel Models:
    AWGN (i.e. flat w/ random phase)
    D-NLOS (stretched)
    SCM Urban Macro
  CSD values range from -[0 : 1 : 7]μs for 1MHz, -[0 : 0.5 : 7.5]μs for 2MHz.
    Unique value used for each Tx stream
    1st stream has no CSD offset (i.e. 0us)
    Example: 1MHz 4Tx Stream case has 35 possible CSD combinations
  Search across all CSD combinations to select best CSD according to metric.

## Slide 11: Optimal >=2MHz Short Frame, Long (Data Portion) Frame CSD Tables
(CSD values listed in absolute time (μs) rather than BW-dependent samples)
Specified per-Tx-Stream
Results show scaled 11n/11ac values are also best choice for 11ah >=2MHz in SCM UMa.
  STF pattern remains same
T_cs(n) for >=2MHz, Short Frame Format and Data portion of Long Frame Format |  |  |  | 
Total number of space-time streams | Cyclic shift (for Tx Stream n) (μs) |  |  | 
 | 1 | 2 | 3 | 4
1 | 0 | - | - | -
2 | 0 | -4 | - | -
3 | 0 | -4 | -2 | -
4 | 0 | -4 | -2 | -6

## Slide 12: Optimal >=2MHz Long (Omni Portion) Frame CSD Tables
Specified per-Tx-Antenna:
  SIG is replicated across TxAntennas
  Same shift values as >=2MHz Long (Data portion) Frame table
T_cs(n) for >=2MHz, Omni Portion of Long Frame Format |  |  |  | 
Total number of Tx antennas | Cyclic shift (for Tx Antenna n) (μs) |  |  | 
 | 1 | 2 | 3 | 4
1 | 0 | - | - | -
2 | 0 | -4 | - | -
3 | 0 | -4 | -2 | -
4 | 0 | -4 | -2 | -6
(CSD values listed in absolute time (μs) rather than BW-dependent samples)

## Slide 13: 1MHz - 2Tx Stream Case Simulations
[0 -4]us is best choice across all channel models for 2Tx Antenna CSD
  Clearly do want to use some CSD (i.e. not [0 0]us)
  SCM UMa is the worst-case: 5-to-95%-tile spread approx. 6dB
Quantitative results of CSD combinations for {2, 3, 4} Tx Stream shown in Appendix.
CSDs for 2Tx Antenna: SCM UMa Channel

## Slide 14: Optimal 1MHz Frame CSD Tables
Specified per-Tx-Stream
  Different from >=2MHz per-Tx-stream CSDs because 1MHz STF is new.
T_cs(n) for 1MHz Frame Format |  |  |  | 
Total number of space-time streams | Cyclic shift (for Tx Stream n) (μs) |  |  | 
 | 1 | 2 | 3 | 4
1 | 0 | - | - | -
2 | 0 | -4 | - | -
3 | 0 | -4 | -1 | -
4 | 0 | -4 | -1 | -5
(CSD values listed in absolute time (μs) rather than BW-dependent samples)

## Slide 15: Strawpoll #1
Do you agree with the application of CSDs on a:
  Per-space-time-stream basis for the 1MHz and >=2MHz Short frame formats?
  Per-space-time-stream basis for the Data portion of the >=2MHz Long frame format?
  Per-antenna basis for the Omni portion of the >=2MHz Long frame format?
  Y
  N
  A

## Slide 16: Strawpoll #2
Do you agree to adopt the following CSD table (reproduced below) for the Short frame format and Data portion of the Long frame format for >= 2MHz modes?
  Y
  N
  A
Data Portion
T_cs(n) for >=2MHz, Short Frame Format and Data portion of Long Frame Format |  |  |  | 
Total number of space-time streams | Cyclic shift (for Tx Stream n) (μs) |  |  | 
 | 1 | 2 | 3 | 4
1 | 0 | - | - | -
2 | 0 | -4 | - | -
3 | 0 | -4 | -2 | -
4 | 0 | -4 | -2 | -6
Long Frame Format, >=2 MHz

## Slide 17: Strawpoll #3
Do you agree to adopt the following CSD table (reproduced below) for the Omni portion of >=2MHz Long frame format?
  Y
  N
  A
T_cs(n) for >=2MHz, Omni Portion of Long Frame Format |  |  |  | 
Total number of Tx antennas | Cyclic shift (for Tx Antenna n) (μs) |  |  | 
 | 1 | 2 | 3 | 4
1 | 0 | - | - | -
2 | 0 | -4 | - | -
3 | 0 | -4 | -2 | -
4 | 0 | -4 | -2 | -6
Long Frame Format, >=2 MHz
Data Portion

## Slide 18: Strawpoll #4
Do you agree to adopt the following CSD table (reproduced below) for the 1MHz Short frame format?
  Y
  N
  A
Short Frame Format, 1 MHz
T_cs(n) for 1MHz Frame Format |  |  |  | 
Total number of space-time streams | Cyclic shift (for Tx Stream n) (μs) |  |  | 
 | 1 | 2 | 3 | 4
1 | 0 | - | - | -
2 | 0 | -4 | - | -
3 | 0 | -4 | -1 | -
4 | 0 | -4 | -1 | -5

## Slide 19
Appendix
  1MHz Frame, 2MHz Short Frame Tx Structure
  >=2MHz Long Frame Tx Structure
  1MHz CSD Search Data

## Slide 20: 1MHz Frame and 2MHz Short Frame Tx Structure
Same CSD values applied to entire Short packet, according to value of N_sts

## Slide 21: >=2MHz Long Frame Tx Structure
Can use per-Tx-Antenna CSDs as there is no Q-Matrix involved.
CSD application prior to Q-Matrix is performed per-Tx-Stream.
Choice of Q-Matrix is up to implementer, hence don’t specify per-antenna CSDs

## Slide 22: 1MHz - 2Tx Stream CSD Rankings
CSD Metric = STF Pwr/Data Pwr
5th and 95th percentile points of CDF of Metric
Values in dB
Ranking by abs(MAX) + abs(MIN) metric
-0.62 | 0.83 |  | -1.12 | 1.05 |  | -1.76 | 1.45 |  | 1.45 | -1.76 | 3.21 |  | [0 4]
-1.23 | 1.25 |  | -1.44 | 1.31 |  | -1.81 | 1.58 |  | 1.58 | -1.81 | 3.39 |  | [0 3]
-1.26 | 1.27 |  | -1.45 | 1.31 |  | -1.81 | 1.60 |  | 1.60 | -1.81 | 3.41 |  | [0 5]
-2.42 | 1.81 |  | -2.06 | 1.61 |  | -3.08 | 2.11 |  | 2.11 | -3.08 | 5.19 |  | [0 2]
-1.21 | 1.24 |  | -3.46 | 2.06 |  | -2.63 | 1.94 |  | 2.06 | -3.46 | 5.52 |  | [0 7]
-1.27 | 1.27 |  | -3.51 | 2.08 |  | -3.36 | 2.09 |  | 2.09 | -3.51 | 5.59 |  | [0 1]
-2.49 | 1.85 |  | -2.09 | 1.63 |  | -3.51 | 2.25 |  | 2.25 | -3.51 | 5.76 |  | [0 6]
5th ptile | 95th ptile |  | 5th ptile | 95th ptile |  | 5th ptile | 95th ptile |  | MAX of 95% of Channel Models | MIN of 5% of Channel Models | abs(MAX) + abs(MIN) |  | CSD Vector
AWGN |  |  | DNLOS (stretched) |  |  | SCM Urban Macro |  |  |  |  |  |  | 

## Slide 23: 1MHz - 3Tx Stream CSD Rankings
-1.17 | 1.44 |  | -2.46 | 1.80 |  | -2.39 | 1.94 |  | 1.94 | -2.46 | 4.40 |  | [0 1 4]
-1.14 | 1.40 |  | -2.41 | 1.79 |  | -2.61 | 1.84 |  | 1.84 | -2.61 | 4.45 |  | [0 3 7]
-1.18 | 1.42 |  | -2.47 | 1.82 |  | -2.04 | 2.02 |  | 2.02 | -2.47 | 4.49 |  | [0 1 5]
-1.15 | 1.46 |  | -2.47 | 1.83 |  | -1.96 | 2.13 |  | 2.13 | -2.47 | 4.61 |  | [0 3 4]
-1.19 | 1.47 |  | -2.45 | 1.84 |  | -2.70 | 1.95 |  | 1.95 | -2.70 | 4.64 |  | [0 4 5]
-1.14 | 1.44 |  | -2.39 | 1.82 |  | -2.66 | 2.08 |  | 2.08 | -2.66 | 4.74 |  | [0 4 7]
-1.68 | 1.94 |  | -2.68 | 2.00 |  | -2.66 | 2.13 |  | 2.13 | -2.68 | 4.81 |  | [0 5 7]
-3.02 | 1.55 |  | -2.03 | 1.58 |  | -2.20 | 1.85 |  | 1.85 | -3.02 | 4.87 |  | [0 3 5]
5th ptile | 95th ptile |  | 5th ptile | 95th ptile |  | 5th ptile | 95th ptile |  | MAX of 95% of Channel Models | MIN of 5% of Channel Models | abs(MAX) + abs(MIN) |  | CSD Vector
AWGN |  |  | DNLOS (stretched) |  |  | SCM Urban Macro |  |  |  |  |  |  | 
Ranking by abs(MAX) + abs(MIN) metric
  Top 8 CSD choices shown for 3Tx Streams

## Slide 24: 1MHz - 4Tx Stream CSD Rankings
Ranking by abs(MAX) + abs(MIN) metric
  Top 20 CSD choices shown for 4Tx Streams
-1.32 | 1.54 |  | -2.63 | 1.94 |  | -2.44 | 1.95 |  | 1.95 | -2.63 | 4.57 |  | [0 1 4 5]
-2.63 | 1.77 |  | -2.48 | 1.90 |  | -2.49 | 1.98 |  | 1.98 | -2.63 | 4.61 |  | [0 3 5 7]
-1.40 | 1.88 |  | -2.70 | 2.02 |  | -2.63 | 2.11 |  | 2.11 | -2.70 | 4.81 |  | [0 2 3 7]
-1.27 | 1.56 |  | -2.64 | 1.95 |  | -2.40 | 2.25 |  | 2.25 | -2.64 | 4.89 |  | [0 3 4 7]
-2.73 | 1.90 |  | -2.61 | 1.97 |  | -2.82 | 2.14 |  | 2.14 | -2.82 | 4.97 |  | [0 1 3 6]
-1.44 | 1.93 |  | -2.75 | 2.07 |  | -2.42 | 2.26 |  | 2.26 | -2.75 | 5.01 |  | [0 1 5 6]
-2.53 | 1.49 |  | -2.83 | 2.09 |  | -2.67 | 2.18 |  | 2.18 | -2.83 | 5.02 |  | [0 1 2 5]
-2.51 | 1.77 |  | -2.59 | 1.89 |  | -2.99 | 2.02 |  | 2.02 | -2.99 | 5.02 |  | [0 2 3 6]
-2.47 | 1.50 |  | -2.71 | 2.08 |  | -2.87 | 2.15 |  | 2.15 | -2.87 | 5.02 |  | [0 3 6 7]
-2.67 | 1.89 |  | -2.61 | 1.97 |  | -2.85 | 2.18 |  | 2.18 | -2.85 | 5.03 |  | [0 3 5 6]
-2.45 | 1.50 |  | -2.76 | 2.07 |  | -2.88 | 2.15 |  | 2.15 | -2.88 | 5.04 |  | [0 1 4 7]
-2.49 | 1.50 |  | -2.77 | 2.09 |  | -2.72 | 2.29 |  | 2.29 | -2.77 | 5.05 |  | [0 3 4 5]
-2.59 | 1.80 |  | -2.91 | 2.16 |  | -2.96 | 2.03 |  | 2.16 | -2.96 | 5.11 |  | [0 1 2 6]
-1.41 | 1.86 |  | -2.69 | 2.06 |  | -2.64 | 2.50 |  | 2.50 | -2.69 | 5.19 |  | [0 4 5 7]
-2.57 | 1.79 |  | -2.80 | 2.16 |  | -2.73 | 2.39 |  | 2.39 | -2.80 | 5.20 |  | [0 2 3 4]
-1.44 | 1.89 |  | -2.76 | 2.08 |  | -3.13 | 2.19 |  | 2.19 | -3.13 | 5.32 |  | [0 1 3 4]
-2.72 | 1.90 |  | -2.68 | 1.92 |  | -3.05 | 2.38 |  | 2.38 | -3.05 | 5.43 |  | [0 2 3 5]
-2.54 | 1.79 |  | -2.86 | 2.13 |  | -3.22 | 2.30 |  | 2.30 | -3.22 | 5.52 |  | [0 4 6 7]
-2.56 | 1.80 |  | -2.84 | 2.17 |  | -3.37 | 2.16 |  | 2.17 | -3.37 | 5.54 |  | [0 4 5 6]
-2.74 | 1.95 |  | -3.25 | 2.36 |  | -3.10 | 2.26 |  | 2.36 | -3.25 | 5.61 |  | [0 1 6 7]
5th ptile | 95th ptile |  | 5th ptile | 95th ptile |  | 5th ptile | 95th ptile |  | MAX of 95% of Channel Models | MIN of 5% of Channel Models | abs(MAX) + abs(MIN) |  | CSD Vector
AWGN |  |  | DNLOS (stretched) |  |  | SCM Urban Macro |  |  |  |  |  |  |