## Slide 1: Speed Frame Exchange
Date: 2012-07-16
Authors:
Eric Wong, Broadcom
Name | Affiliations | Address | Phone | Email
Eric Wong | Broadcom | Sunnyvale, CA | +1 408 922 6672 | ewong@broadcom.com
Matthew Fischer | Broadcom |  |  | mfischer@broadcom.com
Yongho Seok | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jin Sam Kwak | LG Electronics |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Thomas Pare | MediaTek |  |  | 
Kiran Uln | MediaTek |  |  | 
Huai-Rong Shao | Samsung |  |  | 
Chiu Ngo | Samsung |  |  | 
Minyoung Park | Intel |  |  | 
Tom Tetzlaff | Intel |  |  | 
Emily Qi | Intel |  |  | 

## Slide 2
Name | Affiliations | Address | Phone | Email
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Sudhir Srinivasa | Marvell |  |  | 
Simone Merlin | Qualcomm |  |  | 
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
George Calcev | Huawei |  |  | 
Osama Aboul Magd | Huawei |  |  | 
Young Hoon Kwon | Huawei |  |  | 
Betty Zhao | Huawei |  |  | 
David Yangxun | Huawei |  |  | 
Bin Zhen | Huawei |  |  | 
Minho Cheong | ETRI |  |  | 
Jae Seung Lee | ETRI |  |  | 
Hyoungjin Kwon | ETRI |  |  | 
Heejung Yu | ETRI |  |  | 
Jaewoo Park | ETRI |  |  | 
Sok-kyu Lee | ETRI |  |  | 
Sun, Bo | ZTE |  |  | 
Lv, Kaiying | ZTE |  |  | 
Authors:

## Slide 3
Authors:
Name | Affiliations | Address | Phone | Email
Sayantan Choudhury | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Ken Mori | Panasonic |  |  | 
Rojan Chitrakar | Panasonic |  |  | 
Shoukang Zheng | I2R |  |  | 
Haiguang Wang | I2R |  |  | 
Wai Leong Yeow | I2R |  |  | 
Zander Lei | I2R |  |  | 
Jaya Shankar | I2R |  |  | 
Anh Tuan Hoang | I2R |  |  | 
Joseph Teo Chee Ming | I2R |  |  | 

## Slide 4: Outline
Proposal in [1] permits a STA to send a PS-Poll at any time, and AP replies with either DATA or ACK (and More Data field set)
Primarily use for downlink data retrieval by STA
STA uses separate medium access for uplink data transmissions
Inefficient because
  More frame transactions are needed per DATA frame
  Separate uplink and downlink access and contention
Results in
  Longer STA wake times and higher power consumption
This suggests a combined uplink and downlink medium access
Propose an approach for speed frame exchange

## Slide 5: Uplink or Downlink Data Indication
Propose use of More Data field to indicate more UL Data
Currently in 802.11-REVmb/D12 [4], it indicates more DL Data
Buffered data at the AP for a STA in power save (in a DATA frame)
AP has a pending transmissions, if an APSD-STA advertises support for More Data ACK (in an ACK frame)
TDLS peer STA has pending transmissions
More broadcast or multicast frames buffered at the AP (within a group-addressed DATA frame)

## Slide 6: Station with no Uplink or Downlink Data
SIFS
ProbeDelay
AP
ACK
STA wakes from sleep, e.g. at a scheduled wake time
MoreData=0
RspFrm=10
STA returns to sleep since last MoreData from AP is 0
PS-POLL
STA
Wake
STA either misses Beacon, or chooses not to wake for Beacon. [1]

## Slide 7: Station with Downlink Data Only
ACK
STA wakes from sleep, e.g. at a scheduled wake time
STA returns to sleep since last MoreData from AP is 0
SIFS
ProbeDelay
AP
PS-POLL
STA
Wake
DATA
SIFS
AP readies DL DATA for transmission to STA that is scheduled to wake. [1]
MoreData=0
RspFrm=00
MoreData=0
RspFrm=10
MoreData=?
RspFrm=00

## Slide 8: Station with Downlink Data Only
ACK
SIFS
STA wakes from sleep, e.g. at a unscheduled wake time
STA returns to sleep since last MoreData from AP is 0
SIFS
ProbeDelay
AP
PS-POLL
STA
Wake
DATA
ACK
SIFS
MoreData=0
RspFrm=00
AP is unprepared for STA that is waking at an unscheduled time. AP sends DL ACK while it completes the retrieval of DL DATA from buffer space. [1]
MoreData=1
RspFrm=11
Note, new value of Response Frame bits
MoreData=0
RspFrm=10
Notes: Slide 6 - Even if AP knows STA is waking, it does not know whether it has DATA or not

## Slide 9: Data Frame Indication
DATA is another valid response frame type [3]
Use Reserved (b11) to indicate in SIG Field the presence of a DATA frame following this current transmission
Upon receipt, 3rd party STAs will defer by (MAX_PPDU + 2*SIFS + PHY-RXSTARTDelay)
Response Frame (2-Bit) |  | Frame Types
0 | 0 | ACK
0 | 1 | BA
1 | 0 | No Response
1 | 1 | Not ACK, CTS or BA

## Slide 10: Speed Frame Exchange
Propose to combine medium access for uplink and downlink DATA
If STA has buffered UL traffic, it starts frame exchange to the AP with UL DATA, instead of PS-POLL (supported by U-APSD)
Instead of AP returning an ACK to STA, it can send the buffered DL DATA straightaway
  E.g. RDG=1 in UL Data Trigger frame
Presence of next DATA frame indicates previous frame is successful
  I.e. implicit ACK, or combine BA with AMPDU
Collisions are possible with the first UL DATA, but can be significantly reduced if STA is scheduled to wake by the AP [2] [5]
Scheduling also allows AP to prepare DL DATA for a particular STA, reducing ACK-only DL response transmissions

## Slide 11: Station with Uplink Data Only
SIFS
ACK
DATA
STA wakes from sleep, e.g. at a scheduled wake time
STA returns to sleep since last MoreData from AP is 0
SIFS
ProbeDelay
AP
STA
Wake
ACK
SIFS
STA, with buffered UL traffic, starts transmission with UL DATA instead of PS-POLL.
MoreData=0
RspFrm=00
DATA
MoreData=1
RspFrm=00
MoreData=0
RspFrm=11
MoreData=0
RspFrm=10
MoreData is used to allow responder to correctly set Response Frame bits
Because of MoreData in UL, responder knows that DATA is next

## Slide 12: Station with Uplink and Downlink Data
Both AP and STA have equal number of UL and DL DATA frames to be exchanged. Since AP is aware of STA wake time, it prepares DL DATA for STA. Note again, STA starts with UL DATA instead of PS-POLL.
STA
Wake
SIFS
D
STA wakes from sleep, e.g. at a scheduled wake time
STA returns to sleep since last MoreData from AP is 0
SIFS
SIFS
ProbeDelay
AP
SIFS
D
D
MoreData=1
RspFrm=11
MoreData=0
RspFrm=00
MoreData=0
RspFrm=11
A
SIFS
MoreData=1
RspFrm=11
D
MoreData=1
RspFrm=11
D
D
MoreData=1
RspFrm=00
MoreData=0
RspFrm=10
E.g. BA inside of AMPDU with DATA

## Slide 13: Station with Uplink and Downlink Data
STA returns to sleep since last MoreData from AP is 0
MoreData=0
RspFrm=11
SIFS
A
STA wakes from sleep, e.g. at a scheduled wake time
AP and STA have unequal number of UL and DL DATA frames. For example, in a typical smart meter, there are more UL than DL DATA frames.
SIFS
SIFS
AP
STA
Wake
SIFS
MoreData=0
RspFrm=00
MoreData=1
RspFrm=11
D
D
MoreData=1
RspFrm=11
MoreData=0
RspFrm=10
SIFS
MoreData=0
RspFrm=11
D
MoreData=1
RspFrm=00
D
D
A
STA has prior knowledge of the existence of buffered DL DATA, e.g. saw TIM bit in Beacon
B

## Slide 14: Conclusion
Speed frame exchange combines uplink and downlink medium access
This approach reduces medium access and contention time
Fewer frame transactions between AP and STA are needed
STA remains awake for less time, and hence achieves power-saving

## Slide 15: Straw Poll 1
Do you support to include the concept of speed frame exchange, and use of More Data field in the TGah specification framework document?
  Yes
  No
  Abstain
Eric Wong, Broadcom

## Slide 16: Straw Poll 2
Do you support to modify the definition of value (b11) response frame type to indicate the presence of a frame that is not ACK, CTS or BA following current transmission in the TGah specification framework document?
  Yes
  No
  Abstain
Eric Wong, Broadcom

## Slide 17: References
[1] S. Merlin et al., “Low Power Medium Access,” 11-12/0127r1
[2] M. Fischer et al., “Target Wake Time,” 11-12/0823r0
[3] Y. Liu et al., “Early Ack Indication,” 11-12/0119r0
[4] IEEE 802.11 REVmb D12.0
[5] M. Park et al., “Uplink channel access,” 11-12/606r1