## Slide 1
Date: 2012-07-16
Authors:
Restricted Access Window Signaling for Uplink Channel Access
Name | Affiliations | Address | Phone | Email
Chittabrata Ghosh | Nokia | Berkeley, CA | +1 650 200 7566 | chittabrata.ghosh@nokia.com
Klaus Doppler | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA | 408-543-3370 | mfischer@broadcom.com
Eric Wong | Broadcom |  |  | 
Minyoung Park | Intel | Hillsboro, OR | +1 503 712 4705 | minyoung.park@intel.com
Tom Tetzlaff | Intel |  |  | 
Emily Qi | Intel |  |  | 
Yongho Seok | LG Electronics |  |  | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jin Sam Kwak | LG Electronics |  |  | 
ChaoChun Wang | MediaTek |  |  | chaochun.wang@mediatek.com
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Poonampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Thomas Pare | MediaTek |  |  | 
Kiran Uln | MediaTek |  |  | 

## Slide 2: Authors:
Name | Affiliations | Address | Phone | Email
Huai-Rong Shao | Samsung Electronics |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung Electronics |  |  | 
Yong Liu | Marvell |  |  | yongliu@marvel.com
Hongyuan Zhang | Marvell |  |  | 
Sudhir Srinivasa | Marvell |  |  | 
Simone Merlin | Qualcomm | 5775 Morehouse Dr., San Diego, CA | +1 858 845 1243 | smerlin@qualcomm.com
Alfred Asterjadhi | Qualcomm |  |  | 
Amin Jafarian | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
George Calcev | Huawei | Rolling Meadows,IL, USA |  | George.Calcev@huawei.com
Osama Aboul-Magd | Huawei |  |  | 
Young Hoon Kwon | Huawei |  |  | 
Betty Zhao | Huawei |  |  | 
David Yangxun | Huawei |  |  | 
Bin Zhen | Huawei |  |  | 
Minho Cheong | ETRI | 138 Gajiongno, Yuseong-gu, Dajeon, Korea | 82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | 
Hyoungjin Kwon | ETRI |  |  | 
Heejung Yu | ETRI |  |  | 
Jaewoo Park | ETRI |  |  | 
Sok-kyu Lee | ETRI |  |  | 
Sun, Bo | ZTE |  |  | 
Lv, Kaiying | ZTE |  |  | 

## Slide 3
Authors:
Name | Affiliations | Address | Phone | Email
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | 
Shoukang Zheng | I2R |  |  | skzheng@i2r.a-star.edu.sg
Haiguang Wang | I2R |  |  | 
Yeow Wai Leong | I2R |  |  | 
Zander Lei | I2R |  |  | 
Jaya Shankar | I2R |  |  | 
Anh Tuan Hoang | I2R |  |  | 
Joseph Teo Chee Ming | I2R |  |  | 

## Slide 4: Prior Medium Access Proposals
DTIM-1
TIM-1.1
TIM-1.2
TIM-1.3
RAW
RAW
RAW
RAW
Synchronized DCF (S-DCF) among STAs introducing the grouping concept, with group information included in the beacon frame [1]
DTIM Announcement includes restricted access window (RAW) information and STAs covered by the AID segment are allowed to access channel within RAW [2] depicted below
Uplink medium access by STAs within the AID segment in TIM controlled using contention based on TIM information [3]

## Slide 5: RAW Information Element in (Short) Beacon
Beacon Interval
Time
Stamp
Capability Information
SSID
Supported Rates
FH
Parameter
Set
DS
Parameter
Set
CF
Parameter
Set
RAW
Parameter Set
Proposed IE
Propose [1] to add an Information Element termed as Restricted Access Window Parameter Set (RAW) element in (short) Beacon frame for indication of restricted access window (RAW)
RAW parameter set (RPS) for group ‘n’ shall comprise of:
(i) RAW Group: AID range of STA allowed to access channel in RAW
(ii) RAW Start Time: Medium access start time for group ‘n’
(iii) RAW Duration: Duration of medium access
(iv) Options
(v) Slot Definition

## Slide 6: RPS Information Element
Element ID : Grouping element may be issued an Element ID of 222 (at present reserved)
Length: Number of octets in the Information Element (TBD)
RAW 1 to RAW N: Details about initiation, duration and configuration of medium access for N groups
Octets 1 1
Element ID Length RAW 1 RAW 2 RAW N
RAW Duration
RAW Group
RAW Start Time
Options
Slot Definition

## Slide 7: RAW Group
Feature | Value | Interpretation
Page ID | 2 bits | Indicates the page index for hierarchical AID (based on hierarchical AID) of the allocated group
Block Offset | 5 bits | Assuming 32 blocks per page, these bits indicate the starting block index of the allocated group
Block Range | 5 bits | Indicates the number of blocks (starting from the block offset) for the allocated group

## Slide 8: RAW Start Time and RAW Duration
RAW Start Time | 8 bits | Duration in TU from end of beacon transmission to RAW Start time
RAW Duration | TBD | Duration of RAW in TU

## Slide 9: Options Field and Slot definition
Access restricted to paged STA only | 2 bits | Bit 1: Set to 1 if only STA with their TIM bit set to 1 are allowed to perform UL transmissions Bit 2: Set to 1 if RAW is reserved for frames with duration smaller than slot duration, such as PS-Polls / trigger frames (ignored if Bit 1 is not set)
Group/Resource allocation frame indication | 1 bit | Set to 1 to indicate if STAs need to wake up at the beginning of the RAW to receive group addressed frames such as resource allocation (format of the resource allocation frame TBD)
Slot defintion | TBD bits | Include Slot duration signalling Slot assignment to STA Cross boundary transmissions allowed/not allowed Format is TBD
Notes: Resource allocation frame

## Slide 10: Summary
We proposed to add a RAW Parameter Set information element in (short) Beacon frame for restricted access window (RAW)
Definition of the RAW information element

## Slide 11: Straw Poll 1
Do you support to include, in TGah Spec Framework document, the concept of an optionally present RAW Parameter Set IE in the (short) beacon?

## Slide 12: Straw Poll 2
Do you support to include, in TGah Spec Framework document, the concept of the following sub-fields as specified in slides 7-9 in the RAW IE within the (short) beacon ?
- RAW Group with TBD bit allocations
- RAW Start Time
- RAW Duration
- Options Fields and
- Slot definition

## Slide 13: References
[1] Group Synchronized DCF, IEEE 802.11-12/0329r1
[2] Uplink Channel Access General Procedure, IEEE 802.11-12/0831r0 [3] Uplink Channel Access, IEEE 802.11-12/0606r1