## Slide 1: Sectorization for hidden node mitigation
Name | Affiliations | Address | Phone | email
George Calcev | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 x 310 | George.Calcev@huawei.com
Bin Chen | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 | Bin.Chen@huawei.com
Lin Cai | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 x 379 | Lin.Cai@huawei.com
Minyoung Park | Intel Corp. |  |  | minyoung.park@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel Corp. |  |  | emily.h.qi@intel.com
Thomas Kenney | Intel Corp. |  |  | 
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Sudhir Srinivasa | Marvell |  |  | 
Authors:

## Slide 2
Name | Affiliations | Address | Phone | email
Yongho Seok | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jinsam Kwak | LG Electronics |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Authors:

## Slide 3
Name | Affiliations | Address | Phone | email
Matthew Fischer | Broadcom |  |  | 
Eric Wong | Broadcom |  |  | 
Simone Merlin | Qualcomm |  |  | 
Zhi Quan | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI |  |  | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Heejung Yu | ETRI |  |  | heejung@etri.re.kr
Hyoung Jin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Authors:

## Slide 4: Authors:
Name | Affiliations | Address | Phone | email
Haiguang Wang | I2R |  |  | 
Shoukang Zheng | I2R |  |  | 
Yeow Wai Leong | I2R |  |  | 
Zander Lei | I2R |  |  | 
Jaya Shankar | I2R |  |  | 
Anh Tuan Hoang | I2R |  |  | 
Joseph Teo Chee Ming | I2R |  |  | 
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com

## Slide 5: Introduction
The 11ah amendment will support large number of STAs
Most of the sensor devices will have low power transmission,
Smart meters and smart phones will have higher power transmissions
Large radius (up to 1km) and transmission power variability potentially will increase the number of hidden nodes
Hidden node problem in 11ah was pointed out previously [1]

## Slide 6: Logical and Physical layer grouping
In this submission we propose to use grouping as a means of reducing hidden nodes collisions
Idea: In a determined time interval allow transmissions only from those stations that belong to a specific group
This approach reduces number of contentions in a time interval and therefore reducing probability of collisions
A group is a subset of the entire set of STAs
A group could be defined via:
  A logical condition satisfied by a subset of STA’s or traffic type, for instance a sequence of AID numbers, or filter of MAC address etc.
  A physical condition satisfied by a subset of STAs in BSS , for instance stations that receives a beamformed beacon from AP
  A combination of logical and PHY condition , for instance the subset of stations in a sector which have even AIDs

## Slide 7: Physical grouping as a solution of hidden node issue
An example of physical grouping is
provided by sectorization.
In such approach only the stations
in one sector are active at the time.
A STA knows that belongs to a sector
when it receives a beamformed
management frame (such as a beamformed beacon)

## Slide 8: Sectorization for hidden node reduction
AP divides the space in multiple sectors and use a TDM approach to allow STA transmissions in one sector at the time
Stations are allowed to transmit and receive data only in the time interval corresponding with their sector (called as Sector Interval in the drawing)
Some time interval can be left for channel access of all sectors at the same time
Example of channel access:
Beacon
Sector 1
Access STAs in Sector 1
Beacon
Sector 2
Access STAs in sector 2
Beacon
Sector 3
Access STAs in sector 3
Omni
Beacon
Access all STAs in the BSS
Sector Interval 1
Sector Interval 2
Sector Interval 3
BSS Interval

## Slide 9: Sectorization for hidden node reduction
Sectorization solution has minimal impact to the actual 11ah design:
  Selected stations transmit just in an allocated time slot
  The overhead is practically zero (we can reuse the short beacon concept), the STA selects sector based on received sector beacon
  TIM signaling could be repeated in each sector beacon or it just contains the map for the selected stations in a sector
  Can accommodate the short beacon and the long beacon concepts
Requirement:
  The AP is required to implement a time slotted sectorization access (e.g. via the antenna pattern shaping or directional antennas) that illuminates one sector at the time

## Slide 10: SP 1
Do you agree to include in the SFD “The 11ah should support a mode of operation where only a selected group of stations is allowed to transmit during a specified time interval. When a STA finds that belongs to a transmission group it shall transmit only in the time interval reserved for that group and not transmit in the time interval allocated to another group.”?

## Slide 11: SP 2
Do you agree to add in SFD “The transmission group may be identified by a group ID and a group definition field that identifies a logical grouping (such as an AID range of addresses) or a physical grouping, for example using an antenna beam pattern.” ?

## Slide 12: SP 3
Do you agree to include in the SFD “The transmission group definition field, the time interval reserved for the group transmission and its repetition period or the time till the next transmission may be advertized via (short)beacons, probe response or another management frame TBD.”

## Slide 13: References
[1] 11-12-0606-01-Uplink Channel Access, Minyoung Park, Intel, 16-May-2012