## Slide 1: Short MAC Header
Date: 2012-07-16
Authors:

## Slide 4: Introduction
The MAC header is a significant overhead for short MPDUs [1, 2]
  30-36 octets in 11n, without security
  This is inefficient for short-packet applications
    E.g., the FR-EM document includes traffic specifications for sensors (256Bytes), and industrial process automation (64Bytes) [3]. Several other applications with very short transmit packets can be envisioned
Shortening the MAC header has advantages for 11ah
    Prolonged battery lifetime
    Reduced medium occupancy
Motions that define the structure of the Short MAC header have passed [5]
  See next slide for details on the structure
This presentation follows up on the details for
  Sequence Control field
  Frame Control field

## Slide 5: Short MAC Header Format – current status
Order of Address fields
  From AP to STA: 2 byte AID of receiver followed by BSSID (From-DS = 1)
  From STA to AP: 6 byte BSSID followed by 2 byte AID of STA (From-DS=0)
  From STA to STA: 6 byte destination STA MAC address followed by 2 byte source STA AID (From-DS=0)
A3 is optionally present
From-DS = 1
From-DS = 0
(also STA 2 STA)
2B | 2B | 6B | TBD (1 or 2B) | 6B
FC | A1 (AID) | A2 (BSSID) | Sequence Ctrl. | A3 (Optionally present)
2B | 6B | 2B | TBD (1 or 2B) | 6B
FC | A1 (BSSID/RA ) | A2 (AID ) | Sequence Ctrl. | A3 (Optionally present)

## Slide 6: Sequence Control Field
Sequence Number: Needed to detect duplicate packets, Block Ack and fragmentation
Fragment number: needed to support long packets
  11ah must natively support transmission of long packets
  Absence of support for fragmentation was perceived as a weakness in competing technologies
Proposal: Use the same Sequence Control field as normal MAC header
  Supports fragmentation
  STA can seamlessly switch between short and normal MAC header if additional features are required
    No change to receive state machine
b0 b3 | b4 b15
Fragmentation Number | Sequence Number

## Slide 7: Frame Control design
The following fields are considered essential and need be supported
Protocol version
Type field
  Possible to indicate 16 different types of frames
  Short MAC header may be used for a variety of frames (specifics are TBD)
From DS
  Indicate Address fields ordering (see slide #3)
Existing fields in FC of normal MAC header
  More fragments, Power Management, More Data, Protected Frame
Fields taken by the QoS Control fields
  EOSP (End of Service Period)
A3 Present
  Indicates a short MAC Header format with Address 3 present
Other fields may be useful (need discussion)
  Retry, A-MSDU

## Slide 8: Conclusions
Following up on the design of short MAC header [5], we propose
  Include a 2B Sequence Control field, with same structure as existing SC field
    Allows fragmentation
    Allows seamless operation between short and long header
  Define the Frame Control field structure including some essential fields

## Slide 9: References
[1] 11-12-0365-01-00ah-mac-header-compression
[2] 11-12-0110-06-00ah-frame-header-compression
[3] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology
[4] 11-12-0324-00-00ah-short-ack
[5] 11-12-0365-02-00ah-mac-header-compression

## Slide 10: Straw Poll 1
Do you support to include in the spec framework, in section 4.5, the following subfields in the Frame Control field of the short MAC Header for data frames
  Protocol version (2b), Type field (4b), From DS (1b), A3 Present (1b), More Fragments (1b), Power Management (1b), More Data(1b), Protected Frame (1b), EOSP (1b)
bits 2 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3
Protocol Version | Type | From DS | More Fragments | Power Management | More Data | Protected Frame | EOSP | A3 Present | TBD

## Slide 11: Straw Poll 2
Do you support to include in the spec framework, in section 4.5, a Sequence Control Field of 2 bytes for the short MAC Header?
b0 b3 | b4 b15
Fragmentation Number | Sequence Number