## Slide 1: Collision reduction after TIM
Date: 2012-07-16
Authors:

## Slide 4: Introduction
802.11ah to support up to 6000 STA
  Potentially high collisions
  Potentially hidden nodes
In [1] various options for ‘spreading’ the UL transmissions in time to avoid collisions were presented
  The general concept was accepted in SFD [2]
    R.4.2.B: The draft specification shall support the concept of utilizing information from an AP to spread out uplink transmissions over a period of time to mitigate the hidden node problem [May 2012 meeting minutes, 12/606r1]
In [2] general methods for UL and DL data delivery are discussed
We describe in more detail a specific mechanism for reducing the collisions that may be generated after the TIM
  ‘Spread’ the contention process of paged STAs
  Define a mechanism that does not require extra signaling in every beacon

## Slide 5: PS mode and collisions
STAs in PS mode currently operate as follows
  STA wakes up for a beacon and reads a TIM
  If STA is not ‘paged’ by the TIM the STA goes back to Doze mode
  If STA is ‘paged’ by the TIM the STA contends to send a PS-Poll
  AP replies with either ACK or immediate Data
Contention for sending the PS-Poll/trigger frame may cause collisions, especially if a large number of STAs were paged or STAs are hidden
A way to reduce the collision probability is to stagger the transmissions in time
  Quantitative benefits of this concept can be found in [1]
We propose to use implicit info from the TIM to indicate to each paged STA when to start the contention to send the PS-Poll or trigger frame

## Slide 6: Proposed method
STAs that read the TIM and for which the AP has BUs shall behave as follows to send a PS-Poll or trigger frame
  STA i shall not start to contend before a given time Ti
  Ti is computed based on the STA’s position in the TIM IE and additional information which is received a priori from the AP
Example 1
  Ti = STA_Position * X
    X = 10ms, indicated by AP, e.g., at association
Example 2
  Ti = HASH(STA_Position, TSF) * X
    X = 10ms, indicated by AP, e.g., at association
Ti can be computed also in other ways which may account for other implicit information to further increase efficiency

## Slide 7: Required Signaling
The AP may communicate this additional information (e.g., value of X) in different ways
  Include it in the association response or in a management frame
    If an update is required the AP may include it in a beacon
Notes
  Beacon reception is a major source of power consumption
  A Short Bacon format was accepted in [3]
  We should avoid any increase of (short) beacon size

## Slide 8: Conclusions
We propose a mechanism for spreading the access times of the paged STAs by using implicit information in the TIM
  Does not require additional information in the beacon
  Helps reducing collisions of PS-Polls or trigger frames
    Increased power saving for sensor STAs

## Slide 9: References
[1] 11-12-0606-01-00ah-uplink-channel-access
[2] TGah specification framework, DCN 1137r9
[3] Short Beacon, DCN 129 r3

## Slide 10: Straw Poll 1
Do you support to add in the specification framework an operation mode for spreading the PS-Poll/trigger frame transmission, that does not require additional beacon info, by defining the following:
  Paged STA starts the contention at slot boundary defined as a function of STA position in the TIM IE and additional info determined by Association or Beacon frame.